## Slide 1
Lesson 2
Chapter 11
Magnetism & Electromagnets
Sections
11.2 Magnetic effect of an electric current
11.3 The electromagnet
11.4 Magnetic circuit

## Slide 2: 11.2 Magnetic effect of an electric current
An electric current causes a magnetic field to be created around the conductor
Notes: Figure 11.13

## Slide 3: Direction of the field
The direction of the magnetic field depends on the direction of the current
Notes: Figure 11.14

## Slide 4: Right-hand rule for a conductor
Right-hand thumb (or grip) rule to find the direction of the magnetic field around a conductor
Notes: Figure 11.15

## Slide 5: Magnetic field around two conductors
When the current is in the same direction, adjacent conductors are attracted to each other
Notes: Figure 11.16

## Slide 6: Currents in opposite directions
Currents in the opposite direction make adjacent conductors repel each other
Notes: Figure 11.17

## Slide 7: Force between two conductors
where:
F = force in newtons (N) per metre length
I1 = current in one conductor
I2 = current in the other conductor
d = distance in metres between the conductors.

## Slide 8
Example 11.2
Two copper bus bars spaced 25 millimeters apart experience a fault current of 15 000 A that flows in eac bus bar. What is the force acting between them over a 1 meter length?
Values:

## Slide 9: 11.3 The electromagnet
The magnetic field around a coil of wire is the same as a
permanent magnet
Notes: Figure 11.19

## Slide 10: Right-hand rule for a coil
Use the right-hand rule to find the north pole of an electromagnet
Notes: Figure 11.20

## Slide 11: Magnetomotive force
The strength of the magnetic field produced by an air-cored electromagnet depends on the coil current and number of turns.
The product of these two values is called magnetomotive force (Fm).
That is: Fm = I × N
where:
Fm = magnetomotive force in ampere-turns (At)
I = current in amperes
N = number of turns.

## Slide 12
Example 11.3
What is the magnetomotive force developed by an air-cored coil of 250 turns passing a current of 30 amps?
Values:

## Slide 13: Magnetomotive force examples
Magnetic flux produced by an electromagnet is proportional to the current and the number of turns
Notes: Figure 11.21

## Slide 14: Magnetising force
Magnetising force depends on the ampere turns of the coil and the length of the magnetic circuit
Notes: Figure 11.22

## Slide 15: Magnetising force equation
Magnetising force (H) is magnetomotive force divided by length.
That is:
where:
H = magnetising force in ampere-turns per metre (At/m)
Fm = NI = magnetomotive force in ampere-turns (At)
l = length of magnetic path in metres (m).
or

## Slide 16: Magnetising force examples
Magnetising force is the same in all parts of an iron core and is inversely proportional to the length of the core
Notes: Figure 11.23

## Slide 17
Example 11.4
A coil of 1000 turns wound on a 75 mm long iron core has a current of 0.2 amperes passing through the coil. What is the magnetising force (H) in the core?
Values:

## Slide 18: Summing up
Magnetomotive force is the force that establishes and maintains a magnetic flux in a magnetic circuit. Symbol is Fm, measured in ampere-turns (At).
Magnetising force is magnetomotive force per unit length. For air-cored solenoid, the length is that of the coil, for iron-cored solenoid it’s the average length of the iron core. Symbol is H, unit is ampere-turns per metre (At/m).
Magnetic flux is the total number of lines an electromagnet or a permanent magnet produces.

## Slide 19: Summing up (2)
Flux density is the number of lines per square metre. Symbol is B, unit is the tesla (T).
The right-hand thumb rule can be used to find the north pole of an electromagnet.
Adjacent current-carrying conductors will have a force acting to repel them (currents in different directions) or attract them (current in the same direction).

## Slide 20: 11.4 Magnetic circuit
The magnetic circuit:
is like an electric circuit, where voltage causes current to flow, which is opposed by the resistance of the circuit
has magnetomotive force (Fm) equivalent to voltage, and magnetic flux (Φ) equivalent to current
is the path taken by the flux, so its ability to conduct the flux is important. This is related to the material’s permeability.

## Slide 21: Relative permeability (µr)
Relative permeability compares the permeability of a material to the permeability of air (or vacuum).
Symbol is µr (does not have a measurement unit)
where:
B = flux density in teslas (or webers/m2).

## Slide 22: Permeability of air (µ0)
In air (or a vacuum), the ratio of flux density (B) and magnetising force (H) producing the flux gives a value called the permeability of air (free space).
This value is constant regardless of the magnetising force, and is called µ0.
µ0 = 4p x 10–7 henry/metre (H/m)(exactly)
or for practical purposes,
µ0 = 1.26 × 10–6 henry/metre (H/m).

## Slide 23: Absolute permeability (µ)
The absolute permeability (µ) of a material is calculated by multiplying its relative permeability by the permeability of air.
That is:
 = r  0
Note: Absolute permeability (µ) is sometimes referred to as permeability.

## Slide 24: Permeability in terms of B and H
Absolute permeability of a material can also be calculated with:
where:
B is the flux density (tesla)
H is the magnetising force (At/m).
This equation can be transposed in terms of either B or H, giving:
and

## Slide 25: Permeability comparison
Relative permeability (µr) changes with flux density (B). The values shown give an approximate range. Minimum values of permeability (µ) are given.
Notes: Table 11.1 from page 237

## Slide 26
 | H/m
Example 11.5
What is the absolute permeability of an iron core if its relative permeability is 5000 at a certain flux density?
Values:

## Slide 27
Example 11.6
Calculate the magnetising force (H) and the flux density (B) in the core of the electromagnet shown in Figure 11.24.
Values:
Figure 11.24

## Slide 28: Reluctance
A magnetic path has resistance to magnetic flux, referred to as its reluctance.
The symbol for reluctance is Rm or S
Measurement unit is the ampere-turn per weber (At/Wb).

## Slide 29: Rm in terms of Ohm’s law
In an electric circuit, Ohm’s law relates V, I and R.
In a magnetic circuit, there’s a similar relationship between magnetomotive force Fm, magnetic flux F and reluctance Rm:
where:
F is flux in webers (Wb)
Fm is magnetomotive force in ampere-turns (At)
Rm is reluctance in ampere-turns per weber (At/Wb).

## Slide 30: Factors affecting Rm
The reluctance of a magnetic circuit depends on:
length the longer the magnetic circuit, the higher the reluctance
cross-sectional area the smaller the csa, the higher the reluctance
permeability the lower the permeability, the higher the reluctance.

## Slide 31: Rm in terms of µ and area
Reluctance of a magnetic circuit can be calculated with:
where:
Rm is reluctance in ampere-turns per weber (At/Wb)
µ0 is permeability of air = 1.26 × 10–6 henry/metre
µr is relative permeability (if known)
µ is absolute permeability (if known)
A is the cross-sectional area in square metres (m2).
or

## Slide 32: Effect of air gap on reluctance
A relay has an air-gap in the magnetic path when the armature is open, which increases the reluctance of the magnetic circuit
Notes: Figure 11.25

## Slide 33
Example 11.7
The core of the electromagnet in Figure 11.26 has an average length () of 350 mm and a cross sectional area (csa) of 400 . The coil has 20 turns. When a current of 2 A is passed through the coil a total flux of 100 μWb is established in the core.
What is the reluctance () of the core?
What is the flux density (B) in the core?
Determine the magnetising force (H).
Calculate the relative permeability () of the core.
Values:
Figure 11.26

## Slide 34
Example 11.7 (1)
What is the reluctance () of the core?
What is the flux density (B) in the core?
Determine the magnetising force (H).
Figure 11.26
Values:

## Slide 35
Example 11.7 (2)
Calculate the relative permeability () of the core.
Figure 11.26
Values:

## Slide 36: Summing up
Absolute permeability or permeability (µ) is the ability of a material to conduct magnetic flux; unit is henrys per metre
Permeability of a vacuum (µ0) is a constant and equals approximately 1.26 × 10–6 henrys per metre (H/m).
Relative permeability (symbol µr) is a measure of the increase in flux density a magnetic material causes compared to air, for the same magnetising force. For ferromagnetic materials, µr is always greater than one.

## Slide 37: Summing up (2)
Permeability (µ) of a material is the product of its relative permeability (µr) and µ0.
It also equals flux density (B) divided by the magnetising force (H). That is:
Reluctance (symbol Rm) is the resistance a magnetic path offers to magnetic lines of force (F) and is measured in ampere turns per weber (At/W).