## Slide 1
Lesson 4
Chapter 12
Electromagnetic Induction
Sections
12.1 Introduction
12.2 Electromagnetic induction
12.3 Lenz’s law
12.4 Inductance

## Slide 3
Chapter 12
Electromagnetic Induction

## Slide 4: About this chapter
An electric current produces a magnetic field, and as explained in this chapter, a moving magnetic field can cause an electric current. This is called electromagnetic induction and is how most electrical power is generated.
This chapter:
introduces the inductor
explains the property called inductance and some of its effects.

## Slide 5: Contents
12.1 Introduction
12.2 Electromagnetic induction
12.3 Lenz’s law
12.4 Inductance
12.5 Mutual inductance
12.6 The LR circuit

## Slide 6
Lesson 4
Chapter 12
Electromagnetic Induction
Sections
12.1 Introduction
12.2 Electromagnetic induction
12.3 Lenz’s law
12.4 Inductance

## Slide 7: 12.1 Introduction
In 1820, Oersted discovered the link between electricity and magnetism. In 1831, Michael Faraday found that a moving magnetic field causes a current to flow in a conductor.
This effect, called electromagnetic induction, was studied by many notable people of the time.
The first DC generator was produced in 1832, and today most electrical power is produced by electromagnetic induction.

## Slide 8: 12.2 Electromagnetic induction
A conductor moving in a magnetic field causes a voltage to be induced in the conductor
Notes: Figure 12.1

## Slide 9: Reversing direction of motion
The polarity of the induced voltage changes with the direction of movement
Notes: Figure 12.2

## Slide 10: Fleming’s right-hand rule
Fleming’s right-hand rule gives a way of determining the direction of the induced current when a conductor is moving in a magnetic field
Notes: Figure 12.3

## Slide 11: Voltage induced in a conductor
The value of the voltage induced in a conductor is proportional to the:
1. length of the conductor in the magnetic field
2. speed of relative movement between the conductor and the magnetic field
3. strength of the magnetic field.
It is also affected by the angle at which the conductor passes through the magnetic field. This is assumed to be a right angle (90º).

## Slide 12: Calculating induced voltage (e)
e = Blv
where:
e = induced EMF in volts
B = flux density of the magnetic field (teslas)
l = length of the conductor moving at right angles to the field (metres)
v = velocity of the conductor (metres per second).

## Slide 13: Example 12.1
v = 10 m/s, B = 0.001 T, l = 0.01 m
e = Blv
e = 0.0010.0110 = 0.0001 V
e = 100 µV
Notes: Figure 12.4

## Slide 14: Inducing a voltage in a coil
Winding the conductor into a coil increases its length, and therefore increases the induced voltage
Notes: Figure 12.5, drawing (a) only

## Slide 15: No motion, no induced voltage
A voltage is induced in a coil only when the magnet is moving
Notes: Figure 12.5, drawing (b) only

## Slide 16
Reversing direction of motion
The polarity of the induced voltage reverses when the direction of motion is reversed
Notes: Figure 12.5, drawing (c) only

## Slide 17
Voltage induced in a coil
Faraday’s law is another way to calculate induced voltage:
e = N × rate of change of flux
or
where:
e = induced EMF in volts
N = number of turns on the coil
rate of change of flux = flux in webers cut per second.

## Slide 18: Example 12.2
N = 1000 turns, rate of change of flux = 0.0015 Wb/s
e = N × rate of change of flux
e = 1000 × 0.0015
e = 1.5 V
Notes: Figure 12.6

## Slide 19: 12.3 Lenz’s law
Lenz’s law says:
the current induced in a conductor will set up a magnetic field that opposes the magnetic field causing the current.

## Slide 20: Opposition to conductor motion
(a) Fleming’s right-hand rule gives the direction of the induced current.
(b) It shows the current is flowing towards you, causing an anticlockwise field around the conductor. The fields repel because their lines of force are in the same direction.
Notes: Figure 12.7

## Slide 21: Lenz’s law acting in a coil
Lenz’s law – the coil’s magnetic field opposes the
movement of the magnet
Notes: Figure 12.8

## Slide 22: 12.4 Inductance
Inductance:
is the property of a circuit, component or conductor that opposes a change in the value of an electric current
is increased when a conductor is wound into a coil.

## Slide 23: Back-EMF of a coil
A coil produces a back-EMF while the magnetic field builds up, because the expanding field is moving
Notes: Figure 12.10 (a) only

## Slide 24: No motion, no back-EMF
When the field has built up, there is no relative motion and therefore no induced voltage
Notes: Figure 12.10 (b) only

## Slide 25: The inductor
An inductor is a component that has a coil of wire wound around a core. It therefore has inductance.
The unit of inductance is the henry, where one henry causes an induced voltage of one volt when the current is changing at a rate of one ampere per second.
Inductor symbols:
Notes: Figure 12.11

## Slide 26: Factors that determine inductance
The inductance of a coil is determined by:
1. number of turns
2. length of the coil
3. cross-sectional area of the coil
4. permeability of the core.

## Slide 27: Number of turns
Inductance is proportional the square of the number of turns. That is, double the turns gives four times the inductance.
Notes: Figure 12.12

## Slide 28: Length of the coil
Inductance is inversely proportional to the length of a coil
Notes: Figure 12.13

## Slide 29: Area of the coil
Inductance is directly proportional to the cross-sectional area of a coil
Notes: Figure 12.14

## Slide 30: Permeability of the core
Inductance is directly proportional to the permeability of the core
Notes: Figure 12.15

## Slide 31: Equation for inductance
where:
L = inductance in henrys
N = number of turns
A = cross-sectional area in square metres (m2)
 = permeability of the core
l = length of the coil in metres (m).

## Slide 32: Inductor cores
Three main types of core materials used with inductors are:
1. air (or other non-magnetic materials)
2. soft iron
3. ferrite.

## Slide 33: Typical low power inductors
Low power inductors are mainly used in electronics. They have a range of core materials, typically ferrite, silicon steel or air.
Notes: Figure 12.17

## Slide 34: High power inductors
Power inductors can handle high currents and are found in substations.
The iron-cored ‘ballast’ is from a fluorescent light fitting.
Notes: Figure 12.18

## Slide 35: Summing up
Lenz’s law states that the current induced in a conductor will set up a magnetic field that opposes the magnetic field causing the current. This opposition is called inductance.
Inductance is measured in henrys (H). A coil has an inductance of 1 H if a voltage of 1 V is induced in the coil when the current in the coil is changing by 1 A per second.

## Slide 36: Summing up (2)
The inductance (L) of a coil is proportional to the square of the turns (N2), the cross-sectional area (A), the permeability of the core (µ), and is inversely proportional to the length (l) of the core:

## Slide 37: Summing up (3)
Inductors can have a ferromagnetic or an air core. Inductors used with an alternating current have a laminated core.
High power inductors are used in electrical power substations, low power inductors are used in electronics and telecommunications.

## Slide 38: 12.5 Mutual inductance
Mutual inductance occurs between two nearby coils.
When current starts flowing in one coil, it builds up a magnetic field.
The moving field induces a voltage in the other coil.
Notes: Figure 12.19

## Slide 39: Application
A transformer has coils on a common core and works by mutual inductance
Notes: Figure 12.20

## Slide 40: 12.6 The LR circuit
A circuit that has inductance and resistance is called an LR circuit.
All inductors have resistance, so an inductor itself is an LR circuit, as its resistance and inductance are in series.
The resistance of a coil limits the maximum value of the DC current that can flow.
Its inductance opposes changes in the current.

## Slide 41: Basic LR circuit
An LR circuit has inductance and resistance in series, where the resistance is often that of the inductor alone
Notes: Figure 12.21

## Slide 42: Effect of inductance
Inductance opposes a change in current, so the current in an LR circuit increases exponentially, as in an RC circuit
Notes: Figure 12.22

## Slide 43: Effect at switch-off
The back-EMF of the coil causes current to continue after supply is disconnected, making it decay to zero exponentially, as in an RC circuit
Notes: Figure 12.23

## Slide 44: LR time constant
A time constant is the time taken for a current or voltage to reach 63.2 per cent of its final value. The time constant of an LR circuit is found with:
where:
τ = time constant in seconds
L = inductance in henrys
R = resistance in ohms.

## Slide 45: Example
L = 5H
R = 100 ohm
t = 0.05 seconds
Notes: Figure 12.24

## Slide 46: Chapter summary
The voltage (e) induced in a conductor by a moving magnetic field equals the product of the flux density (B), length of the conductor (l) and the velocity of the relative movement (v), or e = Blv.
The voltage (e) induced in a coil equals the number of turns (N) multiplied by the rate of change of the magnetic flux.
That is:

## Slide 47: Chapter summary (2)
Inductance is opposition to a change in current. An inductance of one henry causes an induced voltage of 1 V when the current is changing at a rate of 1 A per second.
The inductance (L) of a coil can be found with the equation:

## Slide 48: Chapter summary (3)
The interaction between the magnetic field of one coil and an adjacent coil is called mutual inductance
The time constant (t) of an LR circuit is the inductance divided by the resistance or L/R seconds.