## Slide 1
Lesson 1
Chapter 11
Magnetism & Electromagnets
Section
11.1 Magnetism

## Slide 2
UEENEEG101A
Solve problems in electromagnetic devices and related circuits
Magnetism & Electromagnetism
DC Machines (Motors & Generators)
Notes: Title

## Slide 3
04/02/19
11/02/19
18/02/19
25/02/19
04/03/19
11/03/19
18/03/19
25/03/19
01/04/19
08/04/19
29/04/19
06/05/19
13/05/19
Term Break

## Slide 4
Magnets & Electromagnetism
11/03/19
13/05/19
To Achieve Competence (AC) in the UEENEEG101A unit a pass mark of 50% is required in both Magnetism & DC Machines, i.e. the student MUST PASS both sections.
DC Machines

## Slide 5
DC Theory
Formulae Sheets

## Slide 6
Electromagnetism & DC Machines
Formulae Sheets

## Slide 7
AC Theory
Formulae Sheets

## Slide 8
Transformers & Rotary Machines
Formulae Sheets

## Slide 10
Chapter 11
Magnetism and electromagnets

## Slide 11: About this chapter
Magnetism and electricity are closely related. Most of the electricity we generate relies on this relationship, as do electric motors and many other electrical components.
This chapter:
reviews magnetism, the magnetic field and some of the terms that describe magnetism
looks at the way different types of materials respond to a magnetic field and how they are classified
explains electromagnets and a number of terms and equations related to magnetism.

## Slide 12: Contents
11.1 Magnetism
11.2 Magnetic effect of an electric current
11.3 The electromagnet
11.4 Magnetic circuit
11.5 Magnetisation curves

## Slide 13
Lesson 1
Chapter 11
Magnetism & Electromagnets
Section
11.1 Magnetism

## Slide 14: 11.1 Magnetism
Magnetism is a force created by a magnetic field.
The Earth has a magnetic field that produces the magnetosphere, which protects the Earth from the sun’s solar wind.
A magnet has two poles (north and south pole), so named because a magnet, if allowed to move freely, aligns itself so its north pole points to the Earth’s magnetic North Pole.

## Slide 15: Basic compass
The north-seeking pole of a magnet points to the Earth’s magnetic North Pole
Notes: Figure 11.2

## Slide 16: Magnetic Field
A magnetic field is made up of lines of force that travel from the north to the south pole of a magnet
Notes: Figure 11.3

## Slide 17
RN Video Magnetism (Part 3)
Magnetic Fields

## Slide 18: Properties of a magnetic field
Properties of a magnetic field include:
they seek the path of least magnetic resistance
they attempt to form closed loops
they never cross one another
they all have the same magnetic strength
they become less dense (spread out) in air or other non-magnetic materials, and become more dense when flowing in a magnetic material, such as iron.
parallel lines of force travelling in the same direction repel each other

## Slide 19: Properties of a magnetic field (2)
Properties of a magnetic field include:
their density decreases with increasing distance from the poles
they are considered to have direction as if flowing, though no actual movement occurs
externally they flow from a magnet’s north pole to a south pole
internally they flow from the south pole to the north pole.

## Slide 20: Lines of force
Lines of force take the path of least magnetic resistance
Notes: Figure 11.5

## Slide 21: Magnetic induction
When a magnetic material is in a magnetic field, it becomes temporarily magnetised.
This is called magnetic induction, because magnetism is induced in the material by the magnetic field of the magnet.
The polarity of the induced magnet is the same as if the material itself was a magnet, with lines of force also travelling (externally) from its north to its south pole.

## Slide 22: Inducing magnetism
Soft iron can be magnetised by induction by stroking the iron with one or two strong magnets
Notes: Figure 11.6

## Slide 23: Magnetic Materials
Materials are either non-magnetic or magnetic.
Non-magnetic materials have no reaction to or effect on a magnetic field.
All magnetic materials react in some way to a magnetic field and are classified according the type of reaction.
There are three classifications of magnetic materials:
ferromagnetic
paramagnetic
diamagnetic.

## Slide 24
Ferromagnetic Materials
Ferromagnetic materials are Ferrous (Fe) metals including iron, steel, nickel, cobalt and a number of alloys
Ferromagnetic materials:
are attracted by a magnetic field,
can be magnetised
affect the shape of a magnetic field
have a high permeability, i.e. have low resistance to lines of force, and
are good conductors of a magnetic field
The symbol for permeability is µ (mu)

## Slide 25
Rare Earth Magnets
Rare earth magnetic alloys can support a stronger magnetic field than conventional alloys.
Called Rare Earths because they were difficult to find.
Rare Earth Magnets include:
samarium-cobalt (Sm-Co), an alloy combining samarium, cobalt and iron
neodymium (Nd-Fe-B), an alloy made of neodymium, iron and boron.

## Slide 26: Ferrite Magnets
A Ferrite is a combination of ferrous oxides in a ceramic base
Ferrite magnets:
have similar properties to ferromagnetic materials
do not conduct an electric current (insulator)
are classed as ferrimagnetic materials

## Slide 27: Magnets
Examples of ferrite, alnico (alloy of aluminium, nickel and cobalt) and rare earth magnets
Notes: Figure 11.7

## Slide 28: Paramagnetic Materials
Paramagnetic materials are weakly attracted to a magnet
Paramagnetic materials:
become weakly magnetised in the same direction as the magnetising force
have a permeability slightly higher than one
have far less strength than a ferromagnetic magnet
lose magnetism when the magnetising force is removed
include aluminium, platinum, manganese, chromium and oxygen

## Slide 29: Diamagnetic Materials
Diamagnetic materials become weakly magnetised in the opposite direction to the magnetising force
Diamagnetic materials:
have a permeability less than one
include:
  Bismuth and carbon graphite, the strongest diamagnetic materials
  mercury, copper, gold, silver, water, diamonds, wood and living tissue which are less strong.

## Slide 30: Non-magnetic Materials
Non-magnetic materials:
have a permeability of one
have no effect on a magnetic field
are not affected by a magnetic field, i.e. don’t become magnetised
for most purposes paramagnetic and diamagnetic materials are considered to be non-magnetic
include air, wood, plastic, water, paper and cloth fabrics

## Slide 31: Preserving a magnet
A magnet of any type will lose some or all of its magnetism if it is exposed to a high temperature.
The loss of magnetism is complete at the Curie temperature (for iron ≈ 770 ºC, for neodymium ≈ 300 ºC).
Hammering or jarring a magnet will also affect its magnetic strength.
A magnet can lose its magnetic strength if it is exposed to another magnetic field.

## Slide 32: Magnetic keeper
Magnets should be stored with an iron keeper to preserve their magnetic strength
Notes: Figure 11.9

## Slide 33: Law of attraction and repulsion
Unlike poles attract, like poles repel
Notes: Figure 11.8

## Slide 34: Magnetic shielding
A magnetic shield keeps magnetic flux away from an area by providing a high permeability path around the area
Notes: Figure 11.10

## Slide 35: Magnetic Flux
Magnetic flux:
is the total number of lines of magnetic force produced by a magnet
is measured in webers (abbreviated to Wb)
one weber equals 100 million (108) lines of force
The symbol for Magnetic Flux is Φ (phi).

## Slide 36: Magnetic flux (2)
A typical horseshoe magnet produces a flux of 0.0001 Wb, or 10 000 lines of force.
Expressed with a metrix prefix: 0.0001 Wb = 0.1 mWb (milliweber)
for calculations written as 0.1 mWb = 0.1 × 10-3 weber.

## Slide 37: Flux density
Flux density is flux divided by the area
Notes: Figure 11.11

## Slide 38: Equation for flux density
where:
B = flux density in teslas (or webers/m2)
Φ = flux in webers
A = area (or csa) in square metres (m2).
One tesla equals one weber per square metre, i.e. one tesla is 108 lines of force in an area of one square metre (m2).

## Slide 39: Units for Area

## Slide 40
Example 11.1
Find the flux density of the two magnets (a) and (b) in Figure 11.11.
Values:
Figure 11.11

## Slide 41: Applications of permanent magnets
Permanent magnets are used in a range of devices
and tools
Notes: Figure 11.12

## Slide 42: Summing up
A magnet can be made by exposing a ferromagnetic material to a strong magnetic field.
The process is called magnetic induction, as the magnet is inducing magnetism in the ferromagnetic material.
A magnet has north and south poles. The north pole of a magnet points towards the Earth’s magnetic North Pole.
Unlike magnetic poles attract
Like magnetic poles repel

## Slide 43
A magnetic field (flux) consists of lines of force that flow from the north pole of a magnet to its south pole.
Lines do not cross each other, they all have the same magnetic strength and although they have a direction, they don’t actually move.
Materials are classified as: ferromagnetic (strongly attracted to a magnetic field) paramagnetic (weakly attracted by a strong magnetic field, e.g. oxygen) and diamagnetic (weakly repelled by a strong magnetic field, e.g. living tissue).
Summing up (2)

## Slide 44
A magnet can lose its magnetism as a result of excess heat, physical vibration and stress, and through exposure to a magnetic field of the opposite polarity.
A soft iron keeper across the poles of a magnet helps it retain its magnetism.
Magnetic flux (symbol F) is measured in webers, where one weber (Wb) is 100 million (108) lines of force.
Most magnetic fields have a flux in milliwebers (mWb) or microwebers (µWb).
Summing up (3)

## Slide 45
Flux density (B) refers to the number of lines of force (F) in a given area (A).
B is measured in teslas, where one tesla equals one weber of flux per square metre.
That is:
Summing up (4)

## Slide 46
Practical Exercise
Magnets & Magnetism
L