## Slide 1
Lesson 3
Chapter 11
Magnetism & Electromagnets
Section
11.5 Magnetisation curves

## Slide 2: 11.5 Magnetisation curves
The way a magnetic material responds to a magnetic field can be shown by measuring the flux density (B) in the material for different values of magnetising force (H).
The magnitude and direction of a magnetic field in a magnetic material can be measured with an instrument called a magnetometer, sometimes known as a Tesla meter, or Gaussmeter.

## Slide 3: B–H curve
A B–H curve shows how the flux density changes with
magnetising force
Notes: Figure 11.27

## Slide 4: Shape of B–H curve
The shape of a B–H curve depends on the material.
Some saturate more rapidly.
Some have a linear region over a wider range of magnetising forces.
Each material will have a different value of flux density at a particular magnetising force.
Notes: Figure 11.28

## Slide 5: Magnetic hysteresis
A test that yields more information about a magnetic material is achieved by passing an alternating current through the coil.
Because the current is periodically changing direction, the magnetic field will periodically change polarity.
That is, the magnetic core will be magnetised in one direction, then in the other, on a repeating basis.
At no stage is the material saturated.

## Slide 6: Hysteresis curve
Called a hysteresis curve (lagging behind) because when H is zero, B is not zero
Notes: Figure 11.29

## Slide 7: Example hysteresis loops
A ‘soft’ magnetic material is more easily magnetised and
de-magnetised than a ‘hard’ magnetic material
Notes: Figure 11.30

## Slide 8: Ferrite hysteresis loop
Ferrite is a hard magnetic material with an almost square
hysteresis loop
Notes: Figure 11.31

## Slide 9: Magnetic losses
1. Hysteresis loss caused by a material’s hysteresis. A comparison between materials can be seen from their hysteresis curves. The smaller the area enclosed by the curve, the lower the losses.
2. Eddy current loss occurs when a coil is supplied with alternating current. To reduce this, the core of the coil is laminated.
3. Fringing and leakage loss due to flux flowing outside the core.

## Slide 10: Reducing eddy current loss
Electromagnets operating with an alternating current have a laminated core to minimise eddy currents flowing in the core
Notes: Figure 11.32

## Slide 11: Magnetic leakage
Magnetic fringing and leakage contribute to the losses in a
magnetic circuit
Notes: Figure 11.33

## Slide 12: Summing up
The B–H curve shows how much flux density B is produced in a material at various values of magnetising force H.
Permeability of a magnetic material changes with flux density, and is maximum near the knee of the B–H curve.
A hysteresis loop (or curve) of a magnetic material shows how the flux density changes when the magnetising force is periodically reversed by passing an alternating current through the magnetising coil.

## Slide 13: Summing up (2)
The term hysteresis means the lag between the magnetising force and the state of magnetisation of the material.
The smaller the area enclosed by a material’s hysteresis loop, the lower the hysteresis losses in the material, and the more suited the material is for use with an alternating magnetic field.
All magnetic circuits have losses, which include hysteresis loss, eddy current loss, magnetic fringing and leakage.