## Slide 1
Lesson 15
Chapter 23
Single Phase Motors
Sections
23.2 Capacitor motors
23.3 Shaded pole induction motors
23.4 Universal motors

## Slide 2: 23.2 Capacitor motors
Typical capacitor motors
Notes: Figure 23.8

## Slide 3: Motor capacitors
Motor capacitors range from a few microfarads to over 200 µF. They have an AC voltage rating.
Capacitors in the starting circuit are often non-polarised electrolytics.
Capacitors in circuit while the motor is running are usually oil-filled paper or plastic film dielectric types.
Notes: Figure 23.9

## Slide 4
Capacitor start motor
Circuit of a capacitor start, induction run motor in which the phase difference between the start and run currents approaches 90º
Notes: Figure 23.10

## Slide 5
Current relay in the start circuit
(a) A current relay is used in the start circuit of capacitor motors rated above 750 W
(b) Capacitor start motors have a starting torque up to four times the rated torque
Notes: Figure 23.11

## Slide 6
Capacitor start, capacitor run motor
The auxiliary (start) winding is always connected to the supply via either of the two capacitors.
The start capacitor has a greater capacitance than the run capacitor.
This type of motor has a good starting torque and is smooth running.
Notes: Figure 23.12

## Slide 7: Permanently-split capacitor motor
A permanently-split capacitor motor does not have a starting switch.
It is reversed by adding an external switch that selects which of the identical windings has a capacitor in series with it.
Notes: Figure 23.13

## Slide 8: Faults in capacitor motors
As well as the faults that can occur in any induction motor, a capacitor motor can fail due to a faulty capacitor.
Capacitor faults are either an open-circuit, low resistance dielectric which means it can’t hold a charge, or a short-circuit.
A failing capacitor can also become leaky in that its dielectric seeps outside the can.

## Slide 9: 23.3 Shaded-pole induction motors
Shaded-pole motors are used in all kinds of fans, small pumps, clothes driers and have power ratings that rarely exceed a few hundred watts
Notes: Figure 23.14

## Slide 10: Shaded-pole operation
The shading rings in a shaded-pole motor cause the flux to concentrate in different parts of the poles, depending on how fast the current is changing
Notes: Figure 23.15

## Slide 11: 23.4 Universal motors
The universal motor is not an induction motor, as it has a wound armature like those in a DC motor.
They are called universal because they operate from AC and DC.
The universal motor is used in mains-powered hand tools (drills, saws, planers, etc.), vacuum cleaners and applications where a high speed, relatively small motor is required.

## Slide 12: Example universal motor
The field coils are in series with the armature, and the stator and armature core are laminated
Notes: Figure 23.16

## Slide 13: Circuit and torque/speed curve
Maximum torque of a universal motor is produced at start-up, and reduces significantly with speed
Notes: Figure 23.17

## Slide 14: Chapter summary
All single-phase induction motors require some means of creating a rotating magnetic field to start the rotor turning.
Once rotating above a certain speed, the rotor and stator magnetic fields produce the rotational torque.
All induction motors have a squirrel cage laminated steel rotor. The cage is usually made of aluminium.

## Slide 15: Chapter summary (2)
A split-phase induction motor has two windings, one with a higher resistance and lower inductance (auxiliary winding) than the other (main winding).
This creates a phase shift between the winding currents, giving a rotating field that can start the motor turning.
The auxiliary winding is disconnected from the supply when the motor reaches around 75 per cent of its rated speed.

## Slide 16: Chapter summary (3)
The auxiliary winding is disconnected from the supply by a centrifugal switch mechanism, or a current relay in series with the main winding.
A capacitor start motor has a large value capacitor in series with the auxiliary winding that provides additional phase shift between the winding currents during starting, giving the motor an increased starting torque.

## Slide 17: Chapter summary (4)
A permanently-split capacitor motor has two identical windings with a capacitor permanently in series with one of them.
It does not have a start switch, it is easily reversed and runs smoothly and quietly.
A shaded-pole motor has a copper shading coil fitted to the trailing tips of the stator poles.
It has limited starting torque, low efficiency, and cannot be easily reversed.

## Slide 18: Chapter summary (5)
A universal motor runs on AC and DC, and has a wound armature in series with the field coils.
The highest torque occurs at start-up, it can reach high speeds when unloaded, and features a high power to weight ratio.
Tests on a motor to prove serviceability include winding resistance tests, confirming correct operation of the start switch mechanism or relay, and measuring the insulation resistance between windings and motor frame.

## Slide 19: Equation summary
where:
ns = synchronous speed in RPM
f = supply frequency in hertz
p = number of poles.

## Slide 20: Equation summary (2)
where:
s% = percentage slip
ns = synchronous speed
n = rotor speed.

## Slide 21: Equation summary (3)
where:
fr = rotor frequency
f = supply frequency.

## Slide 22: Equation summary (4)
where:
Pin = VI cos ϕ