## Slide 1
Lesson 14
Chapter 23
Single Phase Motors
Sections
23.1 Single phase induction motor

## Slide 2
Chapter 23
Single-phase motors

## Slide 3: About this chapter
Single-phase motors are used extensively and operate in a similar way to the three-phase induction motor, but have an additional winding to make them start.
This chapter:
looks at the various types of single-phase motors, including capacitor motors, shaded-pole motors and universal motors
describes these motors, their protection requirements and typical faults.

## Slide 4: Contents
23.1 Single-phase induction motors
23.2 Capacitor motors
23.3 Shaded-pole induction motors
23.4 Universal motors

## Slide 5: 23.1 Single-phase induction motors
A single-phase motor produces a pulsating magnetic field that holds the rotor stationary. It therefore needs an extra winding to make it start rotating.
Notes: Figure 23.1

## Slide 6: Split-phase induction motor
A split-phase induction motor has two sets of windings, in which the run winding has a higher inductance and a lower resistance than the start (auxiliary) winding
Notes: Figure 23.2

## Slide 7: Centrifugal switch
During starting, the phasor addition of the currents in the start and run windings creates a rotating magnetic field.
Once the motor is at around 75% of its running speed, the start winding can be disconnected by a centrifugal switch.
Centrifugal switch assembly
Notes: Figure 23.3

## Slide 8: Circuit – split-phase induction motor
This circuit incorporates a centrifugal switch and circuit
This circuit has a motor start relay to switch the start (auxiliary) winding
Notes: Figure 23.4

## Slide 9: Typical split-phase induction motor
A typical split-phase induction motor with a centrifugal switch in the start circuit
Notes: Figure 23.5

## Slide 10: Split-phase motor characteristics
Synchronous speed of a split-phase motor:
where:
ns = synchronous speed in RPM
f = supply frequency in hertz
p = number of poles.

## Slide 11: Torque/speed curve
Typical torque/speed curve for a split-phase induction motor
Notes: Figure 23.6

## Slide 12: Protection
Motor protection and isolation requirements are specified by AS/NZS 3000:2007 in section 4.13.
Unattended split-phase motors rated higher than 240 VA are required to have protection against over-temperature.
Protection devices include a thermistor embedded in the winding and a bimetal snap-action switch.

## Slide 13: Testing and fault-finding
Common faults in a single-phase induction motor are dust and dirt build-up inside the motor, and bearing failure.
If a motor won’t start, check for faulty centrifugal switch contacts, operation of the thermal overload, an open circuit auxiliary or main winding, a locked rotor or loss of supply.
If the motor hums and attempts to start, the load may be jammed.

## Slide 14: Insulation resistance
Tests include measuring the DC resistance of both windings and measuring the insulation resistance between windings and motor frame, which should be earthed
Notes: Figure 23.7