## Slide 1
Lesson 11
Chapter 22
Three Phase Motors
Sections
22.3 Induction motor load characteristics

## Slide 2: 22.3 Induction motor load characteristics
Losses in an induction motor include iron and copper losses in the stator and the core, and mechanical losses
Notes: Figure 22.21
Adapted from Duff, Alternating Current Fundamentals 4e, © 1991 Delmar Learning, a part of Cengage Learning, Inc, reproduced by permission, www.cengage.com/permissions

## Slide 3: Efficiency
Percentage efficiency of a three-phase induction motor:
Notes: Figure 22.22

## Slide 4: No-load operation
Phasor diagrams of a three-phase induction motor on (a) no-load and (b) full load. Power factor is improved on full load.
Notes: Figure 22.24

## Slide 5: Full-load operation
Graphs relating efficiency, power factor and speed for a typical three-phase induction motor from no-load to full load
Notes: Figure 22.25

## Slide 6: Fault-finding a three-phase induction motor
Aspects to consider with motor failure:
mechanical, such as worn bearings, loose couplings, mechanical failures of the motor itself
three-phase supply problems
electrical problems with the motor windings or stator cage.

## Slide 7: Typical symptoms
Motor fails to start.
Motor does not run properly and exhibits noise and hum.
Motor runs slowly. Could be due to short-circuited or reversed coil or group of coils, worn bearings, overload or loose rotor bars.
Motor becomes too hot. Causes could be overload, worn or tight bearings, winding short-circuit, motor running on single-phase or loose rotor bars.

## Slide 8: Loss of one supply phase
Failure of one phase of the supply while a motor is running will cause it to remain running but to overheat
Notes: Figure 22.26

## Slide 9: Worn bearings
Worn bearings will cause the air gap between the stator and rotor to no longer be consistent
Notes: Figure 22.27

## Slide 10: Reversed winding
The effect of a reversed phase winding is to cause the motor to rotate slowly, if at all, and to emit a growling sound. There will be excessive current in each phase winding.
Notes: Figure 22.28

## Slide 11: Insulation resistance
A motor can have failing winding insulation, particularly in older motors. The resistance of the insulation between windings and motor core should exceed 1 MΩ.
Notes: Figure 22.29

## Slide 12: Effects of reduced voltage
Torque changes with the square of the voltage applied to the motor:
Notes: Figure 22.30

## Slide 13: Summing up
Losses in an induction motor include stator I2R and iron losses, rotor I2R and iron losses, and mechanical losses due to friction and windage.
The input power to a three-phase induction motor:
Pin = √3VLIL cos ϕ.
Motor output power:
Efficiency:

## Slide 14: Summing up (2)
Efficiency of three-phase induction motors is subject to Minimum Energy Performance (MEPS) requirements (AS/NZS 1359.5:2004).
An unloaded motor has a low power factor and zero efficiency.
A loaded motor has a higher power factor and an efficiency determined by the size and design of the motor.

## Slide 15: Summing up (3)
An open-circuit phase winding or loss of one supply phase causes a three-phase motor to operate as a single-phase motor, which will overheat the motor. As well, the motor will not start from rest.
Faults in three-phase motors include short-circuited coils, shorts between windings and frame, low leakage resistance, loose or open-circuit bars in the rotor cage and worn bearings or shafts.

## Slide 16: Summing up (4)
Torque varies with the square of the applied voltage.
A voltage reduction of 50 per cent will reduce the torque to 25 per cent of its rated value.
A low supply voltage to a motor can cause it to stall and burn out.