## Slide 1
Lesson 9
Chapter 22
Three Phase Motors
Sections
22.1 Three Phase Induction Motor

## Slide 2
UEENEEG006A
Solve Problems in Single Phase
& Three Phase Low Voltage Machines
Transformers (Static Machines) &
Rotary Machines (Motors & Generators)
Notes: Title

## Slide 3
01/04/19
08/04/19
29/04/19
06/05/19
13/05/19
20/0519
27/05/19
03/06/19
17/06/19
10/06/19
Term Break
Notes: 10/06/19 is PUBLIC Holiday – Will need to fit 24.1 & 24.2 into one week

## Slide 4
NOTE: No practical for AC Machines Test #1
NOTE: No practical for AC Machines Test #1
04/03/19
25/03/19
13/05/19
17/06/19

## Slide 6
Chapter 22
Three-phase motors

## Slide 7: About this chapter
The three-phase induction AC motor is attributed to a number of people, including Nikola Tesla. Today this type of motor is the workhorse of industry, noted for its simplicity, reliability and smooth running.
This chapter:
explains the operation of three-phase induction and wound rotor motors
explains the principles of motor protection and starting systems
looks at typical faults associated with these types of motors.

## Slide 8: Contents
22.1 Three-phase induction motor
22.2 Wound rotor induction motor
22.3 Induction motor load characteristics
22.4 Motor protection

## Slide 9: 22.1 Three-phase induction motor
Examples of typical three-phase induction motors
Notes: Figure 22.1

## Slide 10: Construction
Construction of a three-phase induction motor
Notes: Figure 22.2
Adapted from Herman, Standard Textbook of Electricity 1e, © 1993 Delmar Learning, a part of Cengage Learning, Inc, reproduced by permission, www.cengage.com/permissions

## Slide 11: Squirrel cage rotor
The rotor in an induction motor consists of bars of either copper or aluminium supported and connected electrically by end rings. This assembly is embedded in a laminated iron core.
Notes: Figure 22.3
Adapted from Duff, Alternating Current Fundamentals 4e, © 1991 Delmar Learning, a part of Cengage Learning, Inc, reproduced by permission, www.cengage.com/permissions

## Slide 12: Stator
The stator is supported inside the motor frame and made with steel laminations. Windings fit inside the slots. A three-phase motor has three sets of windings displaced by 120º.
Notes: Figure 22.4
Adapted from Duff, Alternating Current Fundamentals 4e, © 1991 Delmar Learning, a part of Cengage Learning, Inc, reproduced by permission, www.cengage.com/permissions

## Slide 13: Rotating magnetic field
The windings of a three-phase motor are arranged to provide a rotating magnetic field when connected to a three-phase supply
Notes: Figure 22.5

## Slide 14: Speed of rotation
The speed of rotation of the magnetic field is called the synchronous speed. It can be found for a motor with any number of poles with:
where:
ns = synchronous speed in RPM
f = supply frequency in hertz
p = number of poles.

## Slide 15: Direction of rotation
Reversing the supply phase sequence reverses the direction of rotation of the magnetic field
Notes: Figure 22.6

## Slide 16: Induction motor operating principles
Currents induced in the rotor conductors produce magnetic fields that have a direction to cause the rotor to spin in the direction of the stator’s rotating magnetic field
Notes: Figure 22.7

## Slide 17: Slip speed
An induction motor cannot run at synchronous speed because, to produce torque, there has to be rotor flux, which is only developed when the rotor runs at a slightly slower speed.
The difference between motor speed (n) and synchronous speed (ns) is the slip speed (s), which as a percentage:

## Slide 18
Rotor frequency
Rotor frequency is the frequency of the circulating current induced in the rotor, and is maximum when the rotor is stationary
Notes: Figure 22.8

## Slide 19
Rotor frequency equation
where:
fr = rotor frequency
f = supply frequency
s% = percentage slip.

## Slide 20
Motor terminal block markings
Three-phase motor terminal blocks usually have six terminals with links to change connections
Notes: Figure 22.9

## Slide 21: Example connections
Terminal block connections for internally connected
three-phase motors
Notes: Figure 22.10

## Slide 22: Example connections (2)
Terminal block connections for externally connected three-phase motors
Notes: Figure 22.11

## Slide 23: Summing up
The rotor in an induction motor has a squirrel cage assembly in which induced currents can flow, thereby producing a magnetic field.
The stator of a three-phase induction motor is laminated and contains three sets of identical windings that are connected in delta or star.

## Slide 24: Summing up (2)
A three-phase supply provides a rotating magnetic field which rotates at synchronous speed (ns).
This speed equals 120 times the supply frequency, divided by the number of poles in the motor.
Torque in an induction motor is caused by interaction of the stator and rotor magnetic fields.

## Slide 25: Summing up (3)
An induction motor has to run at slightly less than synchronous speed to maintain torque. This speed is the slip speed, usually expressed as a percentage of the synchronous speed.
Motor windings are identified with the letters U, V and W, the winding starts with a subscript 1, ends with a
subscript 2.