## Slide 1: Chapter 3 Network Noise and Intermodulation Distortion

## Slide 2: Introduction
Noise is one of the most important factors affecting the operations of IC circuits. This is because noise represents the smallest signal the circuit can process.
The principle noise sources are Johnson noise generated in resistors due to random motion of carriers; shot noise arising from the discreteness of charge quanta; mixer noise arising from non-ideal properties of mixers; undesired cross coupling of signals between two sections of the receiver; flicker noise due to defects in the semiconductor; and power supply noise.
Except for Johnson noise and shot noise the other noise sources can be improved or eliminated through proper design
The “Noise Figure” measures the noise generated in a network, together with the “dynamic range” are used to quantify the receiver performance

## Slide 3: Noise
All signals are contaminated with noise
The noisiness of a signal is specified by the signal-to-noise ratio defined as
The last definition will be adopted.
Noise of human origin is usually the dominant factor in receiver noise. This can usually be eliminated through proper design, layout, and shielding. Random noise cannot be eliminated. It sets the theoretical lower limit on receiver noise
The mean square noise voltage are referred to as the noise power
The noise power is normally frequency-dependent and is usually expressed as a power spectral density function. The total noise power is

## Slide 4
Thermal Noise (Johnson Noise)
Discovered by J.B. Johnson and is therefore commonly known as Johnson noise
The rms value of thermal noise voltage En is given by
Since the noise voltage squared is proportional to f. This implies that if the interval is infinite, the noise power contributed by the resistor is also infinite.
In reality the above equation must be modified above 100 MHz, but is sufficiently accurate for low frequency
R(f) is the real part of the impedance Z(f) looking into the two terminals between which En is measured.
If a resistor is connected to a frequency-dependent network as shown

## Slide 5
then the total noise due to R is
Where G(f) is the magnitude squared of the frequency-dependent transfer function between the input and the output voltages
Since R(f) depends on frequency
The integral of G(f) is known as the noise bandwidth Bn of the system.
If 2 resistors are connected in series, it is the voltage squared, not the noise voltages, which are added.

## Slide 6
Example 3.1
The impedance of the parallel combination of a resistor R and capacitor C is given by
The real part is given by
We can calculate E02 using
Since

## Slide 7: Current-source representation
So far we used voltage sources in series with a noiseless resistor to represent thermal noise. Norton’s theorem shows that the voltage noise source can also be represented by a current generator in parallel with a noiseless resistor as show below
Shot Noise
Shot noise is due to discreteness of the electronic charge arriving at the anode giving rise to pulses of current. The current noise power spectrum is

## Slide 8
Flicker Noise
This type of noise is found in all semiconductor devices under the application of a current bias
The mean squared current fluctuation over a frequency range f is
Metal films show no or very small flicker noise, thus they should be used for CKT design if low 1/f noise is desired

## Slide 9
K1 may vary by over orders of magnitude because flicker noise is caused by various unknown mechanisms such crystal imperfections, contamination.
Although flicker noise appears to be dominant at low-frequencies, it may still affect rf applications of the communication circuits through the nonlinear properties of the oscillators and mixers which mixes the noise to the carrier frequencies
Avalanche Noise
This is caused by Zener or avalanche breakdown in a pn junction
Electrons and holes in the depletion region of a reversed-biased junction acquire enough energy
Since additional electrons and holes are generated in the collision process a random series of large noise spikes will be generated.
The most common situation is when Zener diodes are used in the circuit and should therefore be avoided in low noise circuits.
The magnitude of the noise is hard to predict due to its dependence on the materials

## Slide 10: Noise Models of IC Components
I. Junction Diode
The equivalent circuit for a junction diode the equivalent circuit is shown to be
Rs is a physical resistor due to resistivity of the silicon, it exhibits thermal noise.
The current noise source is due to shot noise and flicker noise. Thus

## Slide 11
II. Bipolar Transistors
In a bipolar transistor in the forward-active region, minority carriers entering the collector-base depletion region are being accelerated to the collector. The time of arrival is a random process process, thus IC shows full shot noise.
The base current IB is due to recombination in the base and base-emitter depletion regions and also due to carrier injection from the base into the emitter.
Thus IB also shows full shot noise characteristics. The recombination process in the region also contribute to burst noise and flicker noise.
Transistor base resistor is a physical resistor and thus has thermal noise
Collector rc also shows thermal noise, but since this is in series with the high-impedance collector node, this noise is usually neglected. r and rb are fictitious resistors used for modeling and therefore do not contribute to thermal noise

## Slide 12
The equivalent circuit model for a BJT transistor is shown below
FET Transistor
FET shows full shot noise for the leakage current at the gate as well as thermal noise and flicker noise in the channel region.
Very often in JFETs the dominant type of noise is burst noise instead and in MOSFETs the dominant type of noise is flicker noise

## Slide 13: Circuit Noise Calculations
The device equivalent circuits can be used for calculation of noise performance. Consider a current noise source
if the rms current noise is represented by i, Within a small bandwidth, f, the effect of the noise current can be calculated by substituting by a sinusoidal generator and performing circuit analysis in the usual fashion. When the circuit response to the sinusoid is calculated, the mean-squared value of the output sinusoid gives the mean squared value of the output noise in bandwidth f.
In this way network noise calculations reduce to familiar sinusoidal circuit analysis calculations.
When multiple noise sources exists which is the case in most practical situations, each noise source is represented by a separate sinusoidal generator, and the output contribution of each source is calculated separately.
The total output noise in bandwidth f is calculated as a mean-squared value by adding the individual mean-squared contributions from each output sinusoid.
For example if we have 2 resistors in series the total voltage is

## Slide 14
Since the noise sources v1 and v2 are statistically independent of each other arising from two separate resistors the average of the product v1 v2 will be zero
Analogous results is true for independent current noise sources placed in parallel. The spectra are summed together.
Bipolar Transistor Noise Performance
Consider the noise performance of the simple transistor stage as shown
The total output noise can be calculated by considering each noise source in turn and performing the calculation as if each noise source were a sinusoid with rms value equal to that of the noise source being considered.

## Slide 15
Consider the noise generator vs due to Rs
where Z is the parallel combination of r and C. The output noise voltage due to vs

## Slide 16
Similarly it can shown that the output noise voltages by vb and ib are
Noise at the output due to is
The total output noise is
Substituting for Z we have

## Slide 17
The output noise power spectral density has a frequency-dependent part, which arises because the gain stage begins to fall above frequency f1, and noise due to which appears amplified in the output, also begins to fall. The constant term is due to noise generators
. Note that this noise contribution would also be frequency dependent if the effect of C had not been neglected. The noise voltage spectral density is shown in the following figure

## Slide 18: Equivalent Input Noise and Minimum Detectable Signal
The significance of the noise performance of a circuit is the limitation it places on the smallest input signal. For this reason the noise performance is usually expressed in terms of an equivalent input noise signal, which gives the same output noise as the circuit under consideration.
Such representation allows one to compare directly with incoming signals and the effect of the noise on those signals is easily determined.
Thus the circuit previously studied can be represented by
where is an input noise voltage generator that produces the same output noise as all of the original noise generators. All other source of noise are considered removed. Thus

## Slide 19
The above equation rises at high frequencies due to variation of |Z| with frequencies. This is due to the fact that as the gain of the device falls with frequency, output noise generators have larger effects when referred back to the input.
Example: Calculate the total input noise voltage, , for the circuit of the following circuit from 0 to 1 MHz

## Slide 20
Using the above equation for equivalent input noise
On the other hand we can use for the calculation of
If Av is the low-frequency gain
using the data

## Slide 21
The examples shows that from 0 to 1 MHz the noise appears to come from a 3.78 V rms noise-voltage source in series with the input. This can be used to estimate the smallest signal that the circuit can effectively amplify, sometimes called the minimum detectable signal (MDS). If a sine wave of magnitude 3.78 V were applied to this circuit, and the output in a 1-MHz bandwidth examined on an oscilloscope, the sine wave would be barely detectable
Equivalent Input Noise Generators
Using the equivalent input noise voltage an expression for equivalent input noise generator dependent on the source resistance can be determined.
To extend this to a more general and more useful representation using 2 equivalent input noise generators. The situation is shown below

## Slide 22
Here the two-port network containing noise generators is represented by the same network with internal noise sources removed and with a noise voltage and current generator connected to the input. It can be shown that this representation is valid for any source impedance, provided that the correlation of between the two noise generators is considered.
The 2 noise sources are correlated because they are both dependent on the same set of original noise sources.
However, correlation my significantly complicate the calculation. If the correlation is large, it may be simpler to go to the original circuit.
The need for both voltage and current equivalent input noise generators to represent the noise performance of the circuit for any source resistance can be appreciated as follows. Consider the extreme cases of source resistance RS=, cannot produce output noise and represents the noise performance of the original noisy network.

## Slide 23
The values of the equivalent input generators are readily determined. This is done by first short circuiting the input of both circuits and equating the output noise in each case to calculate . The value of is found by open circuiting the input of each circuit and equating the output noise in each case
Bipolar Transistor Noise Generators
The equivalent input noise generators for BJT can be calculated from the equivalent circuit of the following figure

## Slide 24
The 2 circuits are equivalent and should give the same output noise for any source impedance
The value of can be calculated by short circuiting the input of each circuit and equating the output noise,
From 11.23a we have
From 11.23b we have
Here we use rms noise quantities and make no attempts to preserve the signs of the noise quantities as the noise generators are all independent and have random phase. We also assume that .
Thus we have
Since rb is small the effect of is neglected
Using the fact that vb and ic are independent, we obtain
Using previous definition of
The equivalent noise-voltage spectral density thus appears to come from a resistor Req such that

## Slide 25
This is known as the “equivalent input noise resistance”
Here rb is a physical resistor in series with the input, whereas 1/2gm represents the effect of collector shot noise referred back to the input
The above equations allows one to compare the relative significance of noise from rb and IC in contributing to .
Good noise performance requires the minimization of Req. This can be accomplished by designing the transistor to have a low rb, and running the devices at a large collector bias current to reduce 1/2gm.
To calculate the equivalent input noise current, the inputs of both circuits are open circuited and the output noise currents, i0, are equated
which gives
Since ib and ic are independent generators, we obtain, where

## Slide 26
where 0 is the low-frequency, small signal current gain.
Substituting for gives
where . The last term is due to collector current noise referred to the input. At low frequencies this becomes and is negligible compared with IB for typical 0 values. The equivalent input noise current spectral density appears to come from a current source Ieq and
Ieq is minimized by utilizing low bias currents in the transistor, and using high  transistors. It should be noted that low current requirement to reduce contradicts that for reducing
Spectral density for is frequency dependent both at low and high frequency regime due to flicker noise and collector current noise referred to the input respectively. fb and fa are defined as in the figure below

## Slide 28
Using the definition
The collect current noise is
at high frequencies, which increases as f2. Frequency fb is estimated by equating the above equation to the midband noise and is
For typical values of 0 it is approximately 2qIB We obtain

## Slide 29
The large signal current gain is
Therefore
Once the input noise generators have been calculated, the transistor noise performance with any source impedance is readily calculated.
Consider the following circuit
with a source resistance RS. The noise performance of this circuit can be represented by the total equivalent noise voltage in series with the input of the circuit as shown.
Neglecting noise in Rl and equating the total noise voltage at the base of the transistor

## Slide 30
If correlation between vi and ii is neglected this equation gives
Thus the expression for total equivalent noise voltage is
Using the data from previous example and neglecting 1/f noise we calculate the total input noise voltage for the circuit in a bandwidth 0 to 1 MHz. The total input noise in a 1 MHz bandwidth is

## Slide 31: Field-Effect Transistor Noise Generators
The equivalent noise generators for a field-effect transistor can be calculated from the equivalent circuit below
Figure (a) is made equivalent to figure (b).
The output noise in each case is calculated with a short-circuit load and Cgd is neglected.
If the input of each circuit in the figure is short circuited and the resulting output noise currents i0 are equated we obtain from shorting fig. a that

## Slide 32
Figure (a) is made equivalent to figure (b).
The output noise in each case is calculated with a short-circuit load and Cgd is neglected.
If the input of each circuit in the figure is short circuited and the resulting output noise currents i0 are equated we obtain from shorting fig. a that
From Fig. b we have
Thus
Substituting the expression for into the equation for total noise we have
The equivalent input noise resistance Req is defined as
where in which
The input noise-voltage generator contains a flicker noise component which may extend into the Mega Hertz region. The magnitude of flicker noise depends on the details of the processing procedure, biasing and the area of the device.

## Slide 33
Flicker noise generally increase as 1/A this is because larger devices contains more defects at the Si-SiO2 interface. An averaging effect occurs that reduces the overall noise.
Flicker noise varies inversely with the gate capacitance because trapping and detrapping lead to variation of the threshold voltage which is inversely proportional to the gate capacitance. The equivalent input-referred voltage noise can often be written as
Typical value for Kf is
Effect of Feedback on Noise Performance
The representation of circuit noise performance with two equivalent input noise generators is extremely useful in the consideration of the effect of feedback on noise performance.
Effect of Ideal Feedback
The series-shunt feedback amplifier is shown where the feedback network is ideal in the signal feedback to the input is a pure voltage source and the feedback network is unilateral. Noise in the basic amplifier is represented by input noise generators

## Slide 34
The noise performance of the overall circuit is represented by equivalent input generators

## Slide 35
The value of can be found by short circuiting the input of each circuit and equating the output signal. However, since the output of the feedback network has a zero impedance, the current generators in each circuit are then short circuited and the two circuits are then identical if
If the input terminals are open circuited, both voltage generators have a floating terminal and thus no effect on the circuit, for equal outputs, it is necessary that
Thus for the case of ideal feedback, the equivalent input noise generators can be moved unchanged outside the feedback loop and the feedback has no effect on the circuit noise performance.
Since the feedback reduces circuit gain and the output noise is reduced by the feedback, but desired signals are reduced by the same amount and the signal-to-noise ratio will be unchanged.
Practical Feedback
Series-shunt feedback circuit is typically realized using a resistive divider consisting of RE and RF as shown

## Slide 37
If the noise of the basic amplifier is represented by equivalent input noise generators and , and the thermal noise generators in RE and RF are included in b as shown above. To calculate consider the inputs of the circuits of b and c short circuited, and equate the output noise
where . Assuming that all noise sources are independent we have where
Thus in a practical situation the equivalent input noise voltage of the overall amplifier contains the input noise of the basic amplifier plus two other terms. The second term is usually negligible, but the third represents the thermal noise in R and is often significant.
The equivalent input noise current, , is calculated by open circuiting both inputs and equating output noise. For the case of shunt feedback at the input as shown, opening circuiting the inputs of b and c and equating the output noise we have

## Slide 39
Thus the equivalent input noise current with shunt feedback applied consists of the input noise current of the basic amplifier together with a term representing thermal noise in the feedback resistor. The second term is usually negligible. If the inputs of the circuits of b and c are short circuited ant the output noise equated it follows that

## Slide 40: Amplifier Noise Model
As in the case before, amplifier noise represented by a zero impedance voltage generator in series with the input port and an infinite impedance current generator in parallel in the input and by a complex complex correlation coefficient C.
The equivalent model is shown in the next page where noise sources En, Et and In are used. Here Et is the noise generator for the signal source. Again we determine the equivalent input noise, Eni, to represent all 3 sources. The levels of signal voltage and noise voltage that reach Zin in the circuit are multiplied by the noiseless gain Av

## Slide 41
The system gain is defined by
For signal voltage, linear voltage and current division principles can be applied. However, for the evaluation of noise, we must sum each contribution in mean square values. The total noise at the output port is
The noise at the input to the amplifier is
The total output noise above divided by yields the expression for equivalent input noise
is independent of the amplifier’s gain and its input impedance. This makes the most useful index for comparing the noise characteristics of various amplifiers and devices. If the individual noise sources are correlated an additional term must be added to the above expression

## Slide 42: Noise in Feedback Amplifiers
Feedback is an important technique to alter gains, impedance levels, frequency response and reduce distortion. When negative feedback is properly applied the critical performance indexes are improved by a factor 1+A. However, with noise it was shown that feedback does not affect the equivalent input noise, but the added feedback resistive elements themselves will add noise to the system.
To examine how noise is affected by feedback we consider the block diagram

## Slide 43
The desired input voltage Vin and all the E’s representing the noise voltages being injected at various critical points in the system. Blocks A1 and A2 represent amplifiers with voltage gains and  represents the feedback network. The output voltage V0 is a function of all 5 inputs according to
For comparison consider an open-loop system in which the feedback loop  is taken out
To accomplish a meaningful comparison between the 2 cases we set
and we find that V0 for the open loop case is
Thus feedback does not give any improvement for any noise source introduced at the input to either amplifier regardless of whether this noise source exists before or after the summer. Noise injected at the amplifier’s output is attenuated in the feedback amplifier.

## Slide 44
In fact, if the feedback consists of resistive elements will actually increase the output noise level due to added thermal noise from the feedback resistors.
Amplifier Noise Model for Differential Inputs
Since operational amplifiers are configured with differential inputs. Users can configure the feedback network an input signal so as to produce a noninverting amplifier, an inverting amplifier or a true differential amplifier. Therefore all op amp model having equivalent noise sources must be able to handle all of these different configurations.
The basic amplifier noise model is expanded as below

## Slide 45
Noise sources En1 and In1 are noise contributions from the amplifier reflected to the inverting input terminal referenced to ground. In2 and En2 are that reflected to the non-inverting terminal. Consider the typical amplifier circuit shown

## Slide 46
Voltages Vp and Vn are the voltages at the respective positive and negative inputs to the amplifier referenced to ground. The output voltage for an ideal op amp is
An ideal differential amplifier occurs when we make the coefficients of Vin1 and Vin2 have identical magnitudes and opposite signs. This condition is satisfied by choosing the resistors such that
Thus the output becomes
Thus the ideal difference mode voltage gain is R2/R1. To examine the noise behavior of the differential amplifier, first form a Thevenin equivalent circuit at the noninverting input as shown where Rp=R3//R4 and
Next insert noise voltage and current sources for the op amp and Thevenin equivalent noise sources for the resistors as shown

## Slide 47
Here 7 signal source have arbitrary polarities as shown. Here we assume the op-amp has a finite open loop voltage gain A but is ideal otherwise. The four defining equations for this circuit are

## Slide 48
The four equations give
As A  we obtain
Previously for clarity, we substituted voltage and current signal sources for corresponding noise sources. The gain to the output will be the same for both signal sources and noise sources from the same circuit position
The result is
The equation shows that each noise source contributes to the total squared output noise. Both equivalent input noise voltages and the noise from Rp are reflected to the output by the square of the noninverting voltage gain, .

## Slide 49
The positive input noise current “flows through” Rp establishing a noise voltage which, in turn, is reflected to the output by the same gain factor .
The negative input noise voltage “flows through” the feedback resistor R2 establishing a noise voltage directly at the output. Finally noise contribution due to R2 appears directly at the output.
To determine Eni we first decide which terminal will be the reference. This is critical since the Kt’s are different for the inverting and non-inverting inputs
First reflect to the inverting input by dividing by (R2/R1)2 to obtain
where
Note that two amplifier noise voltages plus are all increased at the input by (1+R1/R2)2. Usually R1<<R2 for a typical high-gain amplifier application, so the first 3 noise voltage sources essentially contribute

## Slide 50
directly to Eni12 as does E2t1. The noise current of the feedback resistor R2 is multiplied by R12. The In1 noise current “flows through” R1 creating a direct contribution to Eni12. The In2 noise current “flows through” Rp to produce a noise voltage and then is reflected to the inverting input by the same factor.
When reflected to the noninverting input, we divide the noise equation by

## Slide 51
Here the two amplifier noise voltages as well as the noise voltage from Rp contribute directly to . The noise voltage in the feedback resistor is divided by the square of feedback factor. The noise in R1 is slightly diminished but essentially unchanged when R1<<R2. The inverting noise flows through the parallel combination of R1 and R2 and then contributes directly to . The non-inverting noise current “flows through” Rp and contributes directly to

## Slide 52: Noise in Inverting Negative Feedback Circuits
The inverting amplifier configuration with resistive negative feedback is the most widely used stage configuration. The input offset voltage due to bias current will be canceled by making Rp a single resistor equal to the parallel combination of Rs and R2.
All noise source are now reflected to the Vin1 input, we obtain

## Slide 53
where
An op amp specification sheet normally provide En and In which are defined as
We can now define a new equivalent amplifier noise voltage
and

## Slide 54: Intermodulation Distortion