## Slide 1: Chapter 5 Sensors and Detectors
A detector is typically the first stage of a communication system. Noise in this stage may have significant effects on the operation of the entire system. In this chapter we will use detector and sensor interchangeably.
A detector or sensor senses a physical parameter of some kind. In the field of optics and infrared the term detector is typically used.
To develop the noise model of a sensor, we can start with its circuit diagram. From this we draw an ac equivalent circuit that includes all impedances and generators. To each resistance and current generator we add the appropriate thermal noise an excess noise. The current generators may have shot noise, 1/f noise and burst noise. Using this equivalent circuit an expression for gain and equivalent input noise can be derived.

## Slide 2
A typical sensor/detector electronic system includes a coupling device or network as well as an amplifier. The noise equivalent circuit of the coupling network is easily obtained, and the En-In representation is valid for the amplifier. When we combine these three parts, we obtain a equivalent for the system.
The derivation of the equivalent input noise for the system follows 3 steps:
  Determine the total output noise.
  Calculate the system gain.
  Divide the total output noise by the system gain to obtain the equivalent input noise.
General Noise Model For Detector System
In the diagram shown the sensor is described by its signal voltage Vs , its internal impedance Zs, and a noise generator Es which represents all sources of sensor noise. To generalize the diagram a coupling network represented by impedance Zc and an noise source Ec is included in shunt with the input. We want to combine and reflect all noise sources to the input as shown in Fig. b and c.

## Slide 4
A general form for the equivalent input noise voltage is
Alternatively
where
If the signal source is a current generator, the equivalent noise current expression is more convenient. If the signal is a voltage generator, the equivalent is more convenient.
Effect of Parallel Load Resistance
The simplest type of sensor is represented by a resistance in series with a signal voltage generator as shown

## Slide 5
Also shown is a shunt network consisting of Rp and noise generator Ep. One practical purpose of the circuit may be to supply the sensor with bias power. The signal Vs and noise Es of the sensor are in series with the source resistance. The input signal-to-noise power ratio is simply the ratio of Vs2 to Es2. When a load resistor such as Rp or other coupling network elements are added, the output signal-to-noise ratio is degraded.
Example: Determine the output signal-to-noise ratio when
Since Es=Ep it follows that
The output signal is Therefore, the output SNR is

## Slide 6
We conclude that a shunt resistor decreases the signal more than the noise and the result is a decrease in the SNR. For the matched condition, source resistance equal to the load resistance the SNR is reduced by 50%.
For a more complete circuit as shown below
Here a noisy shunt resistance is present. For convenience we represent its noise by a current generator . Amplifier noise En and In are added. We calculate the equivalent noise following the steps below:

## Slide 7
From the equivalent circuit determine the output noise Eno
Calculate the system gain Kt the transfer function from sensor to output
Divide the output noise by the system gain to obtain the equivalent input noise
Effect of Shunt Capacitance
Although capacitance is virtually noise free, it can increase the equivalent input noise. A shunt capacitance does not affect the sensor SNR because it decreases the sensor signal and noise equally, but not the following amplifier noise. Consider the equivalent circuit shown and using the method outlined above the output noise is

## Slide 8
The gain of the system is
Thus the equivalent input noise is

## Slide 9
Voltaic Sensor
As a first example we consider the case of a resistive sensor that generates a voltage signal. These detectors include the thermocouple, pyroelectric infrared cell, generators, and other primarily detectors that are resistive in nature that generate a voltage signal.
A simple circuit diagram is shown in

## Slide 10
The sensor is represented by the signal source Vs and the internal series resistance Rs. The voltage Vs is the output from the sensed physical or electrical parameter such as pressure or radiation. A coupling capacitor Cc can be used if we are interested exclusively in the time-varying output of the sensor. The element RL may be needed for impedance matching. The noise model of the sensor-amplifier system is shown in Fig. 8-2. The shunt capacitance Cp can be in the sensor assembly or it may represent the parasitic stray capacitance between lead wires. The amplifier is now represented by the noise parameters En and In.
For low noise, the noise contribution of RL is kept low if it is large. The shunt capacitance should be minimized to avoid increasing En at high frequencies. The decoupling capacitor Cc should be very large or removed to reduce its effect on the amplifier’s In noise at low-frequencies. The amplifier input resistance Ri can often be reduced with overall negative feedback to increase the corner frequency caused by Cp

## Slide 11: Optoelectronic Detector
An optoelectronic detector is used to detect various forms of visible and nonvisible radiation and has a wide range of applications such as infrared detection, heat measurement, light and color measurement, fiber optic detectors, sensors for compact disk players, laser detectors and many other uses.
There are 2 general types of solid-state photon detectors: photoconductive and photovoltaic.
In a photoconductive detector, radiation on a cell produced a current in addition to the dark current. Bias is applied to the cell to collect the current. In a photovoltaic detector, radiation on the cell produces a voltage directly. Photoconductive cells can be fabricated from bulk semiconductor material where the conductivity increases as radiant energy is absorbed.
The simplified circuit
diagram is shown in

## Slide 12
The reverse bias is supplied by VBB, which collects the current generated by the radiant photon signal. A voltage signal is developed across the load or bias resistor RB.
Most often photodiodes are used with op amps employing negative feedback to produce the photoconductive detector as shown below:
The feedback resistor RB produces a virtual ground at the anode of the photodiode which reduces the input impedance, and thereby increasing the frequency response. The output voltage is where ID is the reverse bias current in the photodiode. Ideally, R2=RB to reduce the output

## Slide 13
offset voltage caused by the input bias current. However, R2 adds noise as can be seen from the noise equivalent circuit below: The load resistor RB has the same effect on equivalent input noise and gain for either circuit. The noise equivalent circuit of the photodiode detector is shown in Fig.8-7. The signal current source Is is located at the input and :
rd = noiseless dynamic reverse-bias resistance of the photodiode
RB = feedback resistance
Rcell = cell series resistance (< 50)
R2 = bias resistor for noninverting input
Ecell = thermal noise of Rcell
En = amplifier noise voltage
Cd = cell capacitance
CW = stray wiring capacitance
ID = sensor dc photocurrent plus dark current
InB = (4kT/RB)1/2 = thermal noise of RB
Ip = (Ish2 +IG-R2 +I1/f2)1/2

## Slide 14
In1 = amplifier noise current for inverting input
In2 = amplifier noise current for noninverting input
I2 = thermal noise current of R2

## Slide 15
The cell capacitance Cd and wiring capacitance CW probably will be the frequency-limiting elements so they should be kept as small as possible. The input capacitance, Ci, and input resistance, Ri, drop out of the noise expression, they do affect the amplifier gain. This gives us a mechanism for optimizing the frequency and noise responses separately.