## Slide 1: Integrated Circuits Design for Applications in Communications
Dr. Charles Surya
Department of Electronic and Information Engineering
DE636 6220
ensurya@polyu.edu.hk

## Slide 2: Introduction to Radio Communication System
A radio communication system involves in the transmission of electric energy from one point to another
Electronic circuits including oscillators, amplifiers, transformers, modulators, and demodulators typically make up such a system
A typical satellite communication channel is shown in Fig. 1-2. Each channel is sampled and then converted to a digitally encoded signal that modulates a low-frequency carrier signal.

## Slide 3: A Satellite Communications Channel
The modulated signal uses a different carrier frequency sufficiently separated so that the signals can be combined with frequency overlay. This is known as frequency multiplexing.
The multiplexing is accomplished by shifting the signal in frequency by mixing with a local oscillator signal, then amplified and transmitted. development of which led to the establishment of the radio broadcasting industry.
There are other types of modulation techniques such as angle-modulation as described by

## Slide 4: RECEIVERS
The purpose of the receiver is to recover the original information from the received signal
The modulated signal is transmitted to a receiver where the signal is amplified and the information extracted
Since many different signals present simultaneously at the input it is important for the receiver to select the desired signal
This selection is made on the basis of the frequency of the input signal
The ability of the receiver to discriminate between signals of different frequencies is called receiver selectivity
The receiver may also serve to reconstruct and amplify the original waveform
All receivers have the common problems of selectivity, rejecting input noise, and detecting the desired signal
Early receivers did not have amplification function. However, this was changed with the invention of the vacuum tube triode

## Slide 5
The first vacuum tubes did not provide much gain In search for higher gain, E.H. Armstrong invented the “regenerative receiver” which used positive feedback from the output to the input
A simplified schematic of a regenerative receiver is shown in the following figure
The circuit was susceptible to oscillation and this design led to the invention of the oscillator

## Slide 6
The regenerative receiver was soon replaced by the tuned rf (TRF) receiver, a block diagram of which is shown below
It consists of 3 tuned RF amplifiers in cascade followed by a detector and power amplifier
This design was obsolete with the advance of the superheterodyne receiver by Armstrong
The superhet “shifts” the frequency of the input signal to that of the fixed frequency of the receiver filter.
It multiplies the input signal with a signal generated in a local oscillator

## Slide 7
The incoming signal is converted to an intermediate frequency by the first local oscillator and then is reduced to a low-frequency signal by the second mixer and low-pass filter
The local oscillator is selected so that one of these frequencies is equal to the center frequency of the intermediate-frequency of the IF filter (fIF).
Since the audio frequency fa is much less than the carrier frequency fc, for all practical purposes
where f0 is the local oscillator frequency
The advantage of this form of detection is that the same high-quality filter can be used for all input frequencies by varying f0, the local oscillator frequency
The IF output fIF + fa is then reduced to fa in the second mixer
This detection scheme might present a problem when there are a large number of signals of different frequencies at the input. Such as an “image frequency” which when mixed with the local oscillator produces a signal at IF

## Slide 8
For example, the receiver designed to select the difference frequency at the output of the first mixer is:
Thus the image frequency FIM is given by
which equals fC+2fIF. There is no way to separate the desired signal from a signal at the image frequency after they have entered the mixer
The image frequency signal must be removed before it enters the filter
This is accomplished by adding an image suppression filter known as a preselector before the mixer which must then be tunable. This tunable filter is complex and expensive
Majority of the receivers do include a tunable filter
In many cases the intermediate frequency is lower than the input signal frequency which is shifted down by the local oscillator. The intermediate center frequency can be selected above the input frequency, leading to the upconversion technique

## Slide 9
Also, up conversion technique results in all image frequencies lying above the frequency band to be covered. This implies that all image frequencies can be suppressed using a low-pass filter to the input
Until recently it is not possible to use up conversion as high-quality bandpass filters were not readily available in 30 to 50 MHz range
Another advantage is that oscillator-tuning ratio is less than that for down conversion

## Slide 10: A Modern Communications Receiver
A block diagram of the high frequency section of a modern radio receiver is essentially the same as the superheterodyne receiver but the circuits differ from the earlier models
One difference is that up conversion is often used in high-quality receivers so that the input filter can remain a simple LPF that does not require tuning
Whether an amplifier is required before the mixer depends on the particular application
A main difference between modern and old receivers is the use of the frequency synthesizer to generate the frequencies needed from the variable-frequency oscillator
The output of the synthesizer can be accurately controlled using digital circuitry. Thus, microprocessor control of radio receivers and spectrum analyzers is possible
Typical synthesizers also include a phase-locked-loop

## Slide 11: Direct Conversion Receivers
An immediate extension of the superheterodyne receiver is the direct conversion receiver in which the IF section is eliminated by converting the input signal directly to direct current baseband as shown below
The local oscillator frequency is set at the carrier frequency and the higher frequency signal at the output is removed by a LPF
The advantage is that it is much easier to build a LPF than a narrow-band intermediate frequency filter which requires more component and consumes more power than LPF
This type of receiver is typically referred to as a zero IF or ZIFF receiver

## Slide 12
The problems are 1.) local oscillator drift 2.) dc offsets 3.) local oscillator leakage back into the input stage from which it again mixes with the local oscillator output to create an erroneous dc output
Improvements in modern components led to reduction in the problems. As a result, direct conversion receivers are finding applications in many battery-operated systems
One major problem with direct conversion method is the phase uncertainty
This is solved by using an in-phase and a quadrature channel created by using the LO signal and the LO signal shifted by 90. The outputs of the 2 quadrature channels are then combined to recover the input signal
ZIFF receiver is used in many battery-operated applications
It is difficult to realize 90 over a wide bandwidth
An oscillator that does generate the in-phase and quadrature components of the oscillator signal is referred to as a quadrature oscillator

## Slide 13: Transmitters
The transmitter modulates the information onto a carrier, amplifies the waveform and delivers it to the transmitting antenna
The block diagram is as shown -- the rf oscillator is modulated by the message signal. The modulated signal is then multiplied in frequency up to a desired transmitting frequency and is amplified to a desired power level by the power amplifier
In this case the amplitude remains constant, the angle  is varied in response to the modulating signal.