## Slide 1
10.
Chapter 10
Error Detection and Correction
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2
10.
The Hamming distance between two words is the number of differences between corresponding bits.
Note

## Slide 3
10.
Let us find the Hamming distance between two pairs of words.
1. The Hamming distance d(000, 011) is 2 because
Example 10.4
2. The Hamming distance d(10101, 11110) is 3 because

## Slide 4
10.
The minimum Hamming distance is the smallest Hamming distance between all possible pairs in a set of words.
Note

## Slide 5
10.
Find the minimum Hamming distance of the coding scheme in Table 10.1.
Solution
We first find all Hamming distances.
Example 10.5
The dmin in this case is 2.

## Slide 6
10.
Find the minimum Hamming distance of the coding scheme in Table 10.2.
Solution
We first find all the Hamming distances.
The dmin in this case is 3.
Example 10.6

## Slide 7
10.
To guarantee the detection of up to s errors in all cases, the minimum
Hamming distance in a block code must be dmin = s + 1.
Note

## Slide 8
10.
The minimum Hamming distance for our first code scheme (Table 10.1) is 2. This code guarantees detection of only a single error. For example, if the third codeword (101) is sent and one error occurs, the received codeword does not match any valid codeword. If two errors occur, however, the received codeword may match a valid codeword and the errors are not detected.
Example 10.7

## Slide 9
10.
Our second block code scheme (Table 10.2) has dmin = 3. This code can detect up to two errors. Again, we see that when any of the valid codewords is sent, two errors create a codeword which is not in the table of valid codewords. The receiver cannot be fooled.
However, some combinations of three errors change a valid codeword to another valid codeword. The receiver accepts the received codeword and the errors are undetected.
Example 10.8

## Slide 10
10.
Figure 10.8 Geometric concept for finding dmin in error detection

## Slide 11
10.
Figure 10.9 Geometric concept for finding dmin in error correction

## Slide 12
10.
To guarantee correction of up to t errors in all cases, the minimum Hamming distance in a block code must be dmin = 2t + 1.
Note

## Slide 13
10.
A code scheme has a Hamming distance dmin = 4. What is the error detection and correction capability of this scheme?
Solution
This code guarantees the detection of up to three errors (s = 3), but it can correct up to one error. In other words, if this code is used for error correction, part of its capability is wasted. Error correction codes need to have an odd minimum distance (3, 5, 7, . . . ).
Example 10.9

## Slide 14
10.
10-3 LINEAR BLOCK CODES
Almost all block codes used today belong to a subset called linear block codes. A linear block code is a code in which the exclusive OR (addition modulo-2) of two valid codewords creates another valid codeword.
Minimum Distance for Linear Block Codes Some Linear Block Codes
Topics discussed in this section:

## Slide 15
10.
In a linear block code, the exclusive OR (XOR) of any two valid codewords creates another valid codeword.
Note

## Slide 16
10.
Let us see if the two codes we defined in Table 10.1 and Table 10.2 belong to the class of linear block codes.
1. The scheme in Table 10.1 is a linear block code because the result of XORing any codeword with any other codeword is a valid codeword. For example, the XORing of the second and third codewords creates the fourth one.
2. The scheme in Table 10.2 is also a linear block code. We can create all four codewords by XORing two other codewords.
Example 10.10

## Slide 17
10.
In our first code (Table 10.1), the numbers of 1s in the nonzero codewords are 2, 2, and 2. So the minimum Hamming distance is dmin = 2. In our second code (Table 10.2), the numbers of 1s in the nonzero codewords are 3, 3, and 4. So in this code we have dmin = 3.
Example 10.11

## Slide 18
10.
A simple parity-check code is a single-bit error-detecting code in which n = k + 1 with dmin = 2.
Even parity (ensures that a codeword has an even number of 1’s) and odd parity (ensures that there are an odd number of 1’s in the codeword)
Note

## Slide 19
10.
Table 10.3 Simple parity-check code C(5, 4)

## Slide 20
10.
Figure 10.10 Encoder and decoder for simple parity-check code

## Slide 21
10.
Let us look at some transmission scenarios. Assume the sender sends the dataword 1011. The codeword created from this dataword is 10111, which is sent to the receiver. We examine five cases:
1. No error occurs; the received codeword is 10111. The syndrome is 0. The dataword 1011 is created.
2. One single-bit error changes a1 . The received codeword is 10011. The syndrome is 1. No dataword is created.
3. One single-bit error changes r0 . The received codeword is 10110. The syndrome is 1. No dataword is created.
Example 10.12

## Slide 22
10.
4. An error changes r0 and a second error changes a3 .
The received codeword is 00110. The syndrome is 0. The dataword 0011 is created at the receiver. Note that
here the dataword is wrongly created due to the
syndrome value.
5. Three bits—a3, a2, and a1—are changed by errors. The received codeword is 01011. The syndrome is 1. The dataword is not created. This shows that the simple parity check, guaranteed to detect one single error, can also find any odd number of errors.
Example 10.12 (continued)

## Slide 23
10.
A simple parity-check code can detect an odd number of errors.
Note

## Slide 24
10.
All Hamming codes discussed in this book have dmin = 3 (2 bit error detection and single bit error correction).
A codeword consists of n bits of which k are data bits and r are check bits.
Let m = r, then we have: n = 2m -1
and k = n-m
Note

## Slide 25
10.
Figure 10.11 Two-dimensional parity-check code

## Slide 26
10.
Figure 10.11 Two-dimensional parity-check code

## Slide 27
10.
Figure 10.11 Two-dimensional parity-check code

## Slide 28
10.
Table 10.4 Hamming code C(7, 4) - n=7, k = 4

## Slide 29
10.
Modulo 2 arithmetic:
r0 = a2 + a1 + a0
r1 = a3 + a2 + a1
r2 = a1 + a0 + a3
Calculating the parity bits at the transmitter
:
Calculating the syndrome at the receiver:
s0 = b2 + b1 + b0
s1 = b3 + b2 + b1
s2 = b1 + b0 + b3

## Slide 30
10.
Figure 10.12 The structure of the encoder and decoder for a Hamming code

## Slide 31
10.
Table 10.5 Logical decision made by the correction logic analyzer

## Slide 32
10.
Let us trace the path of three datawords from the sender to the destination:
1. The dataword 0100 becomes the codeword 0100011. The codeword 0100011 is received. The syndrome is 000, the final dataword is 0100.
2. The dataword 0111 becomes the codeword 0111001. The received codeword is: 0011001. The syndrome is 011. After flipping b2 (changing the 1 to 0), the final dataword is 0111.
3. The dataword 1101 becomes the codeword 1101000. The syndrome is 101. After flipping b0, we get 0000, the wrong dataword. This shows that our code cannot correct two errors.
Example 10.13

## Slide 33
10.
We need a dataword of at least 7 bits. Calculate values of k and n that satisfy this requirement.
Solution
We need to make k = n − m greater than or equal to 7, or 2m − 1 − m ≥ 7.
1. If we set m = 3, the result is n = 23 − 1=7 and k = 7 − 3, or 4, which is < 7.
2. If we set m = 4, then n = 24 − 1 = 15 and k = 15 − 4 = 11, which satisfies the condition k>7. So the code is
Example 10.14
C(15, 11)

## Slide 34: Burst Errors
Burst errors are very common, in particular in wireless environments where a fade will affect a group of bits in transit. The length of the burst is dependent on the duration of the fade.
One way to counter burst errors, is to break up a transmission into shorter words and create a block (one word per row), then have a parity check per word.
The words are then sent column by column. When a burst error occurs, it will affect 1 bit in several words as the transmission is read back into the block format and each word is checked individually.

## Slide 35
10.
Figure 10.13 Burst error correction using Hamming code

## Slide 36
10.
10-4 CYCLIC CODES
Cyclic codes are special linear block codes with one extra property. In a cyclic code, if a codeword is cyclically shifted (rotated), the result is another codeword.
Cyclic Redundancy Check Hardware Implementation Polynomials Cyclic Code Analysis
Advantages of Cyclic Codes Other Cyclic Codes
Topics discussed in this section:

## Slide 37
10.
Table 10.6 A CRC code with C(7, 4)

## Slide 38
10.
Figure 10.14 CRC encoder and decoder

## Slide 39
10.
Figure 10.15 Division in CRC encoder

## Slide 40
10.
Figure 10.16 Division in the CRC decoder for two cases

## Slide 41
10.
Figure 10.17 Hardwired design of the divisor in CRC

## Slide 42
10.
Figure 10.18 Simulation of division in CRC encoder

## Slide 43
10.
Figure 10.19 The CRC encoder design using shift registers

## Slide 44
10.
Figure 10.20 General design of encoder and decoder of a CRC code

## Slide 45: Using Polynomials
We can use a polynomial to represent a binary word.
Each bit from right to left is mapped onto a power term.
The rightmost bit represents the “0” power term. The bit next to it the “1” power term, etc.
If the bit is of value zero, the power term is deleted from the expression.

## Slide 46
10.
Figure 10.21 A polynomial to represent a binary word

## Slide 47
10.
Figure 10.22 CRC division using polynomials

## Slide 48
10.
The divisor in a cyclic code is normally called the generator polynomial
or simply the generator.
Note

## Slide 49
10.
In a cyclic code,
If s(x) ≠ 0, one or more bits is corrupted.
If s(x) = 0, either
a. No bit is corrupted. or
b. Some bits are corrupted, but the decoder failed to detect them.
Note

## Slide 50
10.
In a cyclic code, those e(x) errors that are divisible by g(x) are not caught.
Received codeword (c(x) + e(x))/g(x) =
c(x)/g(x) + e(x)/gx
The first part is by definition divisible the second part will determine the error. If “0” conclusion -> no error occurred. Note: that could mean that an error went undetected.
Note

## Slide 51
10.
If the generator has more than one term and the coefficient of x0 is 1, all single errors can be caught.
Note

## Slide 52
10.
Which of the following g(x) values guarantees that a single-bit error is caught? For each case, what is the error that cannot be caught?
a. x + 1 b. x3 c. 1
Solution
a. No xi can be divisible by x + 1. Any single-bit error can be caught.
b. If i is equal to or greater than 3, xi is divisible by g(x). All single-bit errors in positions 1 to 3 are caught.
c. All values of i make xi divisible by g(x). No single-bit error can be caught. This g(x) is useless.
Example 10.15

## Slide 53
10.
Figure 10.23 Representation of two isolated single-bit errors using polynomials

## Slide 54
10.
If a generator cannot divide xt + 1 (t between 0 and n – 1),
then all isolated double errors can be detected.
Note

## Slide 55
10.
Find the status of the following generators related to two isolated, single-bit errors.
a. x + 1 b. x4 + 1 c. x7 + x6 + 1 d. x15 + x14 + 1
Solution
a. This is a very poor choice for a generator. Any two errors next to each other cannot be detected.
b. This generator cannot detect two errors that are four positions apart.
c. This is a good choice for this purpose.
d. This polynomial cannot divide xt + 1 if t is less than 32,768. A codeword with two isolated errors up to 32,768 bits apart can be detected by this generator.
Example 10.16

## Slide 56
10.
A generator that contains a factor of x + 1 can detect all odd-numbered errors.
Note

## Slide 57
10.
❏ All burst errors with L ≤ r will be detected.
❏ All burst errors with L = r + 1 will be detected with probability 1 – (1/2)r–1.
❏ All burst errors with L > r + 1 will be detected with probability 1 – (1/2)r.
Note

## Slide 58
10.
Find the suitability of the following generators in relation to burst errors of different lengths.
a. x6 + 1 b. x18 + x7 + x + 1 c. x32 + x23 + x7 + 1
Solution
a. This generator can detect all burst errors with a length less than or equal to 6 bits; 3 out of 100 burst errors with length 7 will slip by; 16 out of 1000 burst errors of length 8 or more will slip by.
Example 10.17

## Slide 59
10.
b. This generator can detect all burst errors with a length less than or equal to 18 bits; 8 out of 1 million burst errors with length 19 will slip by; 4 out of 1 million burst errors of length 20 or more will slip by.
c. This generator can detect all burst errors with a length less than or equal to 32 bits; 5 out of 10 billion burst errors with length 33 will slip by; 3 out of 10 billion burst errors of length 34 or more will slip by.
Example 10.17 (continued)

## Slide 60
10.
A good polynomial generator needs to have the following characteristics:
1. It should have at least two terms.
2. The coefficient of the term x0 should be 1.
3. It should not divide xt + 1, for t between 2 and n − 1.
4. It should have the factor x + 1.
Note

## Slide 61
10.
Table 10.7 Standard polynomials

## Slide 62
10.
10-5 CHECKSUM
The last error detection method we discuss here is called the checksum. The checksum is used in the Internet by several protocols although not at the data link layer. However, we briefly discuss it here to complete our discussion on error checking
Idea One’s Complement Internet Checksum
Topics discussed in this section:

## Slide 63
10.
Suppose our data is a list of five 4-bit numbers that we want to send to a destination. In addition to sending these numbers, we send the sum of the numbers. For example, if the set of numbers is (7, 11, 12, 0, 6), we send (7, 11, 12, 0, 6, 36), where 36 is the sum of the original numbers. The receiver adds the five numbers and compares the result with the sum. If the two are the same, the receiver assumes no error, accepts the five numbers, and discards the sum. Otherwise, there is an error somewhere and the data are not accepted.
Example 10.18

## Slide 64
10.
We can make the job of the receiver easier if we send the negative (complement) of the sum, called the checksum. In this case, we send (7, 11, 12, 0, 6, −36). The receiver can add all the numbers received (including the checksum). If the result is 0, it assumes no error; otherwise, there is an error.
Example 10.19

## Slide 65
10.
How can we represent the number 21 in one’s complement arithmetic using only four bits?
Solution
The number 21 in binary is 10101 (it needs five bits). We can wrap the leftmost bit and add it to the four rightmost bits. We have (0101 + 1) = 0110 or 6.
Example 10.20

## Slide 66
10.
How can we represent the number −6 in one’s complement arithmetic using only four bits?
Solution
In one’s complement arithmetic, the negative or complement of a number is found by inverting all bits. Positive 6 is 0110; negative 6 is 1001. If we consider only unsigned numbers, this is 9. In other words, the complement of 6 is 9. Another way to find the complement of a number in one’s complement arithmetic is to subtract the number from 2n − 1 (16 − 1 in this case).
Example 10.21

## Slide 67
10.
Let us redo Exercise 10.19 using one’s complement arithmetic. Figure 10.24 shows the process at the sender and at the receiver. The sender initializes the checksum to 0 and adds all data items and the checksum (the checksum is considered as one data item and is shown in color). The result is 36. However, 36 cannot be expressed in 4 bits. The extra two bits are wrapped and added with the sum to create the wrapped sum value 6. In the figure, we have shown the details in binary. The sum is then complemented, resulting in the checksum value 9 (15 − 6 = 9). The sender now sends six data items to the receiver including the checksum 9.
Example 10.22

## Slide 68
10.
The receiver follows the same procedure as the sender. It adds all data items (including the checksum); the result is 45. The sum is wrapped and becomes 15. The wrapped sum is complemented and becomes 0. Since the value of the checksum is 0, this means that the data is not corrupted. The receiver drops the checksum and keeps the other data items. If the checksum is not zero, the entire packet is dropped.
Example 10.22 (continued)

## Slide 69
10.
Figure 10.24 Example 10.22

## Slide 70
10.
Sender site:
1. The message is divided into 16-bit words.
2. The value of the checksum word is set to 0.
3. All words including the checksum are added using one’s complement addition.
4. The sum is complemented and becomes the checksum.
5. The checksum is sent with the data.
Note

## Slide 71
10.
Receiver site:
1. The message (including checksum) is divided into 16-bit words.
2. All words are added using one’s complement addition.
3. The sum is complemented and becomes the new checksum.
4. If the value of checksum is 0, the message is accepted; otherwise, it is rejected.
Note

## Slide 72
10.
Let us calculate the checksum for a text of 8 characters (“Forouzan”). The text needs to be divided into 2-byte (16-bit) words. We use ASCII (see Appendix A) to change each byte to a 2-digit hexadecimal number. For example, F is represented as 0x46 and o is represented as 0x6F. Figure 10.25 shows how the checksum is calculated at the sender and receiver sites. In part a of the figure, the value of partial sum for the first column is 0x36. We keep the rightmost digit (6) and insert the leftmost digit (3) as the carry in the second column. The process is repeated for each column. Note that if there is any corruption, the checksum recalculated by the receiver is not all 0s. We leave this an exercise.
Example 10.23

## Slide 73
10.
Figure 10.25 Example 10.23