## Slide 1
Chapter 10
Error Detection and Correction
Copyright © The McGraw-Hill Companies, Inc. Permission required for reproduction or display.

## Slide 2
Data can be corrupted during transmission.
Some applications require that errors be detected and corrected.
Note

## Slide 3
10-1 INTRODUCTION
Let us first discuss some issues related, directly or indirectly, to error detection and correction.
Types of Errors Redundancy Detection Versus Correction Forward Error Correction Versus Retransmission Coding
Modular Arithmetic
Topics discussed in this section:

## Slide 4
In a single-bit error, only 1 bit in the data unit has changed.
Note

## Slide 5
Figure 10.1 Single-bit error

## Slide 6
A burst error means that 2 or more bits in the data unit have changed.
Note

## Slide 7
Figure 10.2 Burst error of length 8

## Slide 8
To detect or correct errors, we need to send extra (redundant) bits with data.
Note

## Slide 9
Figure 10.3 The structure of encoder and decoder

## Slide 10
In this book, we concentrate on block codes; we leave convolution codes to advanced texts.
Note

## Slide 11
In modulo-N arithmetic, we use only the integers in the range 0 to N −1, inclusive.
Note

## Slide 12
Figure 10.4 XORing of two single bits or two words

## Slide 13
10-2 BLOCK CODING
In block coding, we divide our message into blocks, each of k bits, called datawords. We add r redundant bits to each block to make the length n = k + r. The resulting n-bit blocks are called codewords.
Error Detection Error Correction Hamming Distance
Minimum Hamming Distance
Topics discussed in this section:

## Slide 14
Figure 10.5 Datawords and codewords in block coding

## Slide 15
The 4B/5B block coding discussed in Chapter 4 is a good example of this type of coding. In this coding scheme, k = 4 and n = 5. As we saw, we have 2k = 16 datawords and 2n = 32 codewords. We saw that 16 out of 32 codewords are used for message transfer and the rest are either used for other purposes or unused.
Example 10.1

## Slide 16: Error Detection
Enough redundancy is added to detect an error.
The receiver knows an error occurred but does not know which bit(s) is(are) in error.
Has less overhead than error correction.

## Slide 17
Figure 10.6 Process of error detection in block coding

## Slide 18
Let us assume that k = 2 and n = 3. Table 10.1 shows the list of datawords and codewords. Later, we will see how to derive a codeword from a dataword.
Assume the sender encodes the dataword 01 as 011 and
sends it to the receiver. Consider the following cases:
1. The receiver receives 011. It is a valid codeword. The receiver extracts the dataword 01 from it.
Example 10.2

## Slide 19
2. The codeword is corrupted during transmission, and 111 is received. This is not a valid codeword and is discarded.
3. The codeword is corrupted during transmission, and 000 is received. This is a valid codeword. The receiver incorrectly extracts the dataword 00. Two corrupted bits have made the error undetectable.
Example 10.2 (continued)

## Slide 20
Table 10.1 A code for error detection (Example 10.2)

## Slide 21
An error-detecting code can detect only the types of errors for which it is designed; other types of errors may remain undetected.
Note

## Slide 22
Figure 10.7 Structure of encoder and decoder in error correction

## Slide 23
Let us add more redundant bits to Example 10.2 to see if the receiver can correct an error without knowing what was actually sent. We add 3 redundant bits to the 2-bit dataword to make 5-bit codewords. Table 10.2 shows the datawords and codewords. Assume the dataword is 01. The sender creates the codeword 01011. The codeword is corrupted during transmission, and 01001 is received. First, the receiver finds that the received codeword is not in the table. This means an error has occurred. The receiver, assuming that there is only 1 bit corrupted, uses the following strategy to guess the correct dataword.
Example 10.3

## Slide 24
1. Comparing the received codeword with the first codeword in the table (01001 versus 00000), the receiver decides that the first codeword is not the one that was sent because there are two different bits.
2. By the same reasoning, the original codeword cannot be the third or fourth one in the table.
3. The original codeword must be the second one in the table because this is the only one that differs from the received codeword by 1 bit. The receiver replaces 01001 with 01011 and consults the table to find the dataword 01.
Example 10.3 (continued)

## Slide 25
Table 10.2 A code for error correction (Example 10.3)