## Slide 1: Wave Propagation
Chapter 12

## Slide 2: Objectives
Discuss the makeup of electromagnetic waves
Explain
  Reflection
  Refraction
  Diffraction
Describe the important aspects of satellite communication

## Slide 3
Describe ground wave propagation
Describe space wave propagation
Calculate the approximate radio horizon based on antenna height
Discuss the effects of the ionosphere on sky wave propagation
Define critical angle and skip zone for sky wave

## Slide 4: Compliments of
IPS
LC

## Slide 5: Electrical to Magnetic Conversion
The antennas are the transducers
  The transmitting antenna changes the electrical energy into electromagnetic or waves
  The receiving antenna changes the electromagnetic energy back into electrical energy
These electromagnetic waves propagate at rates ranging from 150kHz to 300GHz

## Slide 6: Electromagnetic Waves
Consist of
  Magnetic wave
  Electrical wave
Most of the energy is returned to the circuit.
If it isn’t, then some it must be “set free” or radiated. Radiated energy is not desirable.
link

## Slide 7: Radio-frequency Interference
If the radiated energy comes from another radio transmitter, then it is considered radio-frequency interference (RFI)
The transmitting antenna should be specifically designed to prevent the energy from being returned to the circuit.
It is desirable that the antenna “free” the energy in order that it might radiate into space

## Slide 8: Electromagnetic Interference
If the energy comes from else where, then it is electromagnetic interference (EMI)

## Slide 9: Transverse Waves
Transverse waves are those whose direction of propagation is perpendicular to both the electrical field and the magnetic field The electrical field and the magnetic fields lie in planes that are perpendicular to each other. (x and y planes)
Thus the direction of propagation will be in the z plane or third dimension

## Slide 10: Polarization of the Electrical Field
The polarization of the electrical field is determined by the direction of oscillations
  If the oscillations are in the vertical direction then the polarization is said to be vertical
  If the oscillations are in the horizontal direction then the polarization is said to be horizontal

## Slide 11
Thus a “vertical” antenna will result in a vertically polarized wave.
A vertical antenna is one that consists of a vertical tower, wire, or rod, usually a quarter wavelength in length that is fed at the ground and uses the ground as a reflecting surface.

## Slide 12: Wavefronts
A wavefront is a plane joining all points of equal phase in a wave
Take a point in space. Imagine waves radiating outward in all directions from this point. The result would resemble a sphere. The point of radiation is called the isotropic point source

## Slide 13
Since the power at any point away from the isotropic point is inversely proportional to the square of the distance from the point, then the power decreases rapidly the further away from the point you need.
Although the wavefront is curved in shape, from a distance small sections appear planar and can be thought of as plane wavefronts

## Slide 14: Characteristic Impedance of Free Space
In free space:
   = 1.26 x 10-6 H/m
   = 8.85 x 10-12 F/m
   = 377 

## Slide 15: Not Free Space

## Slide 16: Four Types of Waves
Incident
Reflected
Refracted
Diffracted

## Slide 17: Reflection
Reflection is the abrupt reversal in direction
Caused by any conductive medium such as
  Metal surfaces or
  Earth’s surface
There will normally be a shift in phase
Coefficient of reflection is less than 1

## Slide 18: Complete Reflection
Complete reflection will occur only in perfect conductors and when the electric field is perpendicular to the reflecting element or medium
Coefficient of Reflection will be 1
Coefficient of Reflection is the ratio of the reflected wave intensity to the incident wave intensity

## Slide 19: Electrical Fields Parallel to the Conductor
When the E fields are parallel to the conductor or conducting medium, the electrical energy is absorbed by the medium thus acting like a short

## Slide 20: Refraction
Occurs when the waves pass from one medium to another whose densities are different
Coefficient of reflection is less than 1
The angle of incidence and the angle of refraction is related by Snell’s Law

## Slide 21: Diffraction
Waves traveling in straight lines bend around obstacles
Based on Huygen’s principle (1690)
  Each point on a wavefront can be thought of as an isotropic point or a source of secondary spherical energy
Concepts explains why radio waves can be heard behind tall mountains or buildings that are normally considered to block line of sight transmissions

## Slide 22: Ground and Space Waves

## Slide 23: Ground Waves
Radio wave that travels along the earth’s surface (surface wave)
Vertically polarized
Changes in terrain have strong effect
Attenuation directly related to surface impedances
  More conductive the more attenuated
  Better over water

## Slide 24
Attenuation related to frequency
  Loses increase with increase in frequency
  Not very effective at frequencies above 2Mhz
  Very reliable communication link
  Reception is not affected by daily or seasonal weather changes

## Slide 25
Used to communicate with submarines
ELF (30 to 300 Hz) propagation is utilized

## Slide 26: FIGURE 12-6 Direct and ground reflected space waves.
Gary M. Miller, Jeffrey S. Beasley Modern Electronic Communication, 7e
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.

## Slide 27: Space Wave
Two types
  Direct
  Ground reflected

## Slide 28: Direct
Limited to “line-of sight” transmission distances
Antenna height and curvature of earth are limiting factors
Radio horizon is about 80% greater than line of sight because of diffraction effects

## Slide 29: FIGURE 12-7 Radio horizon for direct space waves.
Gary M. Miller, Jeffrey S. Beasley Modern Electronic Communication, 7e
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.

## Slide 30: Reflected
Part of the signal from the transmitter is bounced off the ground and reflected back to the receiving antenna
Can cause problems if the phase between the direct wave and the reflected wave are not in phase
Detuning the antenna so that the reflected wave is too weak to receive

## Slide 31: Sky Waves

## Slide 32: FIGURE 12-9 Sky-wave propagation.
Gary M. Miller, Jeffrey S. Beasley Modern Electronic Communication, 7e
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.

## Slide 33
Radio waves radiated from the transmitting antenna in a direction toward the ionosphere
Long distance transmissions
Sky wave strike the ionosphere, is refracted back to ground, strike the ground, reflected back toward the ionosphere, etc until it reaches the receiving antenna
Skipping is he refraction and reflection of sky waves

## Slide 34: Atmospheric Phenomenon
Three layers:
  Troposphere: earth’s surface to about 6.5 mi
  Stratosphere: extends from the troposphere upwards for about 23 mi
  Ionosphere: extends from the stratosphere upwards for about 250mi
  Beyond this layer is free space

## Slide 35: FIGURE 12-10 Layers f the ionosphere.
Gary M. Miller, Jeffrey S. Beasley Modern Electronic Communication, 7e
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.

## Slide 36
Temperature in the stratosphere is believed to be fairly constant and is not subject to temperature changes or inversions and will not cause significant refractions
This is called an isothermal region

## Slide 37
The ionic density in the ionosphere varies from very dense at the border between the ionosphere and stratosphere to very low density as it approaches free space
The ions in the far reaches of the ionosphere are easily susceptible to the sun’s radiation with the susceptibility reducing as one approaches the stratosphere

## Slide 38: Ionosphere
Three layers
  D: low frequencies can be refracted but the high frequencies tend to pass on through
  E: signals as high as 20MHz can be refracted while higher ones pass through
  F: during the day light hours there are two layers:
    F1 and F2

## Slide 39
F: during the night hours the ionization layer is relatively constant and the higher frequencies can be refracted
During the night hours, the D and E layers virtually disappear and signals that would be refracted at lower levels now are refracted at higher levels.
This results in greater skip distances and better reception at greater distances than in the daytime hours.

## Slide 40: Ionosphere
The layers that form the ionosphere vary greatly in altitude, density, and thickness with the varying degrees of solar activity.
The upper portion of the F layer is most affected by sunspots or solar disturbances
There is a greater concentration of solar radiation during peak sunspot activity.
The greater radiation activity the more dense the F layer and the higher the F layer becomes and the greater the skip distance

## Slide 41: FIGURE 12-11 Relationship of frequency to refraction by the ionosphere.
Gary M. Miller, Jeffrey S. Beasley Modern Electronic Communication, 7e
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.

## Slide 42: FIGURE 12-12 Relationship of frequency to critical angle.
Gary M. Miller, Jeffrey S. Beasley Modern Electronic Communication, 7e
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.

## Slide 43: Solar Cycle
Every 11 years the sun undergoes a period of activity called the "solar maximum", followed by a period of quiet called the "solar minimum". During the solar maximum there are many sunspots, solar flares, and coronal mass ejections, all of which can affect communications and weather here on Earth.

## Slide 44
The Sun goes through a periodic rise and fall in activity which affects HF communications; solar cycles vary in length from 9 to 14 years. At solar minimum, only the lower frequencies of the HF band will be supported by the ionosphere, while at solar maximum the higher frequencies will successfully propagate, figure 1.4. This is because there is more radiation being emitted from the Sun at solar maximum, producing more electrons in the ionosphere which allows the use of higher frequencies.

## Slide 46
One way we track solar activity is by observing sunspots. Sunspots are relatively cool areas that appear as dark blemishes on the face of the sun. They are formed when magnetic field lines just below the sun's surface are twisted and poke though the solar photosphere. The twisted magnetic field above sunspots are sites where solar flares are observed to occur, and we are now beginning to understand the connection between solar flares and sunspots.

## Slide 47
During solar maximum there are many sunspots, and during solar minimum there are few. The plot at right shows the number of sunspots observed during the last two solar cycles. The last maximum occurred around 1989, and the next is predicted to fall in the year 2000. This plot is updated monthly. Click here for a plot of sunspot numbers from the year 1749 through the present.

## Slide 48: How Do Sunspots Affect Earth
The Earth is affected by both solar flares and sunspots. Solar flares emit high-speed particles which cause auroras, known in the northern hemisphere as Northern Lights. The image shown here is a real-time satellite image of the Earth's auroral region above the North Pole. From the ground auroras appear as shimmering curtains of red and green light in the sky.

## Slide 49
Particles from solar flares can also disrupt radio communication, and the radiation from the flares can give passengers in airplanes a dose of radiation equivalent to a medical X-ray. Sunspots may have a long-term connection with the Earth's climate. Scientists are currently debating whether ice ages on Earth are related to the Sun having fewer sunspots than usual.

## Slide 50: How Does HF Radio Work Over Long Distances?
An HF signal transmitted from the earth may travel some way through the ionosphere before being "bent" back down towards the ground. This occurs due to the interaction between the HF signal and electrically charged particles in the ionosphere. The signal can then "bounce" off the ground back into the ionosphere, return to the earth again, and so on. The distance a given HF signal will travel depends on the frequency, transmitter power, take-off angle relative to the ground and the state of the ionosphere through which it is travelling.

## Slide 51
For any given distance and time, there will be a certain range of HF frequencies that are most likely to provide successful communications; frequencies outside that range will work poorly or not at all. Simply increasing the power of an HF signal will not help if the frequency is too high for the distance required. Increasing the power may help if the frequency is too low, but using a higher, more suitable frequency is the best option. The highest frequency which may be used for reliable HF communications is known as the Maximum Usable Frequency (MUF).

## Slide 52: How Do Conditions Affecting the Use of HF Radio Vary Over Time?
Extreme Ultraviolet (EUV) radiation from the sun creates the ionosphere. The EUV radiation arises from the bright and hot regions which overlie sunspots (areas of strong magnetic fields on the sun's surface). As the sun progresses through its eleven year cycle of activity, the number and size of sunspots will vary, as will the level of EUV radiation. Changes to the ionosphere that result from this mean that conditions affecting the use of HF radio will also change over the solar cycle.

## Slide 53
At the low point of the solar cycle, only the lower frequency HF signals can be transmitted over a given distance. At the peak of the cycle, the higher frequencies in the HF band can be transmitted over the same distance. Other factors important in determining the range of usable HF frequencies include the seasons, the time of day and the relative locations of the transmit and receive points

## Slide 54: What Kind of Disturbances Can Degrade HF Communications?
Short-Wave Fadeouts - short lived (up to two hours) disturbances, in which solar flare activity results in the absorption of lower frequency HF signals. These will only affect signals passing through the daylight ionosphere

## Slide 55
Ionospheric Storms - large scale changes in the chemical composition of the ionosphere resulting in changes to the MUF. Decreased MUFs restrict the frequencies available for use over a given distance. Ionospheric storms normally last for one to two days.

## Slide 56: Terms
Critical Frequency:
  The highest frequency that will be returned to the earth when transmitted vertically under given ionospheric conditions
Critical Angle:
  The highest angle with respect to a vertical line at which a radio wave of a specified frequency can be propagated and still be returned to the earth from the ionosphere

## Slide 57
Maximum usable frequency (MUF)
  The highest frequency that is returned to the earth from the ionosphere between two specific points on earth
Optimum Working frequency:
  The frequency that provides for the most consistent communication path via sky waves

## Slide 58
Quiet Zone or Skip Zone:
  The space between the point where the ground wave is completely dissipated and the point where the first sky wave is received
Fading:
  Variations in signal strength that may occur at the receiver over a period of time.

## Slide 59
Tropospheric Scattering
  Signals are aimed at the troposphere rather than the ionosphere
  350 Mhz to 10GHz for paths up to 400 mi
  Received signal = 10-6 th of the transmitted power
  Fading a problem

## Slide 60: Satellite communicatons

## Slide 61: Terms
Synchronous orbit—when a satellite’s position remains fixed with respect to the earth’s rotation
Uplink—transmission of signals to the satellite
Downlink—receiving signals from a satellite
Transponder—electronic system on a satellite that performs reception, frequency translation, and retransmission of received signals

## Slide 62: Intelsat III
Uplinks at 5.93 to 6.42 GHz
Translates down to 3.7 to 4.2 GHz
Amplifies signals to 7 watts outout
Downlinks to earth
Frequency change prevents interference between the transmission and receiving

## Slide 63
Round trip distance—90000km
Transmission time—300ms
600ms delay in transoceanic telephone communication
Thus routing of international calls ensures that no more than a single satellite hop is utilized.
Special circuits minimize the echo

## Slide 64
Geosynchoronous orbit (GEO)—another name for synchronous orbit
Low earth orbit (LEO)
  Launch costs reduced
  Signal time delay reduced to 5 to 15 msec
  Not stationary—obit time is 90 minutes and visible to earth for 5 to 20 minutes per orbit

## Slide 65: LEO
Satellites are linked for real time communication
Subscriber connections between satellites must be passed from one to the other as the satellites pass over the horizon—somewhat like cellphone

## Slide 66: GPS Systems
Global Positioning System
  Provides pinpoint geographic location information
  Originally used by the government and law enforcement
  The satellites transmit position data signals and the receiver processes and computes the time to receive each one
  By using four or more satellites allows the receiver to determine exact latitude and longitude.

## Slide 67
Uses a constellation of 28 satellites orbiting earth at about 11,000 miles
Satellites complete an orbit every 12 hours
Satellites transmit two signals:
  Course acquisition signal on 1575.2 MHz
  Precision code on 1227.6 MHz and 1575.42 MHz

## Slide 68
Requires three satellites for latitude and longitude
Requires four satellites to include elevation
They measure the time it takes for the signals to travel from the satellite to the receiver.
Civillian GPS has accuracy of 10m

## Slide 69: FDMA
Frequency division multiplex access
Early GPS systems
Several channels
Earth station sends a signal requesting permission to transmit, a control signal responds with the available frequency to transmit on.

## Slide 70: TDMA
Time division multiplex access
Single satellite to service multiple earth stations simultaneously
All stations use the same carrier but transmit one or more traffic bursts in nonoverlapping time frames

## Slide 71: TDMA Advantages
Single carrier for the transponder to operate on
  Less subject to intermodulation problems
  Can operate at a higher power output with smaller range of frequencies
Achieve selectivity
  Simpler
  Less expensive
Suited to digital communications

## Slide 72: CDMA
Code division multiple access
Allows use of one carrier
Each station uses a different binary sequence to modulate the carrier
Control uses a correlator that separates and distributes the signals to appropriate downlink

## Slide 73: VSAT
Very small aperture terminal fixed satellite communication systems
Allow multiple inexpensive stations to be linked to a large central installation
Kmart has VSATs at over 2000 stores linked to a mainframe computer in Mi.
Allows them to
  Verify checks and credit cards
  Convey data such as inventory

## Slide 74
Dish is typically 1 m in diameter
Power is just 2 to 3 watts
Immune to optical fiber for another 20 years or until fiber replaces copper

## Slide 75: Chrysler
6000 dealerships
Assists in
  Repair
  Sales
  Delivery dates
  Inventory
    Spare parts
    autos

## Slide 76
Gary M. Miller, Jeffrey S. Beasley Modern Electronic Communication, 7e
Copyright ©2002 by Pearson Education, Inc. Upper Saddle River, New Jersey 07458 All rights reserved.

## Slide 77: MSAT
Ultrasmall aperture terminal mobile satellite systems
VSAT’s on Wheels
Large national trucking firms
Allows dispatching center to maintain continuous communication with each of its trucks

## Slide 78: Summary
Definitions:
  Electromagnetic waves
  Isotropic point source
  Wavefront
  Characteristic impedance of free space
Effect of environment on wave propagation
Explanation of ground and space wave propagation

## Slide 79
Description of ionospheric laers and their effects on sky wave propagation
Definitions
  Skipping
  Critical frequency
  Critical angle
  MUF

## Slide 80
Definitions:
  Skip zone
  Fading
  Tropospherice scatter
Description and use of Satellite communications
Descriptions:
  FDMA
  TDMA
  CDMA

## Slide 81
Description and use of
  VSAT
  MSAT
Study guide
On-line Quiz

## Slide 82: The end of this chapter!!