## Slide 1: Chapter Fifteen: Radio-Wave Propagation

## Slide 2: Introduction
Radio waves are one form of electromagnetic radiation
Electromagnetic radiation has a dual nature:
  In some cases, it behaves as waves
  In other cases, it behaves as particles (photons)
For radio frequencies the wave model is generally more appropriate
Electromagnetic waves can be generated by many means, but all them involve the movement of electrical charges

## Slide 3: Electromagnetic Spectrum

## Slide 4: Electromagnetic Waves
Electromagnetic transmissions move in space as Transverse waves
Waves are characterized by frequency and wavelength:

## Slide 5: Electric and Magnetic Fields
An electromagnetic wave propagating through space consists of electric and magnetic fields, perpendicular both to each other and to the direction of travel of the wave
The relationship between electric and magnetic field intensities is analogous to the relation between voltage and current in circuits
This relationship is expressed by:

## Slide 6: Power Density
Power density in space is the amount of power that flows through each square meter of a surface perpendicular to the direction of travel

## Slide 7: Plane and Spherical Waves
The simplest source of electromagnetic waves would be a point in space, with waves radiating equally in all directions. This is called an isotropic radiator
A wavefront that has a surface on which all the waves are the same phase would be a sphere

## Slide 8: Circular Polarization
The polarization of a plane wave is simply the direction of its electric field vector
The wave can rotate in either direction - it is called right-handed if it rotates clockwise

## Slide 9: Free-Space Propagation
Radio waves propagate through free space in a straight line with a velocity of the speed of light (300,000,000 m/s)
There is no loss of energy in free space, but there is attenuation due to the spreading of the waves

## Slide 10: Attenuation of Free Space
An isotropic radiator would produce spherical waves
The power density of an isotropic radiator is simply be the total power divided by the surface area of the sphere, according to the square-law:

## Slide 11: Transmitting Antenna Gain
In practical communication systems, it is important to know the signal strength at the receiver input
It depends on the transmitter power and the distance from the transmitter to the receiver, but also upon the transmitting and receiving antennas
Two important antenna characteristics are:
  Gain for the transmitting antenna
  Effective area for the receiving antenna
Antennas are said to have gain in those directions in which the most power is radiated

## Slide 12: Receiving Antenna Gain
A receiving antenna absorbs some of the energy from radio waves that pass it
A larger antenna receives more power than a smaller antenna (in relation to surface area)
Receiving antennas are considered to have gain just as transmitting antennas do
The power extracted from a receiving antenna is a function of its physical size and its gain

## Slide 13: Path Loss
Free-space attenuation is the ratio of received power to transmitted power
The decibel gain between transmitter and receiver is negative (loss) and the loss found this way is called free-space loss or path loss

## Slide 14: Reflection, Refraction, and Diffraction
These three properties are shared by light and radio waves
For both reflection and refraction, it is assumed that the surfaces involved are much larger than the wavelength; if not, diffraction will occur

## Slide 15: Reflection
Reflection of waves from a smooth surface (specular reflection) results in the angle of reflection being equal to the angle of incidence

## Slide 16: Other Types of Reflection
Corner reflector Parabolic reflector Diffuse Reflection

## Slide 17: Refraction
A transition from one medium to another results in the bending of radio waves, just as it does with light
Snell’s Law governs the behavior of electromagnetic waves being refracted:

## Slide 18: Diffraction
As a result of diffraction, electromagnetic waves can appear to “go around corners”
Diffraction is more apparent when the object has sharp edges, that is when the dimensions are small in comparison to the wavelength

## Slide 19: Ground-Wave Propagation
Most of the time, radio waves are not quite in free space
Terrestrial propagation modes include:
  Line-of-sight propagation
  Space-wave propagation
  Ground waves
  Sky waves

## Slide 20: Ionospheric Propagation
Long-range communication in the high-frequency band is possible because of refraction in a region of the upper atmosphere called the ionosphere
The ionosphere is divided into three regions known as the D, E, and F layers
Ionization is different at different heights above the earth and is affected by time of day and solar activity

## Slide 21: Line-of-Sight Propagation
Signals in the VHF and higher range are not usually returned to earth by the ionosphere
Most terrestrial communication at these frequencies uses direct radiation from the transmitter to the receiver
This type of propagation is referred to as space-wave, line-of-sight, or tropospheric propagation

## Slide 22: Propagation in a Mobile/Portable Environment
Multipath propagation creates interference for communication systems
Mobile environments are often so cluttered that the square-law attenuation of free space does not apply (for example, in a city with many buildings)

## Slide 23: Repeaters and Cellular Systems
Because mobile systems have relatively small antenna heights, systems must be in place to improve signal strength and reception capabilities
Mobile units make use of repeaters that are full-duplex and use resonant cavities called a duplexer
Cellular systems do not use the horizon as the limit of coverage
Antennas may still be mounted high, but the range is deliberately limited by using as low a transmitter power as is possible

## Slide 24: Control of Fading in Mobile Systems
Fading is a problem with mobile systems and increasing power and typical frequency diversity are not workable solutions to this problem
Spread-spectrum systems can correct fading through alternative frequency diversity systems such as CDMA
Using a rake receiver, a CDMA system can receive several data streams at once

## Slide 25: Other Propagation Modes
Tropospheric Scatter - makes use of the scattering of radio waves in the troposphere to propagate signals in the 250 MHz –5 GHz range

## Slide 26: Ducting
Under certain conditions, especially over water, a superrefractive layer can form in the troposphere and return signals to earth
The signals can then propagate over long distances by alternately reflecting from the earth and refracting from the superrefractive layer
A related condition involves a thin tropospheric layer with a high refractive index, so that a duct forms

## Slide 27: Examples of Ducting

## Slide 28: Meteor-Trail Propagation
Meteors are constantly entering the earth’s atmosphere and being destroyed
The meteors that enter the atmosphere leave behind an ionized trail that can be used for communication. It is not suitable for voice communication