## Slide 1: Amateur Radio Frequency Propagation
Presented by John Woika, W8JW

## Slide 2: Radio Waves, Propagation and Antennas
Doing things right.

## Slide 3: HF (3 MHz - 30 MHz) Propagation
<number>
It is the unpredictable nature of HF propagation that makes the HF bands so much fun.
Long distance communication (DX) is accomplished by the reflection of radio waves by the ionosphere, the upper layers of the atmosphere ionized by ultraviolet radiation from the sun.

## Slide 4: Ionospheric Protection
<number>
The ionosphere and magnetosphere protect us from harmful radiation from the sun.
Notes: <number>

## Slide 5: How the Ionosphere is Formed
<number>
Notes: <number>

## Slide 6: The Ionosphere
<number>
F2 Layer (Reflecting)
F1 Layer (Reflecting)
E Layer (Reflecting)
D Layer (Absorbing)
Notes: <number>

## Slide 8: Ionospheric Layers
HF Communications: D, E, F1, F2 layers
D layer (45-55 miles): Acts as an RF sponge with maximum absorption during daylight hours thus dictates the LUF
E layer (65-75 miles): Effective refraction only during daylight hours
F layer (90-250 miles: During daylight, there are two layers, F1 and F2
F1 is not an important propagation medium; the F2 region is the primary medium supporting HF communications (200 miles); F1 and F2 combine onto one layer at night

## Slide 9: Layers of the Ionosphere
<number>
D Layer, Absorbing, Disappears at night
E Layer, Reflecting, Disappears at night
F1 and F2 Layers, Reflecting, combine into a single F layer at night.
The reflective layers are responsible for sky wave propagation.
Notes: <number>

## Slide 10: Sporadic-E
<number>
There are two natural phenomena that can propagate VHF signals over long distances.
Sporadic E occurs when the E-layer reflects VHF signals!

## Slide 11: The Blessings of Sky Wave
The medium for most all amateur radio communication below 30 mhz
The ionosphere refracts the radio wave and returns it to earth
The maximum usable frequency (MUF) is a function of how highly ionized the F region is
The lowest usable frequency (LUF) is a function of obsorbtion, signal-to-noise ratio, power and transmission mode; Correlates with movement of the sun and peaks at noon

## Slide 12: Sky wave Propagation (Skip)
<number>
Over the horizon
communication is
possible by sky-
wave propagation,
bouncing signals
off the ionosphere.
Occurs mostly at HF frequencies (less than 30 MHz).

## Slide 13: HF Band Prediction Characteristics
80 & 40 mtrs – good bands for distant communication especially during sunspot minimum
30 mtrs – allows greater distances than 40 mtrs at night
20 mtrs – most popular long haul band during all phases of the sunspot cycle but closes down at night during winter and sunspot minimum
15 mtrs – during sunspot minimum few stations heard day or night
10 mtrs – with low absorption allows good communication with relatively low power during daytime

## Slide 14: Sunspots
<number>
Sunspots peak during 11-year cycles.
The higher the sunspot count, the more the atmosphere is ionized.
Thus, higher sunspot counts support a higher Maximum Usable Frequency (MUF).

## Slide 15: VHF/UHF Propagation
<number>
Generally line of sight
Can be blocked by and/or reflected off mountains and large buildings – even the Moon!
Temperature inversions in the troposphere can cause “ducting,” and a path will open briefly for 500 - 600 miles.
VHF/UHF will penetrate the Ionosphere, making these frequencies ideal for satellite, and Earth-Moon-Earth (EME) operations.

## Slide 16: Line of Sight Propagation
<number>
Worldwide
communications
by line of sight is
not possible due
to the curvature
of the Earth

## Slide 17: VHF/UHF Propagation
<number>
VHF/UHF signals
travel only in straight
lines. We call this
“line of sight”
propagation
Direct communications are not
possible because of the mountain

## Slide 18: How far can I talk with these radios?
<number>
There is never an exact answer for any radio. Many factors come into play!
  Geography
  Frequency
  Buildings
  Distance

## Slide 19: VHF & UHF
<number>
FM signals are subject to fading.
  Stronger signals trump weaker ones.
Line-of-Sight Propagation
  “Radio Horizon”
Signals are subject to multi-path distortion
  When signals hit objects, they can be refracted. Move the radio a bit and things might get better.
Mobile stations are subject to “picket fencing.”
  Rapid fluttering sound during a transmission.

## Slide 20: Antennas
The long and short of those magical wires

## Slide 21
<number>
All Forms and Shapes

## Slide 22: Rubber Duck
<number>
A “rubber duck” is the antenna you find on most HTs. They are not the ideal antenna, but they do serve a purpose when you need to access a repeater.

## Slide 23: Antennas and Feed lines
<number>
Antenna systems are resonant - that is, they respond best to a certain frequency.
For best operation, the transmitter, feed line and antenna must all be tuned to resonance - or something that looks like resonance.
The transmitting antenna induces a radio wave into the air. The radio wave travels to the receiving antenna, and induces a current in that antenna.

## Slide 24: The 1/2 Wave Dipole
<number>
Length of resonant dipole in feet =

## Slide 25: The Yagi (This one is for HF)
<number>
The Favorite
This antenna has 4 monoband Yagis on the same boom. 2 elements on 40 and 20, 3 elements on 15 and 4 on 10.

## Slide 26: The Yagi
<number>
Gain
Boom
Feedline
Reflector
Director
Driver
The reflector
acts like a
mirror
The director
acts like a
lens

## Slide 27: The Yagi
<number>
The yagi antenna
focuses RF energy in
one direction, giving
the appearance of
getting “free power.”
This free power is
called Antenna Gain.

## Slide 28
<number>
T9A08
What type of antennas are the quad, Yagi, and dish?
A. Antennas invented after 1985
B. Loop antennas
C. Directional or beam antennas
D. Antennas that are not permitted for amateur radio stations

## Slide 29: Let’s review the basics
The sun influences all radio communication beyond ground-wave or line of sight ranges
Conditions vary with the time of day, season, and latitude/ longitude
REFLECTION occurs at any boundary between materials with different dielectric constants
Radio waves may be reflected by buildings, trees, vehicles, the ground, water, ionized layers in the outer atmosphere, or different air masses having different temperatures and moisture content

## Slide 30: The Basics Continued
Some radio energy will be absorbed by the medium it passes through, some passes on through the material
REFRACTION is the bending of a wave as it passes through one medium into another
Bending occurs because the wave is at a different speed in the new material
Amount of bending increases at higher frequencies
Speed of waves through the atmosphere change as the temperature, air density and levels of ionization are different
Most HF bands depend upon refraction

## Slide 31: Refraction
If waves were not bent:

## Slide 32: The Ionosphere
Affects frequencies below 30 mhz
30-260 miles above the earth’s surface
Contains free ions and electrons
Ionization depends on ultraviolet radiation from the sun
Skip distances depend upon frequency used, time of day, and density of the ionosphere
Several layers of varying distances at various heights

## Slide 33: Ionospheric Layers
HF Communications: D, E, F1, F2 layers
D layer (45-55 miles): Acts as an RF sponge with maximum absorption during daylight hours thus dictates the LUF
E layer (65-75 miles): Effective refraction only during daylight hours
F layer (90-250 miles: During daylight, there are two layers, F1 and F2
F1 is not an important propagation medium; the F2 region is the primary medium supporting HF communications (200 miles); F1 and F2 combine onto one layer at night

## Slide 34: Types of Propagation
Ionospheric waves (sky waves): Main portion of the radiation that leaves the antenna at angles above the horizon
Tropospheric waves: Radiation kept close to the earth’s surface due to bending in the lower atmosphere (higher HF or lower VHF)
Ground waves (surface waves): Radiation directly affected by the earth’s surface
- Earth-guided surface wave
- Vertically polarized and absorbtion increases with freq
- Travels much further over water than over land

## Slide 35: The Main Inhibitor: Solar Cycles
Sunspot cycles average 10.7 years in length
At solar maxima, the ionosphere is capable of refracting radio signals up to 40 mhz or higher
At solar minimum, refraction is reduced and frequencies above 20 mhz become unreliable
We are currently in the downward slope of cycle 23

## Slide 36: 100 Year Solar Cycles

## Slide 37: Propagation Information Websites
ARRL propagation page: http://www.arrl.org/tis/info/propagation.html
NOAA propagation report: http://www.sec.noaa.gov
QRZ Solar Report: www.qrz.com
Eham Propagation: www.eham.net
DX Summit: oh2aq.kolumbus.com/dxs/
Solar Terrestrial Activity Report: http://www.dxlc.com/solar

## Slide 38: Questions?
<number>