## Slide 1: Wireless LANs (WLANs)
Chapter 5 Updated January 2009
Raymond Panko’s Business Data Networks and Telecommunications, 7th edition May only be used by adopters of the book
Notes: <number>

## Slide 2: Orientation
5-<number>
LANs Are Governed by Layer 1 and 2 Standards
  So they are governed by OSI Standards
Chapter 3 (Layer 1 Transmission)
Chapter 4
  Ethernet 802.3 standards are OSI standards
Chapter 5
  Wireless 802.11 LAN (WLAN) standards are OSI standards
  But not all wireless technologies are OSI standards
  Operation, security, and management
  Bluetooth and other wireless options
Notes: <number>

## Slide 3: Basic 802.11 WLAN Operation
Notes: <number>

## Slide 4: 5-1/5-2: 802.11 Wireless LANs (WLANs)
5-<number>
Wireless LAN Technology
  802.11 is the dominant WLAN technology today
  Standardized by the 802.11 Working Group
  Popularly known as Wi-Fi
Notes: <number>

## Slide 5: 5-1/5-2: 802.11 Wireless LANs (WLANs)
5-<number>
Wireless hosts connect
by radio to access points
Notes: <number>

## Slide 6: 5-3: 802.11 Wireless Access Points and NICs
5-<number>
Notes: <number>

## Slide 7: 5-1/5-2: 802.11 Wireless LANs (WLANs)
5-<number>
WLANs usually supplement wired LANs
instead of replacing them.
The access point connects wireless users
to the firm’s main wired LAN (Ethernet)
This gives the mobile client user access to
the firm’s servers on the wired LAN and
the firm’s router for Internet access
1
Notes: <number>

## Slide 8: 5-1/5-2: 802.11 Wireless LANs (WLANs)
5-<number>
Companies can build large WLANs by placing
access points judiciously around the building
Notes: <number>

## Slide 9: 5-1/5-2: 802.11 Wireless LANs (WLANs)
5-<number>
Transmission speed: up to 300 Mbps but usually 10 Mbps to 100 Mbps.
Distances between station and access point: 30 to 100 meters.
Notes: <number>

## Slide 10: Wireless Transmission Concepts
Notes: <number>

## Slide 11: 5-4: Recap of Radio Propagation Concepts
5-<number>
Frequency
  Radio waves are measured in terms of frequency
  Measured in hertz (Hz)—the number of complete cycles per second
Most Common Frequency Range for WLANs:
  High megahertz to low gigahertz range
Notes: <number>

## Slide 12: 5-4: Recap of Radio Propagation Concepts from Chapter 3
5-<number>
Propagation Problems
  Electromagnetic interference
  Rapid inverse-square law attenuation
  Absorptive attenuation
  Shadow zones (dead spots)
  Multipath interference
As Frequency Increases
  Greater attenuation through absorptive attenuation
  Deader shadow zones
Notes: <number>

## Slide 13: 5-5: The Frequency Spectrum, Service Bands, and Channels
5-<number>
Notes: <number>

## Slide 14: 5-6: Channel Bandwidth and Speed
5-<number>
Signal Bandwidth
  Chapter 3 showed a wave operating at a single frequency
  Real signals spread over a range of frequencies
  As speed increases, the signal spreads more
Notes: <number>

## Slide 15: 5-6: Channel Bandwidth and Speed
5-<number>
Channel Bandwidth
  Channel bandwidth is the highest frequency in a channel minus the lowest frequency
  An 88.0 MHz to 88.2 MHz channel has a bandwidth of 0.2 MHz (200 kHz)
Notes: <number>

## Slide 16: 5-6: Channel Bandwidth and Speed
5-<number>
Shannon Equation
  C = B [Log2 (1+S/N)]
    C = Maximum possible transmission speed in the channel (bps)
    B = Bandwidth (Hz)
    S/N = Signal-to-noise ratio measured as the simple ratio of signal power to noise power, not as decibels
Notes: <number>

## Slide 17: 5-6: Channel Bandwidth and Speed
5-<number>
Shannon Equation
  Note that doubling the bandwidth doubles the maximum possible transmission speed
  Multiplying the bandwidth by X multiplies the maximum possible speed by X
  Wide bandwidth is the key to fast transmission
  Increasing S/N helps slightly, but usually cannot be done to any significant extent
Notes: <number>

## Slide 18: 5-6: Channel Bandwidth Speed
5-<number>
Broadband and Narrowband Channels
  Broadband means wide channel bandwidth and therefore high speed
  Narrowband means narrow channel bandwidth and therefore low speed
  Today, any speed, whether in channels or not, is called narrowband or broadband
    Narrowband is below 200 kbps
    Broadband is above 200 kbps
Notes: <number>

## Slide 19: 5-6: Channel Bandwidth and Speed
5-<number>
The Golden Zone
  Most organizational radio technologies operate in the golden zone in the high megahertz to low gigahertz range
  Golden zone frequencies are high enough for there to be large total bandwidth
  Golden zone frequencies are low enough to allow fairly good propagation characteristics
  Growing demand creates intense competition for frequencies in the Golden Zone
Notes: <number>

## Slide 20: 5-6: Channel Bandwidth and Speed
5-<number>
Channel Bandwidth and Spectrum Scarcity
  Why not make all channels broadband?
  There is a limited amount of spectrum at desirable frequencies
  Making each channel broader than needed would mean having fewer channels or widening the service band
  Service band design requires tradeoffs between speed requirements, channel bandwidth, and service band size
Notes: <number>

## Slide 21: Licensed and Unlicensed Bands and Spread Spectrum Transmission
Notes: <number>

## Slide 22: 5-8: Licensed and Unlicensed Bands
5-<number>
Licensed Radio Bands
  If two nearby radio hosts transmit in the same channel, their signals will interfere
  Most radio bands are licensed bands, in which hosts need a license to transmit
  The government limits licenses to avoid interference
  Television bands, AM radio bands, etc., are licensed
  In cellular telephone bands, which are licensed, only the central transceivers are licensed, not the mobile phones
Notes: <number>

## Slide 23: 5-8: Licensed and Unlicensed Bands
5-<number>
Unlicensed Radio Bands
  Some service bands are set aside as unlicensed bands
  Hosts do not need to be licensed to be turned on or moved
  802.11 operates in unlicensed radio bands
  This allows access points and hosts to be moved freely
Notes: <number>

## Slide 24: 5-8: Licensed and Unlicensed Bands
5-<number>
Unlicensed Radio Bands
  However, there is no way to stop interference from other nearby users
  Your only recourse is to negotiate with others
  At the same time, you must not cause unreasonable interference—for instance, by transmitting beyond legal power limits
Notes: <number>

## Slide 25: 5-9: 802.11 in the 2.4 GHz and 5 GHz Unlicensed Bands
5-<number>
The 2.4 GHz Unlicensed Band
  Defined the same in almost all countries (2.400 GHz to 2.485 GHz)
  This sameness reduces radio costs
  Propagation characteristics are good
  For 20 MHz 802.11 channels, only three nonoverlapping channels are possible
    Channels 1, 6, and 11
Notes: <number>

## Slide 26: 5-9: 802.11 in the 2.4 GHz and 5 GHz Unlicensed Bands
5-<number>
The 2.4 GHz Unlicensed Band
  There will be mutual channel interference between nearby access points transmitting in the same 20 MHz channel
  With only 3 channels, it is difficult or impossible to put nearby access points on different channels in you have many that are near each other
  Also, potential interference problems from microwave ovens, cordless telephones, etc.
Notes: <number>

## Slide 27: 5-10: Mutual Interference in the 2.4 GHz Unlicensed Band
5-<number>
If two nearby access points operate on the same channel,
the access points and their stations will interfere with each other
Notes: <number>

## Slide 28: 5-9: 802.11 in the 2.4 GHz and 5 GHz Unlicensed Bands
5-<number>
The 5 GHz Unlicensed Band
  Radios in the 5 GHz band are expensive because frequencies in different countries are different and because higher-frequency technology is more expensive than lower-frequency technology
  Also, smaller market sales mean more expensive devices
  Shorter propagation distance than in the 2.4 GHz band because of greater absorptive attenuation at higher frequencies
  Deader shadow zones because of higher frequencies
Notes: <number>

## Slide 29: 5-9: 802.11 in the 2.4 GHz and 5 GHz Unlicensed Bands
5-<number>
The 5 GHz Unlicensed Band
  More bandwidth than in the 2.4 GHz band, so between 11 and 24 non-overlapping channels
  Allows many nearby access points to operate on non-overlapping channels
  Or, some access points can operate on two channels
    They serve some clients with one channel, some with the other
    This allows them to serve more clients with good throughput
Notes: <number>

## Slide 30: 5-11: Spread Spectrum Transmission
5-<number>
Spread Spectrum Transmission
  You are required by law to use spread spectrum transmission in unlicensed bands
  Spread spectrum transmission reduces propagation problems
    Especially multipath interference
  Spread spectrum transmission is NOT used for security in WLANs
    Although the military does use spread spectrum transmission to make signals hard to detect
    This requires a different spread spectrum technology
Notes: <number>

## Slide 31: 5-12: Normal and Spread Spectrum Transmission
5-<number>
Notes: <number>

## Slide 32: 5-13: Spread Spectrum Transmission Methods
5-<number>
Early spread spectrum products used one of two slow methods.
In frequency hopping spread spectrum, the signal was kept narrow,
but it hopped around in frequency every two or three frames.
In direct sequence spread spectrum, the signal is spread over
The entire spread spectrum band.
Both have technical limits and all newer 802.11 standards
use a different type of spread spectrum transmission.
Notes: <number>

## Slide 33: 5-13: Spread Spectrum Transmission Methods
5-<number>
Newer 802.11 standards use OFDM:
Orthogonal Frequency Division Multiplexing.
OFDM divides the entire channel into smaller subcarriers (subchannels).
It sends part of the signal in each subcarrier.
Information is sent redundantly among the subcarriers, so the whole message will get through even if some subcarriers are bad
Using smaller channels gives more precise signal spreading
than spreading the signal over the entire channel.
This in turn allows much faster transmission speeds.
Notes: <number>

## Slide 34: Typical Access Point Operation
Notes: <number>

## Slide 35: 5-14: Typical 802.11 Wireless LAN Operation with Wireless Access Points
5-<number>
802.11 and 802.3 have different frames
1. The access point receives an 802.11
frame carrying the packet
2. The access point removes the packet,
places the packet into an 802.3 frame
and passes the frame on
The access point does NOT forward
The 802.3 frame or convert the frame
Notes: <number>

## Slide 36: 5-15: Hosts and Access Points Transmit in a Single Channel
5-<number>
5-<number>
The access point and all the hosts it serves
transmit in a single channel
If two devices transmit at the same time,
their signals will collide, becoming unreadable
Media access control (MAC) methods
govern when a device may transmit;
It only lets one device transmit at a time
Notes: <number>

## Slide 37: 5-16: CSMA/CA+ACK in 802.11 Wireless LANs
5-<number>
CSMA/CA (Carrier Sense Multiple Access with Collision Avoidance)
  Sender listens for traffic
    1. If there is traffic, the sender waits
    2. If there is no traffic:
      2a. If there has been no traffic for less than a present amount of time, waits a random amount of time, then returns to Step 1.
      2b, If there has been no traffic for more than a preset amount of time, sends without waiting
      This avoids collision that would result if hosts could transmit as soon as one host finishes transmitting
Box
Notes: <number>

## Slide 38: 5-16: CSMA/CA+ACK in 802.11 Wireless LANs
5-<number>
ACK (Acknowledgement)
  Receiver immediately sends back an acknowledgement
    If sender does not receive the acknowledgement, retransmits using CSMA
  CSMA/CA plus ACK is a reliable protocol
    CSMA/CA+ACK must be reliable because radio transmission is unreliable
Box
Notes: <number>

## Slide 39: 5-17: Request to Send/Clear to Send
5-<number>
Box
Notes: <number>

## Slide 40: Main 802.11 Standards
Notes: <number>

## Slide 41: 5-18: Specific 802.11 Wireless LAN Standards
5-<number>
Characteristic | 802.11 | 802.11a | 802.11b | 802.11g | 802.11g with 802.11b | 802.11n
Spread Spectrum Method, etc. | FHSS | OFDM | DSSS | OFDM | OFDM and DSSS | OFDM + MIMO
Unlicensed Band | 2.4 GHz | 5 GHz | 2.4 GHz | 2.4 GHz | 2.4 GHz | 2.4 GHz and 5 GHz
Remarks | Dead and gone | Little market accep-tance | Bloomed briefly | Today’s dominant 802.11 standard | Get rid of old 802.11b equipment | Both greater speeds and distances
Notes: <number>

## Slide 42: 5-18: Specific 802.11 Wireless LAN Standards
5-<number>
Characteristic | 802.11 | 802.11a | 802.11b | 802.11g | 802.11g with 802.11b | 802.11n
Rated Speed | 2 Mbps | 54 Mbps | 11 Mbps | 54 Mbps | Not Speci-fied | 100 Mbps to 300 Mbps
Actual Throughput, 3 m | 1 Mbps | 25 Mbps | 6 Mbps | 25 Mbps | 12 Mbps | Closer to rated speed than earlier standards
Actual Throughput, 30 m | ? | 12 Mbps | 6 Mbps | 20 Mbps | 11 Mbps | High at longer distances
Notes: <number>

## Slide 43: 5-18: Specific 802.11 Wireless LAN Standards
5-<number>
Characteristic | 802.11 | 802.11a | 802.11b | 802.11g | 802.11g with 802.11b* | 802.11n
Is throughput shared by all stations using an access point? | Yes | Yes | Yes | Yes | Yes | Yes
By definition, throughput is shared by all stations
that are transmitting in a single channel.
Notes: <number>

## Slide 44: 5-18: Specific 802.11 Wireless LAN Standards
5-<number>
802.11g
  Most popular 802.11 standard today
  54 Mbps rated speed with much slower throughput
  Generally sufficient for Web browsing
  Inexpensive
  All access points support it
Notes: <number>

## Slide 45: 5-19: Multiple Input/Multiple Output (MIMO) Transmission
5-<number>
Notes: <number>

## Slide 46: 5-18: Specific 802.11 Wireless LAN Standards
5-<number>
802.11n
  Uses MIMO to give higher throughputs and longer transmission distances
  Also uses 40 MHz channels instead of normal 20 MHz 802.11 channels to further increase throughput
  100 Mbps throughputs are common
  A bit of overkill for most users
  Today, the standard is still in draft, so devices bought today may not be upgradeable or may be upgradeable only with more effort than most users will want to make
Notes: <number>

## Slide 47: 5-20: Mesh Wireless Network
5-<number>
In mesh wireless networks, the access points do all routing
There is no need for a wired network
The 802.11s standard for mesh networking is under development
Notes: <number>

## Slide 48: Figure 5-21: Smart Antenna
5-<number>
Notes: <number>

## Slide 49: 802.11 Security
Notes: <number>

## Slide 50: 5-22: WLAN Security Threats
5-<number>
Drive-By Hackers
  Sit outside the corporate premises and read network traffic
  Can send malicious traffic into the network
  Easily done with readily available downloadable software
War Drivers
  Merely discover unprotected access points—become drive-by hackers only if they break in
Notes: <number>

## Slide 51: 5-24: 802.11 Core Security Standards
5-<number>
Provide Security between the Wireless Station and the Wireless Access Point
  Client (and perhaps access point) authentication
  Passes key to client
  Subsequent encryption of messages for confidentiality
Authentication
Protected
Communication
Notes: <number>

## Slide 52: 5-24: 802.11 Core Security Standards
5-<number>
Protection Does Not Extend Beyond Access Point
  Only protects the wireless client—access point connection
Protected
Communication
No Protection
Notes: <number>

## Slide 53: 5-24: 802.11 Core Security Standards
5-<number>
Wired Equivalent Privacy (WEP)
  Initial rudimentary core security provided with 802.11 in 1997
  Everyone shared the same secret encryption key, and this key could not be changed automatically
  Because secret key was shared, it does not seem to be secret
    Users often give out freely
  Key initially could be cracked in 1–2 hours; now can be cracked in 3–10 minutes using readily available software
Notes: <number>

## Slide 54: 5-24: 802.11 Core Security Standards
5-<number>
Wireless Protected Access (WPA)
  The Wi-Fi Alliance
    Normally certifies interoperability of 802.11 equipment
      Certified products get to use the Wi-Fi logo
    Created WPA as a stop-gap core security standard in 2002 until 802.11i was finished
Notes: <number>

## Slide 55: 5-24: 802.11 Core Security Standards
5-<number>
Wireless Protected Access (WPA)
  Designed for upgrading old equipment
    WPA uses a subset of 802.11i that can run on older wireless NICs and access points
    WPA added simpler security algorithms for functions that could not run on older machines
  Equipment that cannot be upgraded to WPA should be discarded
  Since the book went to press, part of WPA has been cracked
New
Notes: <number>

## Slide 56: 5-24: 802.11 Core Security Standards
5-<number>
802.11i (WPA2)
  Uses AES-CCMP with 128-bit keys for confidentiality and key management
  Gold standard in 802.11 core security
  But companies have large installed bases of WPA-configured equipment
  Now that WPA has been partially cracked, companies should upgrade to 802.11i
New
Notes: <number>

## Slide 57: 5-25: 802.11 Security in 802.1X and PSK Modes
802.1X Mode (See Figure 5-26)
  Uses a central authentication server for consistency
  Wi-Fi Alliance calls this enterprise mode
  Both WPA and 802.11i use 802.1X mode
5-<number>
Notes: <number>

## Slide 58: 5-25: 802.11 Security in 802.1X and PSK Modes
802.1X Mode (See Figure 5-26)
  For UTP connections, 802.1X provides no protection between the supplicant and the network access server
  OK because UTP is difficult to tap
5-<number>
Notes: <number>

## Slide 59: 5-25: 802.11 Security in 802.1X and PSK Modes
802.1X Mode (See Figure 5-26)
  However, with wireless transmission, protection is needed between the wireless supplicant and the access point because radio transmissions are easy to tap
5-<number>
Notes: <number>

## Slide 60: 5-25: 802.11 Security in 802.1X and PSK Modes
5-<number>
802.1X Mode (See Figure 5-26)
  Extended versions of EAP provide this protection
  There are several—PEAP, EAP-TLS, etc.
Notes: <number>

## Slide 61: 5-25: 802.11 Security in 802.1X and PSK Modes
5-<number>
Pre-Shared Key (PSK) Mode: Stations Share a Key with the Access Point
  For networks with a single access point
  Access point does all authentication and key management
  All users must know an initial pre-shared key (PSK)
  Each, however, is later given a unique key
PSK
PSK
Unique
Key
Unique
Key
Notes: <number>

## Slide 62: 5-25: 802.11 Security in 802.1X and PSK Modes
5-<number>
Pre-Shared Key (PSK) Mode: Stations Share a Key with the Access Point
  If the pre-shared key is weak, it is easily cracked
  Pass phrases that generate key must be at least 20 characters long
  Wi-Fi Alliance calls this personal mode
    This is a good name because it is designed for home use
Notes: <number>

## Slide 63: 5-25: 802.11 Security in 802.1X and PSK Modes
5-<number>
 | WPA | 802.11i (WPA2)
Can use 802.1X (Enterprise) Mode? | Yes | Yes
Can use PSK (Personal) Mode? | Yes | Yes
Notes: <number>

## Slide 64: 5-22: WLAN Security Threats
5-<number>
Rogue Access Points
  Unauthorized access points that are set up by a department or an individual
  They often fail to implement core security
  This gives drive-by hackers free access to the internal network, bypassing both the border firewall and access point security
  Often operate at high power, attracting many hosts to their low-security service
Notes: <number>

## Slide 65: 5-23: Evil Twin Access Point
5-<number>
An attacker makes his or her computer act as an access point.
It operates at very high power.
Victim wireless clients within the victim building
associate with the evil twin access point
instead of with a legitimate access point within the building.
Notes: <number>

## Slide 66: 5-23: Evil Twin Access Point
5-<number>
1. The victim sends its authentication credentials to the evil twin.
2. The evil twin passes the credentials on to the legitimate access point.
3. The legitimate access point sends back a secret key.
4. The evil twin remembers the key, then sends it to the client.
Notes: <number>

## Slide 67: 5-23: Evil Twin Access Point
5-<number>
Afterwards, the Evil Twin intercepts each encrypted message
It decrypts it, reads it, and reencrypts it, and passes it on.
Notes: <number>

## Slide 68: 5-23: Evil Twin Access Point
5-<number>
The Evil Twin can also generate messages on its own
These can be attack messages against internal hosts
These attacks bypass the main border firewall
Notes: <number>

## Slide 69: Figure 5-27: Added Wireless Protection: VPNs and VLANs
5-<number>
Virtual Private Networks (VPNs)
  Provides end-to-end protection from the client all the way to the server on the wired LAN
EAP Protected
Communication
VPN Protection
Preshared
VPN
Key
Preshared
VPN
Key
Notes: <number>

## Slide 70: Figure 5-27: Added Wireless Protection: VPNs and VLANs
5-<number>
Virtual Private Networks (VPNs)
  VPN protection defeats evil twins because the two devices preshared a key that is never transmitted
EAP Protected
Communication
VPN Protection
Preshared
VPN
Key
Preshared
VPN
Key
Frustrated
Evil Twin
Notes: <number>

## Slide 71: 5-27: Added Wireless Protection: VPNs and VLANs
5-<number>
Virtual Private Networks (VPNs)
  VPNs are somewhat expensive to implement
  Of greatest importance in high-threat environments, like public hot spots, where evil twin access points are common
Notes: <number>

## Slide 72: 5-27: Added Wireless Protection: VPNs and VLANs
5-<number>
Virtual LANs (VLANs) (Discussed in Chapter 4)
  With VLANs, clients can only talk to some servers
  Wireless clients who first come can be assigned to a VLAN in which they can only connect to a single server-an authentication server
  When the client authenticates itself to the authentication server, they are taken off the restrictive VLAN
Pre-
Authentication
VLAN
Rest of
the network
Authentication
Server
Notes: <number>

## Slide 73: Network Management
Notes: <number>

## Slide 74: 5-28: Wireless LAN Management
5-<number>
Initial Access Points Placement in a Building
  Must be done carefully to have good coverage yet to minimize interference between access points
  Lay out 30-meter to 50-meter radius circles on blueprints
  Adjust for obvious potential problems such as brick walls
  In multistory buildings, must consider interference in three dimensions
Notes: <number>

## Slide 75: 5-28: Wireless LAN Management
5-<number>
Access Points Placement in a Building
  Install access points and do site surveys to determine signal quality
  Adjust access point placement and signal strength as needed
  Adjust them frequently afterward as conditions change
  Adjust either their placements or relative signal powers
Notes: <number>

## Slide 76: Figure 5-29: Wireless Access Point Management Alternatives
5-<number>
A firm will have many access points.
Managing them can be very expensive.
Centralized management can greatly reduce costs.
Notes: <number>

## Slide 77: Figure 5-29: Wireless Access Point Management Alternatives
5-<number>
Smart access points can be managed directly.
However, the intelligence makes them expensive.
Notes: <number>

## Slide 78: Figure 5-29: Wireless Access Point Management Alternatives
5-<number>
Another approach is manageable WLAN switches.
The manager talks to the manageable WLAN switch.
Each manageable WLAN switch
serves several dumb access points.
This may be cheaper than smart access points.
Notes: <number>

## Slide 79: 5-28: Wireless LAN Management
5-<number>
Remote Access Point Management
  Desired functionality
    Notify the WLAN administrators of failures immediately
    Support remote access point adjustment
    Should provide continuous transmission quality monitoring
    Allow software updates to be pushed out to all access points or WLAN switches
    Work automatically whenever possible
Notes: <number>

## Slide 80: Other Local Wireless Technologies
Notes: <number>

## Slide 81: 5-30: Bluetooth Personal Area Networks (PANs)
5-<number>
For Personal Area Networks (PANs)
  Very-short-distance networks
  To connect devices on a person’s body and nearby (mobile phone, PDA, notebook computer, etc.)
  Devices around a desk (computer, mouse, keyboard, printer)
  The goal: cable elimination
  Standardized by the Bluetooth consortium
Notes: <number>

## Slide 82: 5-30: Bluetooth Personal Area Networks
5-<number>
Disadvantages Compared with 802.11
  Short distance (10 meters)
  Low speed (3 Mbps today with a slower reverse channel)
Notes: <number>

## Slide 83: Figure 5-30: Bluetooth Personal Area Networks
5-<number>
Advantages Compared to 802.11
  Low battery power drain, so long battery life between recharges
  Application profiles
    Define how devices will work together without configuration work
    Sending print jobs to printers
    File synchronization
    Etc.
    Somewhat rudimentary
    Devices typically only automate a few access profiles
Notes: <number>

## Slide 84: 5-30: Bluetooth Personal Area Networks
5-<number>
Bluetooth over Other Radio Options
  The idea: Run Bluetooth application radios over other radio standards
  Bluetooth over 802.11: Gives 802.11 speeds and distances
  Bluetooth over UWB (described later): 480 Mbps over 10 meters
Bluetooth Application Profile
Bluetooth
Transmission
802.11
Transmission
UWB
Transmission
Notes: <number>

## Slide 85: 5-31: Emerging Local Wireless Technologies
5-<number>
Ultrawideband (UWB)
  Uses channels that are several gigahertz wide
    Each UWB channel spans multiple frequency bands!
  Low power per hertz to avoid interference with other services
  Wide bandwidth gives very high speeds
  But limited to short distance
  Wireless USB provides 480 Mbps up to 3 meters, 110 Mbps up to 10 meters
Notes: <number>

## Slide 86: 5-31: Emerging Local Wireless Technologies
5-<number>
ZigBee for almost-always-off sensor networks
  Very low speeds (250 kbps maximum)
  Very long battery life
  At the other end of the performance spectrum from UWB
Notes: <number>

## Slide 87: 5-31: Emerging Local Wireless Technologies
5-<number>
RFID (Radio Frequency ID) Tags
  Like UPC tags but readable remotely
  In passive ID tags, the radio signal from the reader provides power for the RFID tag
    The RFID tag uses this power to transmit information about itself
  Active (battery-powered) RFID tags can send farther and send more information
Notes: <number>

## Slide 88: 5-31: Emerging Local Wireless Technologies
5-<number>
Software-Defined Radio
  Can implement multiple wireless protocols
  No need to have separate radio circuits for each protocol
  Reduces the cost of multi-protocol devices
Notes: <number>

## Slide 89: Topics Covered
Notes: <number>

## Slide 90: Wireless LANs
5-<number>
802.11 WLANs
  Access points connect wireless hosts to main corporate network for resources
  For large corporate WLANs by using many access points
  Dominates corporate WLANs
  Also called Wi-Fi
Notes: <number>

## Slide 91: Frequency Concepts
5-<number>
The Frequency Spectrum
  Service Bands
    Channels
Channel Bandwidth and Speed
  C = B Log2 (1+S/N)
802.11 in the 2.4 and 5 GHz Bands
  Unlicensed radio bands
  2.4 GHz band has better propagation
  5 GHz band has more channels to reduce interference between nearby access points
Notes: <number>

## Slide 92: Interference Between Access Points
5-<number>
Devices Operating in the Same Channel Must Take Turns
(Box) Media Access Control
  To allow only one device to act as a time
  CSMA/CA+ACK is the normal MAC standard
    Reliable protocol
  RTS/CTS
Notes: <number>

## Slide 93: 802.11 Standards
5-<number>
802.11g
  OFDM, 20 MHz channels
  Adequate speed and distance for most needs
  Less expensive
802.11n
  OFDM, MIMO, 40 MHz channels
  Faster speed and longer distance
  Expensive
  Many 802.11n draft products

## Slide 94: 802.11 Security Threats
5-<number>
Drive-By Hackers Versus War Drivers
Rogue Access Points
Evil Twin Access Points
  Create a man-in-the-middle attack
  Steal keys and so can decrypt all communication between the wireless host and the access point

## Slide 95: 802.11 Core Security
5-<number>
Between the Wireless Host and the Access Point
  Not beyond the access point
  WEP (obsolete, ineffective)
  WPA (good)
  802.11i (best)
Two Modes of Operation (Both WPA and 802.11i)
  802.1x with central authentication servers
  Pre-shared key
  Extended EAP protocols needed: PEAP, EAP-TLS, etc.

## Slide 96: Added 802.11 Security
5-<number>
Virtual Private Networks (VPNs)
  Core security only protects traffic between the wireless host and access points
  VPNs protect traffic all the way from the wireless host to the destination network or even the destination host
  Frustrate evil twin access point attacks
Virtual LANs (VLANs)
  Wireless hosts initially are on a VLAN that only connects them to an authentication server

## Slide 97: 802.11 WLAN Management
5-<number>
Access Point Placement
  Draw circles on blueprints
  Install access points and do a site survey
Remote Access Point Management
  To reduce labor costs
  Smart access points versus wireless switches
  Continuous monitoring
  Ability to make changes automatically

## Slide 98: Other Local Wireless Technologies
5-<number>
Bluetooth
  For personal area networks
  Wire replacement technology
  Application profiles to allow devices to work together automatically
  Now 3 Mbps; will be faster
Other Emerging Technologies
  UWB
  ZigBee
  RFIDs
  Software-defined radio

## Slide 99
5-<number>
All rights reserved. No part of this publication may be reproduced, stored in a retrieval system, or transmitted, in any form or by any means, electronic, mechanical, photocopying, recording, or otherwise, without the prior written permission of the publisher. Printed in the United States of America.
Copyright © 2009 Pearson Education, Inc.
Publishing as Prentice Hall