## Slide 5: Angle Modulation
Angle modulation includes both frequency and phase modulation.
FM is used for: radio broadcasting, sound signal in TV, two-way fixed and mobile radio systems, cellular telephone systems, and satellite communications.
PM is used extensively in data communications and for indirect FM.

## Slide 6: Comparison of FM or PM with AM
Advantages over AM:
better SNR, and more resistant to noise
efficient - class C amplifier can be used, and less power is required to angle modulate
capture effect reduces mutual interference
Disadvantages:
much wider bandwidth is required
slightly more complex circuitry is needed

## Slide 7: PLL FM Detector
PLL and quadrature detectors are commonly found in modern FM receivers.

Phase
Detector
LPF
Demodulated
output
VCO
FM IF
Signal

## Slide 8: Quadrature Detector
Both the quadrature and the PLL detector are conveniently found as IC packages.

## Slide 9: Radio-Wave Propagation
Radio waves, infrared, visible light, ultraviolet, X rays, and gamma rays are all different forms of electromagnetic radiation.
The waves propagate as transverse electromagnetic waves (TEM) - i.e. the electric field, the magnetic field, and the direction of travel of the waves are all mutually perpendicular.

## Slide 10: Transverse Electromagnetic Waves
x
y
z
Electric Field
Magnetic Field
Direction of Propagation

## Slide 11: Speed & Wavelength of em Waves
The speed of propagation  and the wavelength () of an electromagnetic wave are given, respectively, by:
where c = 3x108 m/s, r = medium’s relative permittivity
or dielectric constant, and f = frequency of wave in Hz.

## Slide 12: Reflection
Radio waves behave like light waves:
They reflect from a surface where the angle of incidence, i = the angle of reflection, r . To minimize reflective losses, the surface should be an ideal conductor and smooth.
Normal
Incident
Ray
Reflected
Ray
i
r
Conductor

## Slide 13: Refraction
Radio waves will bend or refract when they go from one medium with refractive index, n1 to another with refractive index, n2. The angles involved are given by :
1
2
n1<n2
where r = relative
permittivity of medium

## Slide 14: Diffraction
Diffraction is the phenomenon which results in radio waves that normally travel in a straight line to bend around an obstacle.
Direction of wave propagation
Obstacle

## Slide 15: Ground-Wave Propagation
At frequencies up to about 2 MHz, the most important method of propagation is by ground waves which are vertically polarized. They follow the curvature of the earth to propagate far beyond the horizon. Relatively high power is required.
Direction of wave travel
Increasing
Tilt
Earth

## Slide 16: Ionospheric Propagation
HF radio waves are returned from the F-layer of the ionosphere by a form of refraction.
The highest frequency that is returned to earth in the vertical direction is called the critical frequency, fc.
The highest frequency that returns to earth over a given path is called the maximum usable frequency (MUF). Because of the general instability of the ionosphere, the optimum working frequency (OWF) = 0.85 MUF, is used instead.

## Slide 17: Sky-Wave Propagation
From geometry (assuming flat earth):
d = 2hv tan i
From theory (secant law):
MUF = fc sec i
i
hv
d
F-Layer
Earth

## Slide 18: Sky-wave Propagation: Pros & Cons
Sky-wave propagation allows communication over great distances with simple equipment and reasonable power levels : 100 W to a few kW.
However, HF communication via the ionosphere is noisy and uncertain. It is also prone to phase shifting and frequency-selective fading. For instance, the phase shift and signal attenuation may be different for the upper and lower sidebands of the same signal. Data transmission is restricted to very low rates.

## Slide 19: Space-Wave Propagation
Most terrestrial communications in the VHF or higher frequency range use direct, line-of-sight, or tropospheric radio waves. The approximate maximum distance of communication is given by:
where d = max. distance in km
hT = height of the TX antenna in m
hR = height of the RX antenna in m

## Slide 20: Space-Wave Propagation (cont’d)
The radio horizon is greater than the optical horizon by about one third due to refraction of the atmosphere.
Reflections from a relatively smooth surface, such as a body of water, could result in partial cancellation of the direct signal - a phenomenon known as fading. Also, large objects, such as buildings and hills, could cause multipath distortion from many reflections.

## Slide 21: Optical Fibre Communications
Advantages over metallic/coaxial cable:
  much wider bandwidth and practically interference-free
  lower loss and light weight
  more resistive to environmental effects
  safer and easier to install
  almost impossible to tap into a fibre cable
  potentially lower in cost over the long term
Disadvantages:
  higher initial cost in installation & more expensive to repair/maintain

## Slide 22: Optical Fibre Link
Input
Signal
Coder or
Converter
Light
Source
Source-to-fibre
Interface
Fibre-to-light
Interface
Light
Detector
Amplifier/Shaper
Decoder
Output
Fibre-optic Cable
Transmitter
Receiver

## Slide 23: Types Of Optical Fibre
Single-mode step-index fibre
Multimode step-index fibre
Multimode graded-index fibre
n1 core
n2 cladding
no air
n2 cladding
n1 core
Variable
n
no air
Light
ray
Index porfile