## Slide 1: Chapter 3
Mobile Radio Propagation

## Slide 2: Outline
Speed, Wavelength, Frequency
Types of Waves
Radio Frequency Bands
Propagation Mechanisms
Radio Propagation Effects
Free-Space Propagation
Land Propagation
Path Loss
Fading: Slow Fading / Fast Fading
Delay Spread
Doppler Shift
Co-Channel Interference
The Near-Far Problem
Digital Wireless Communication System
Analog and Digital Signals
Modulation Techniques

## Slide 3: Speed, Wavelength, Frequency
System | Frequency | Wavelength
AC current | 60 Hz | 5,000 km
FM radio | 100 MHz | 3 m
Cellular | 800 MHz | 37.5 cm
Ka band satellite | 20 GHz | 15 mm
Ultraviolet light | 1015 Hz | 10-7 m
Light speed = Wavelength x Frequency
= 3 x 108 m/s = 300,000 km/s

## Slide 4: Types of Waves
Transmitter
Receiver
Earth
Sky wave
Space wave
Ground wave
Troposphere (0 - 12 km)
Stratosphere (12 - 50 km)
Mesosphere (50 - 80 km)
Ionosphere (80 - 720 km)

## Slide 5: Radio Frequency Bands
Classification Band | Initials | Frequency Range | Characteristics
Extremely low | ELF | < 300 Hz | Ground wave
Infra low | ILF | 300 Hz - 3 kHz | 
Very low | VLF | 3 kHz - 30 kHz | 
Low | LF | 30 kHz - 300 kHz | 
Medium | MF | 300 kHz - 3 MHz | Ground/Sky wave
High | HF | 3 MHz - 30 MHz | Sky wave
Very high | VHF | 30 MHz - 300 MHz | Space wave
Ultra high | UHF | 300 MHz - 3 GHz | 
Super high | SHF | 3 GHz - 30 GHz | 
Extremely high | EHF | 30 GHz - 300 GHz | 
Tremendously high | THF | 300 GHz - 3000 GHz | 

## Slide 6: Propagation Mechanisms
Reflection
  Propagation wave impinges on an object which is large as compared to wavelength
- e.g., the surface of the Earth, buildings, walls, etc.
Diffraction
  Radio path between transmitter and receiver obstructed by surface with sharp irregular edges
  Waves bend around the obstacle, even when LOS (line of sight) does not exist
Scattering
  Objects smaller than the wavelength of the propagation wave
- e.g. foliage, street signs, lamp posts

## Slide 7: Radio Propagation Effects
Transmitter
d
Receiver
hb
hm
Diffracted Signal
Reflected Signal
Direct Signal
Building

## Slide 8: Free-space Propagation
The received signal power at distance d:
where Pt is transmitting power, Ae is effective area, and Gt is the transmitting antenna gain. Assuming that the radiated power is uniformly distributed over the surface of the sphere.
Transmitter
Distance d
Receiver
hb
hm

## Slide 9: Antenna Gain
For a circular reflector antenna
Gain G =  (  D /  )2
 = net efficiency (depends on the electric field distribution over the antenna aperture, losses, ohmic heating , typically 0.55)
D = diameter
thus, G =  ( D f /c )2, c =  f (c is speed of light)
Example:
Antenna with diameter = 2 m, frequency = 6 GHz, wavelength = 0.05 m
G = 39.4 dB
Frequency = 14 GHz, same diameter, wavelength = 0.021 m
G = 46.9 dB
* Higher the frequency, higher the gain for the same size antenna

## Slide 10: Land Propagation
The received signal power:
where Gr is the receiver antenna gain,
L is the propagation loss in the channel, i.e.,
L = LP LS LF
Fast fading
Slow fading
Path loss

## Slide 11: Path Loss (Free-space)
Definition of path loss LP :
Path Loss in Free-space:
where fc is the carrier frequency.
This shows greater the fc , more is the loss.

## Slide 12: Path Loss (Land Propagation)
Simplest Formula:
        Lp = A d-α
where
A and α: propagation constants
d : distance between transmitter and receiver
α : value of 3 ~ 4 in typical urban area

## Slide 13: Example of Path Loss (Free-space)

## Slide 14: Path Loss (Urban, Suburban and Open areas)
Urban area:
where
Suburban area:
Open area:

## Slide 15: Path Loss
Path loss in decreasing order:
  Urban area (large city)
  Urban area (medium and small city)
  Suburban area
  Open area

## Slide 16: Example of Path Loss (Urban Area: Large City)

## Slide 17: Example of Path Loss (Urban Area: Medium and Small Cities)

## Slide 18: Example of Path Loss (Suburban Area)

## Slide 19: Example of Path Loss (Open Area)

## Slide 20: Fading
Signal Strength
(dB)
Distance
Path Loss
Slow Fading (Long-term fading)
Fast Fading (Short-term fading)

## Slide 21: Slow Fading
The long-term variation in the mean level is known as slow fading (shadowing or log-normal fading). This fading caused by shadowing.
Log-normal distribution:
- The pdf of the received signal level is given in decibels by
where M is the true received signal level m in decibels, i.e., 10log10m, M is the area average signal level, i.e., the mean of M,
 is the standard deviation in decibels

## Slide 22: Log-normal Distribution
M
M
2
p(M)
The pdf of the received signal level

## Slide 23: Fast Fading
The signal from the transmitter may be reflected from objects such as hills, buildings, or vehicles.
  When MS far from BS, the envelope distribution of received signal is Rayleigh distribution. The pdf is
where  is the standard deviation.
  Middle value rm of envelope signal within sample range to be satisfied by
  We have rm = 1.777

## Slide 24: Rayleigh Distribution
The pdf of the envelope variation
r
2
4
6
8
10
P(r)
0
0.2
0.4
0.6
0.8
1.0
=1
=2
=3

## Slide 25: Fast Fading (Continued)
When MS far from BS, the envelope distribution of received signal is Rician distribution. The pdf is
where
 is the standard deviation,
I0(x) is the zero-order Bessel function of the first kind,
 is the amplitude of the direct signal

## Slide 26: Rician Distribution
r
Pdf p(r)
 = 2
 = 1
= 0 (Rayleigh)
 = 1
 = 3
The pdf of the envelope variation

## Slide 27: Characteristics of Instantaneous Amplitude
Level Crossing Rate:
  Average number of times per second that the signal envelope crosses the level in positive going direction.
Fading Rate:
  Number of times signal envelope crosses middle value in positive going direction per unit time.
Depth of Fading:
  Ratio of mean square value and minimum value of fading signal.
Fading Duration:
  Time for which signal is below given threshold.

## Slide 28: Doppler Shift
Doppler Effect: When a wave source and a receiver are moving towards each other, the frequency of the received signal will not be the same as the source.
  When they are moving toward each other, the frequency of the received signal is higher than the source.
  When they are opposing each other, the frequency decreases.
Thus, the frequency of the received signal is
where fC is the frequency of source carrier,
fD is the Doppler frequency.
Doppler Shift in frequency:
where v is the moving speed,
 is the wavelength of carrier.
MS
Signal
Moving speed v


## Slide 29: Delay Spread
When a signal propagates from a transmitter to a receiver, signal suffers one or more reflections.
This forces signal to follow different paths.
Each path has different path length, so the time of arrival for each path is different.
This effect which spreads out the signal is called “Delay Spread”.

## Slide 30: Moving Speed Effect
Time
V1
V2
V3
V4
Signal strength

## Slide 31: Delay Spread
Delay
Signal Strength
The signals from close by reflectors
The signals from intermediate reflectors
The signals from far away reflectors

## Slide 32: Intersymbol Interference (ISI)
Caused by time delayed multipath signals
Has impact on burst error rate of channel
Second multipath is delayed and is received during next symbol
For low bit-error-rate (BER)
R (digital transmission rate) limited by delay spread d.

## Slide 33: Intersymbol Interference (ISI)
Time
Time
Time
Transmission signal
Received signal (short delay)
Received signal (long delay)
1
0
1
Propagation time
Delayed signals

## Slide 34: Coherence Bandwidth
Coherence bandwidth Bc:
  Represents correlation between 2 fading signal envelopes at frequencies f1 and f2.
  Is a function of delay spread.
  Two frequencies that are larger than coherence bandwidth fade independently.
  Concept useful in diversity reception
    Multiple copies of same message are sent using different frequencies.

## Slide 35: Cochannel Interference
Cells having the same frequency interfere with each other.
rd is the desired signal
ru is the interfering undesired signal
 is the protection ratio for which
rd  ru (so that the signals interfere the least)
If P(rd  ru ) is the probability that rd  ru ,
Cochannel probability Pco = P(rd  ru )