## Slide 1: Antennas and Propagation
Chapter 5

## Slide 2: Introduction
An antenna is an electrical conductor or system of conductors
  Transmission - radiates electromagnetic energy into space
  Reception - collects electromagnetic energy from space
In two-way communication, the same antenna can be used for transmission and reception

## Slide 3: Radiation Patterns
Radiation pattern
  Graphical representation of radiation properties of an antenna
  Depicted as two-dimensional cross section
Beam width (or half-power beam width)
  Measure of directivity of antenna
Reception pattern
  Receiving antenna’s equivalent to radiation pattern

## Slide 4: Types of Antennas
Isotropic antenna (idealized)
  Radiates power equally in all directions
Dipole antennas
  Half-wave dipole antenna (or Hertz antenna)
  Quarter-wave vertical antenna (or Marconi antenna)
Parabolic Reflective Antenna

## Slide 5: Antenna Gain
Antenna gain
  Power output, in a particular direction, compared to that produced in any direction by a perfect omnidirectional antenna (isotropic antenna)
Effective area
  Related to physical size and shape of antenna

## Slide 6: Antenna Gain
Relationship between antenna gain and effective area
    G = antenna gain
    Ae = effective area
    f = carrier frequency
    c = speed of light (» 3 ´ 108 m/s)
     = carrier wavelength

## Slide 7: Propagation Modes
Ground-wave propagation
Sky-wave propagation
Line-of-sight propagation

## Slide 8: Ground Wave Propagation

## Slide 9: Ground Wave Propagation
Follows contour of the earth
Can Propagate considerable distances
Frequencies up to 2 MHz
Example
  AM radio

## Slide 10: Sky Wave Propagation

## Slide 11: Sky Wave Propagation
Signal reflected from ionized layer of atmosphere back down to earth
Signal can travel a number of hops, back and forth between ionosphere and earth’s surface
Reflection effect caused by refraction
Examples
  Amateur radio
  CB radio

## Slide 12: Line-of-Sight Propagation

## Slide 13: Line-of-Sight Propagation
Transmitting and receiving antennas must be within line of sight
  Satellite communication – signal above 30 MHz not reflected by ionosphere
  Ground communication – antennas within effective line of site due to refraction
Refraction – bending of microwaves by the atmosphere
  Velocity of electromagnetic wave is a function of the density of the medium
  When wave changes medium, speed changes
  Wave bends at the boundary between mediums

## Slide 14: Line-of-Sight Equations
Optical line of sight
Effective, or radio, line of sight
    d = distance between antenna and horizon (km)
    h = antenna height (m)
    K = adjustment factor to account for refraction, rule of thumb K = 4/3

## Slide 15: Line-of-Sight Equations
Maximum distance between two antennas for LOS propagation:
    h1 = height of antenna one
    h2 = height of antenna two

## Slide 16: LOS Wireless Transmission Impairments
Attenuation and attenuation distortion
Free space loss
Noise
Atmospheric absorption
Multipath
Refraction
Thermal noise

## Slide 17: Attenuation
Strength of signal falls off with distance over transmission medium
Attenuation factors for unguided media:
  Received signal must have sufficient strength so that circuitry in the receiver can interpret the signal
  Signal must maintain a level sufficiently higher than noise to be received without error
  Attenuation is greater at higher frequencies, causing distortion

## Slide 18: Free Space Loss
Free space loss, ideal isotropic antenna
    Pt = signal power at transmitting antenna
    Pr = signal power at receiving antenna
     = carrier wavelength
    d = propagation distance between antennas
    c = speed of light (» 3 ´ 10 8 m/s)
    where d and  are in the same units (e.g., meters)

## Slide 19: Free Space Loss
Free space loss equation can be recast:

## Slide 20: Free Space Loss
Free space loss accounting for gain of other antennas
    Gt = gain of transmitting antenna
    Gr = gain of receiving antenna
    At = effective area of transmitting antenna
    Ar = effective area of receiving antenna

## Slide 21: Free Space Loss
Free space loss accounting for gain of other antennas can be recast as

## Slide 22: Categories of Noise
Thermal Noise
Intermodulation noise
Crosstalk
Impulse Noise

## Slide 23: Thermal Noise
Thermal noise due to agitation of electrons
Present in all electronic devices and transmission media
Cannot be eliminated
Function of temperature
Particularly significant for satellite communication

## Slide 24: Thermal Noise
Amount of thermal noise to be found in a bandwidth of 1Hz in any device or conductor is:
    N0 = noise power density in watts per 1 Hz of bandwidth
    k = Boltzmann's constant = 1.3803 ´ 10-23 J/K
    T = temperature, in kelvins (absolute temperature)

## Slide 25: Thermal Noise
Noise is assumed to be independent of frequency
Thermal noise present in a bandwidth of B Hertz (in watts):
    or, in decibel-watts

## Slide 26: Noise Terminology
Intermodulation noise – occurs if signals with different frequencies share the same medium
  Interference caused by a signal produced at a frequency that is the sum or difference of original frequencies
Crosstalk – unwanted coupling between signal paths
Impulse noise – irregular pulses or noise spikes
  Short duration and of relatively high amplitude
  Caused by external electromagnetic disturbances, or faults and flaws in the communications system

## Slide 27: Expression Eb/N0
Ratio of signal energy per bit to noise power density per Hertz
The bit error rate for digital data is a function of Eb/N0
  Given a value for Eb/N0 to achieve a desired error rate, parameters of this formula can be selected
  As bit rate R increases, transmitted signal power must increase to maintain required Eb/N0

## Slide 28: Other Impairments
Atmospheric absorption – water vapor and oxygen contribute to attenuation
Multipath – obstacles reflect signals so that multiple copies with varying delays are received
Refraction – bending of radio waves as they propagate through the atmosphere

## Slide 29: Multipath Propagation

## Slide 30: Multipath Propagation
Reflection - occurs when signal encounters a surface that is large relative to the wavelength of the signal
Diffraction - occurs at the edge of an impenetrable body that is large compared to wavelength of radio wave
Scattering – occurs when incoming signal hits an object whose size in the order of the wavelength of the signal or less

## Slide 31: The Effects of Multipath Propagation
Multiple copies of a signal may arrive at different phases
  If phases add destructively, the signal level relative to noise declines, making detection more difficult
Intersymbol interference (ISI)
  One or more delayed copies of a pulse may arrive at the same time as the primary pulse for a subsequent bit

## Slide 32: Types of Fading
Fast fading
Slow fading
Flat fading
Selective fading
Rayleigh fading
Rician fading

## Slide 33: Error Compensation Mechanisms
Forward error correction
Adaptive equalization
Diversity techniques

## Slide 34: Forward Error Correction
Transmitter adds error-correcting code to data block
  Code is a function of the data bits
Receiver calculates error-correcting code from incoming data bits
  If calculated code matches incoming code, no error occurred
  If error-correcting codes don’t match, receiver attempts to determine bits in error and correct

## Slide 35: Adaptive Equalization
Can be applied to transmissions that carry analog or digital information
  Analog voice or video
  Digital data, digitized voice or video
Used to combat intersymbol interference
Involves gathering dispersed symbol energy back into its original time interval
Techniques
  Lumped analog circuits
  Sophisticated digital signal processing algorithms

## Slide 36: Diversity Techniques
Diversity is based on the fact that individual channels experience independent fading events
Space diversity – techniques involving physical transmission path
Frequency diversity – techniques where the signal is spread out over a larger frequency bandwidth or carried on multiple frequency carriers
Time diversity – techniques aimed at spreading the data out over time