## Slide 1: Mobile Radio Propagation - Large Scale Path Loss
Asad Ali

## Slide 2: Introduction ..
Question:
What are reasons why wireless signals are hard to send and receive?

## Slide 3: Introduction to Radio Wave Propagation
The mobile radio channel places fundamental limitations on the performance of wireless communication systems
Paths can vary from simple line-of-sight to ones that are severely obstructed by buildings, mountains, and foliage
Radio channels are extremely random and difficult to analyze
The speed of motion also impacts how rapidly the signal level fades as a mobile terminals moves about.

## Slide 4: Problems Unique to Wireless systems
Interference from other service providers
Interference from other users (same network)
  CCI due to frequency reuse
  ACI due to Tx/Rx design limitations & large # users sharing finite BW
Shadowing
  Obstructions to line-of-sight paths cause areas of weak received signal strength

## Slide 5: Problems Unique to Wireless systems
Fading
  When no clear line-of-sight path exists, signals are received that are reflections off obstructions and diffractions around obstructions
  Multipath signals can be received that interfere with each other
  Fixed Wireless Channel → random & unpredictable
    must be characterized in a statistical fashion
    field measurements often needed to characterize radio channel performance

## Slide 6: Mechanisms that affect the radio propagation ..
Reflection
Diffraction
Scattering
In urban areas, there is no direct line-of-sight path between:
the transmitter and the receiver, and where the presence of high- rise buildings causes severe diffraction loss.
Multiple reflections cause multi-path fading

## Slide 7
Reflection, Diffraction, Scattering
Reflections arise when the plane waves are incident upon a surface with dimensions that are very large compared to the wavelength
Diffraction occurs according to Huygens's principle when there is an obstruction between the transmitter and receiver antennas, and secondary waves are generated behind the obstructing body
Scattering occurs when the plane waves are incident upon an object whose dimensions are on the order of a wavelength or less, and causes the energy to be redirected in many directions.

## Slide 8
Mobile Radio Propagation Environment
The relative importance of these three propagation mechanisms depends on the particular propagation scenario.
As a result of the above three mechanisms, macro cellular radio propagation can be roughly characterized by three nearly independent phenomenon;
  Path loss variation with distance (Large Scale Propagation )
  Slow log-normal shadowing (Medium Scale Propagation )
  Fast multipath fading. (Small Scale Propagation )
Each of these phenomenon is caused by a different underlying physical principle and each must be accounted for when designing and evaluating the performance of a cellular system.

## Slide 9
Transmission path between Tx and Rx
Line of Sight (LOS)
Non Line of Sight (NLOS)

## Slide 10
Radio Propagation Mechanisms
The physical mechanisms that govern radio propagation are complex and diverse
Generally attributed to the following four factors
  Direct Mode
  Reflection
  Diffraction
  Scattering.
They have an impact on the wave propagation in a mobile communication system
The most important parameter, “Received power” is predicted by Large Scale Propagation models based on the physics of reflection, diffraction and scattering

## Slide 11
Radio Propagation Mechanisms
Illustration ..
1
2
3
4
Line Of Sight (LOS)
Non Line Of Sight (NLOS)

## Slide 12
Line of Sight (LOS)
Line-of-sight is the direct propagation of radio waves between antennas that are visible to each other.
This is probably the most common of the radio propagation modes at VHF and higher frequencies.
Radio signals can travel through many non-metallic objects, radio can be picked up through walls. This is still line-of-sight propagation.
Examples would include propagation between a satellite and a ground antenna or reception of television signals from a local TV transmitter.

## Slide 13
Mobile Radio Propagation with respect to LOS
The received signal is directly received at the receiver the effects such as reflection, diffraction and scattering doesn’t affect the signal reception that much.

## Slide 14
Free Space Propagation Model
Free space propagation model is used to predict:
    Received Signal Strength when the transmitter and receiver have a clear, unobstructed LoS between them.
    The free space propagation model assumes a transmit antenna and a receive antenna to be located in an otherwise empty environment. Neither absorbing obstacles nor reflecting surfaces are considered. In particular, the influence of the earth surface is assumed to be entirely absent.
    Satellite communication systems and microwave line-of-sight radio links typically undergo free space propagation.

## Slide 15
Free Space Propagation Model
Path Loss
  Signal attenuation as a positive quantity measured in dB and defined as the difference (in dB) between the effective transmitter power and received power.
Friis is an application of the standard “Free Space Propagation Model “
  It gives the Median Path Loss in dB ( exclusive of Antenna Gains and other losses )

## Slide 16
Friis Transmission Equation (Far field)
clear, unobstructed line-of-sight path → satellite and fixed microwave
  Friis transmission formula → Rx power (Pr) vs. T-R separation (d)

## Slide 17
Friis Free Space Equation
Pt Transmitted power,
Pr(d) Received power
Gt Transmitter antenna gain,
Gr Receiver antenna gain,
d T-R separation distance
L System loss factor not related to propagation

## Slide 18
Friis Free Space Equation
λ = wavelength = c / f (m)
So, as frequency increases, what happens to the propagation characteristics?
L = system losses (antennas, transmission lines between equipment and antennas, atmosphere, etc.)
  L = 1 for zero loss
d = T-R separation distance (m)
Signal fades in proportion to d2

## Slide 19
Friis Free Space Equation
The ideal conditions assumed for this model are almost never achieved in ordinary terrestrial communications, due to obstructions, reflections from buildings, and most importantly reflections from the ground.
The Friis free space model is only a valid predictor for “Pr ” for values of “d” which are in the far-field of the “Transmitting antenna

## Slide 20
Free Space Propagation Model
Thus in practice, power can be measured at d0 and predicted at d using the relation

## Slide 21
Example 1
Find the far-field distance for an antenna with maximum dimension of 1 m and operating frequency of 900 MHz.

## Slide 22
Example 2
If a transmitter produces 50 watts of power, express the transmit power in units of (a) dBm, and (b) dBW. If 50 watts is applied to a unity gain antenna with a 900 MHz carrier frequency, find the received power in dBm at a free space distance of 100 m from the antenna, What is Pr (10 km)? Assume unity gain for the receiver antenna.

## Slide 23
Solution example 2

## Slide 24
Non Line of Sight (NLOS)
There are three basic propagation mechanisms in addition to line-of-sight paths
  Reflection - Waves bouncing off of objects of large dimensions
  Diffraction - Waves bending around sharp edges of objects
  Scattering - Waves traveling through a medium with small objects in it (foliage, street signs, lamp posts, etc.) or reflecting off rough surfaces

## Slide 25
NLOS
1
2
3
4
Line Of Sight (LOS)
Non Line Of Sight (NLOS)

## Slide 26
Reflections
Reflection occurs when RF energy is incident upon a boundary between two materials (e.g. air/ground) with different electrical characteristics
Example: reflections from earth and buildings
These reflections may interfere with the original signal constructively or destructively

## Slide 27
Reflections
Upon reflection or transmission, a ray attenuates by factors that depend on the frequency, the angle of incidence, and the nature of the medium (its material properties, thickness homogeneity, etc.)
The amount of reflection depends on the reflecting material.
  Smooth metal surfaces of good electrical conductivity are efficient reflectors of radio waves.
  The surface of the Earth itself is a fairly good reflector...

## Slide 28
Ground Reflection (2-Ray) Model
In a mobile radio channel, a single direct path between the base station and mobile is rarely the only physical path for propagation
  Hence the free space propagation model in most cases is inaccurate when used alone
Hence we use the 2 Ray GRM
  It considers both- direct path and ground reflected propagation path between transmitter and receiver

## Slide 29
Ground Reflection (2-Ray) Model
This was found reasonably accurate for predicting large scale signal strength over distances of several kilometers for mobile radio systems using tall towers ( heights above 50 m )

## Slide 30
Ground Reflection (2-Ray) Model
Good for systems that use tall towers (over 50 m tall)
Good for line-of-sight microcell systems in urban environments
ETOT is the electric field that results from a combination of a direct line-of-sight path and a ground reflected path

## Slide 31
Ground Reflection (2-Ray) Model
  The maximum T-R separation distance ( In most mobile communication systems ) is only a few tens of kilometers, and the earth may be assumed to be flat.
      ETOT =The total received E-field,
      ELOS=The direct line-of-sight component
      Eg =The ground reflected component,

## Slide 32
Example 3
A mobile is located 5 km away from a base station and uses a vertical λ/4 monopole antenna with a gain of 2.55 dB to receive cellular radio signals. The E-field at 1 km from the transmitter is measured to be 10 Exp-3V/mn. The carrier frequency used for this system is 900 MHz
  (a) Find the length and the gain of the receiving antenna
  (b) Find the received power at the mobile using the 2-ray ground reflection model assuming the height of the transmitting antenna is 50 m and the receiving antenna is 1.5 m above ground.

## Slide 33
Solution 3

## Slide 34
Diffraction
Occurs when the radio path between sender and receiver is obstructed by an impenetrable body and by a surface with sharp irregularities (edges)
The received field strength decreases rapidly as a receiver moves deeper into the obstructed (shadowed) region, the diffraction field still exists and often has sufficient strength to produce a useful signal.
Diffraction explains how radio signals can travel urban and rural environments without a line-of-sight path

## Slide 35
Illustration of Diffraction

## Slide 36
Diffraction
The phenomenon of diffraction can be explained by Huygen's principle, which states that all points on a wave front can be considered as point sources for the production of secondary wavelets, and that these 'wavelets combine to produce a new wave front in the direction of propagation
The field strength of a diffracted wave in the shadowed region is the vector sum of the electric field components of all the secondary wavelets in the space around the obstacle.

## Slide 37
Illustration of diffraction II

## Slide 38
Next time ..
Scattering ..

## Slide 39
Scattering
The medium which the wave travels consists of objects with dimensions smaller than the wavelength and where the number of obstacles per unit volume is large – rough surfaces, small objects, foliage, street signs, lamp posts.

## Slide 40
Illustration ..

## Slide 41
Scattering
Generally difficult to model because the environmental conditions that cause it are complex
Modeling “position of every street sign” is not feasible.

## Slide 42
We also have looked at ..
Propagation in free space always like light (straight line)
Received power proportional to 1/d² (d = distance between sender and receiver)
Receiving power additionally influenced by
  shadowing
  reflection at large obstacles
  refraction depending on the density of a medium
  scattering at small obstacles
  diffraction at edges

## Slide 43
Conclusion
As a mobile moves through a coverage area, different propagation mechanisms have an impact on the instantaneous received signal strength.
When a mobile has a clear LoS path to the base-station
  Diffraction and scattering will not dominate the propagation.
When a mobile is at a street level without LOS
  Diffraction and scattering will dominate the propagation.

## Slide 44
Conclusion – Urban Cellular Systems
No direct LoS path between Transmitter and Receiver
Presence of high-rise buildings causing severe diffraction loss.
Due to multiple reflections from various objects, the electromagnetic waves travel along different paths of varying lengths.
The interaction between these waves causes multipath fading at a specific location,
Strengths of the waves decrease as the distance between the transmitter and receiver increases.