## Slide 1: Radio Propagation - Large-Scale Path Loss
CS 515 Mobile and Wireless Networking
Ibrahim Korpeoglu
Computer Engineering Department
Bilkent University, Ankara

## Slide 2: Reading Homework Due Date: Next Wednesday
Read the handouts that wa have put into the library
Read the following paper:
    J. B. Andersen, T. S. Rappaport, S. Yoshida, Propagation Measurements and Models for Wireless Communications Channels, IEEE Communications Magazine, (January 1995), pp. 42-49.
Read Chapter 4 of Rappaport’s Book.
You have of course read the previous 4 papers!

## Slide 3: Basics
When electrons move, they create electromagnetic waves that can propagate through the space
Number of oscillations per second of an electromagnetic wave is called its frequency, f, measured in Hertz.
The distance between two consecutive maxima is called the wavelength, designated by 

## Slide 4: Basics
By attaching an antenna of the appropriate size to an electrical circuit, the electromagnetic waves can be broadcast efficiently and received by a receiver some distance away.
In vacuum, all electromagnetic waves travel at the speed of light: c = 3x108 m/sec.
In copper or fiber the speed slows down to about 2/3 of this value.
Relation between f,  , c: f = c

## Slide 5: Basics
We have seen earlier the electromagnetic spectrum.
The radio, microwave, infrared, and visible light portions of the spectrum can all be used to transmit information
  By modulating the amplitude, frequency, or phase of the waves.

## Slide 6: Basics
We have seen wireless channel concept earlier: it is characterized by a frequency band (called its bandwidth)
The amount of information a wireless channel can carry is related to its bandwidth
Most wireless transmission use narrow frequency band (f << f)
    f: frequency band
    f: middle frequency where transmission occurs
New technologies use spread spectrum techniques
    A wider frequency band is used for transmission

## Slide 7: Basics - Propagation
Radio waves are
    Easy to generate
    Can travel long distances
    Can penetrate buildings
    They are both used for indoor and outdoor communication
    They are omni-directional: can travel in all directions
    They can be narrowly focused at high frequencies (greater than 100MHz) using parabolic antennas (like satellite dishes)
    Properties of radio waves are frequency dependent
        At low frequencies, they pass through obstacles well, but the power falls off sharply with distance from source
        At high frequencies, they tend to travel in straight lines and bounce of obstacles (they can also be absorbed by rain)
        They are subject to interference from other radio wave sources

## Slide 8: Basics - Propagation
At VLF, LF, and MF bands, radio
waves follow the ground. AM radio
broadcasting uses MF band
At HF bands, the ground
waves tend to be absorbed by the
earth. The waves that reach ionosphere
(100-500km above earth surface),
are refracted and sent back to
earth.
absorption
reflection
Ionosphere

## Slide 9: Basics - Propagation
LOS path
Reflected Wave
Directional antennas are used
Waves follow more direct paths
- LOS: Line-of-Sight Communication
- Reflected wave interfere with the original signal
VHF Transmission

## Slide 10: Basics - Propagation
Waves behave more like light at higher frequencies
    Difficulty in passing obstacles
    More direct paths
They behave more like radio at lower frequencies
    Can pass obstacles

## Slide 11: Propagation Models
We are interested in propagation characteristics and models for waves with frequencyy in range: few MHz to a few GHz
Modeling radio channel is important for:
    Determining the coverage area of a transmitter
        Determine the transmitter power requirement
        Determine the battery lifetime
    Finding modulation and coding schemes to improve the channel quality
        Determine the maximum channel capacity

## Slide 12: Radio Propagation Models
Transmission path between sender and receiver could be
    Line-of-Sight (LOS)
    Obstructed by buildings, mountains and foliage
Even speed of motion effects the fading characteristics of the channel

## Slide 13: Radio Propagation Mechanisms
The physical mechanisms that govern radio propagation are complex and diverse, but generally attributed to the following three factors
      Reflection
      Diffraction
      Scattering
  Reflection
    Occurs when waves impinges upon an obstruction that is much larger in size compared to the wavelength of the signal
    Example: reflections from earth and buildings
    These reflections may interfere with the original signal constructively or destructively

## Slide 14: Radio Propagation Mechanisms
  Diffraction
    Occurs when the radio path between sender and receiver is obstructed by an impenetrable body and by a surface with sharp irregularities (edges)
    Explains how radio signals can travel urban and rural environments without a line-of-sight path
  Scattering
    Occurs when the radio channel contains objects whose sizes are on the order of the wavelength or less of the propagating wave and also when the number of obstacles are quite large.
    They are produced by small objects, rough surfaces and other irregularities on the channel
    Follows same principles with diffraction
    Causes the transmitter energy to be radiated in many directions
    Lamp posts and street signs may cause scattering

## Slide 15: Radio Propagation Mechanisms
Building Blocks
D
R
S
R: Reflection
D: Diffraction
S: Scattering
transmitter
receiver
D
Street

## Slide 16: Radio Propagation Mechanisms
As a mobile moves through a coverage area, these 3 mechanisms have an impact on the instantaneous received signal strength.
    If a mobile does have a clear line of sight path to the base-station, than diffraction and scattering will not dominate the propagation.
    If a mobile is at a street level without LOS, then diffraction and scattering will probably dominate the propagation.

## Slide 17: Radio Propagation Models
As the mobile moves over small distances, the instantaneous received signal will fluctuate rapidly giving rise to small-scale fading
      The reason is that the signal is the sum of many contributors coming from different directions and since the phases of these signals are random, the sum behave like a noise (Rayleigh fading).
      In small scale fading, the received signal power may change as much as 3 or 4 orders of magnitude (30dB or 40dB), when the receiver is only moved a fraction of the wavelength.

## Slide 18: Radio Propagation Models
As the mobile moves away from the transmitter over larger distances, the local average received signal will gradually decrease. This is called large-scale path loss.
    Typically the local average received power is computed by averaging signal measurements over a measurement track of 5 to 40For PCS, this means 1m-10m track)
The models that predict the mean signal strength for an arbitrary-receiver transmitter (T-R) separation distance are called large-scale propagation models
    Useful for estimating the coverage area of transmitters

## Slide 19: Small-Scale and Large-Scale Fading
14 16 18 20 22 24 26 28
T-R Separation (meters)
-70
-60
-50
-40
-30
Received Power (dBm)
This figure is just an illustration to show the concept. It is not based on read data.

## Slide 20: What is Decibel (dB)
What is dB (decibel):
  A logarithmic unit that is used to describe a ratio.
    Let say we have two values P1 and P2. The difference (ratio) between them can be expressed in dB and is computed as follows:
      10 log (P1/P2) dB
    Example: transmit power P1 = 100W, received power P2 = 1 W
        The difference is 10log(100/1) = 20dB.

## Slide 21: dB
dB unit can describe very big ratios with numbers of modest size.
    See some examples:
      Tx power = 100W, Received power = 1W
        Tx power is 100 times of received power
        Difference is 20dB
      Tx power = 100W, Received power = 1mW
        Tx power is 100,000 times of received power
        Difference is 50dB
      Tx power = 1000W, Received power = 1mW
        Tx power is million times of received power
        Difference is 60dB

## Slide 22: dBm
For power differences, dBm is used to denote a power level with respect to 1mW as the reference power level.
    Let say Tx power of a system is 100W.
    Question: What is the Tx power in unit of dBm?
    Answer:
      Tx_power(dBm) = 10log(100W/1mW) = 10log(100W/0.001W) = 10log(100,0000) = 50dBm

## Slide 23: dBW
For power differences, dBW is used to denote a power level with respect to 1W as the reference power level.
    Let say Tx power of a system is 100W.
    Question: What is the Tx power in unit of dBW?
    Answer:
      Tx_power(dBW) = 10log(100W/1W) = 10log(100) = 20dBW.

## Slide 24
Decibel (dB)
versus
Power Ratio
Comparison of
two Sound Systems

## Slide 25: Free-Space Propagation Model
Used to predict the received signal strength when transmitter and receiver have clear, unobstructed LOS path between them.
The received power decays as a function of T-R separation distance raised to some power.
Path Loss: Signal attenuation as a positive quantity measured in dB and defined as the difference (in dB) between the effective transmitter power and received power.

## Slide 26: Free-Space Propagation Model
Free space power received by a receiver antenna separated from a radiating transmitter antenna by a distance d is given by Friis free space equation:
  Pr(d) = (PtGtGr2) / ((4)2d2L) [Equation 1]
      Pt is transmited power
      Pr(d) is the received power
      Gt is the trasmitter antenna gain (dimensionless quantity)
      Gr is the receiver antenna gain (dimensionless quantity)
      d is T-R separation distance in meters
      L is system loss factor not related to propagation (L >= 1)
        L = 1 indicates no loss in system hardware (for our purposes we will take L = 1, so we will igonore it in our calculations).
       is wavelength in meters.

## Slide 27: Free-Space Propagation Model
  The gain of an antenna G is related to its affective aperture Ae by:
    G = 4Ae / 2 [Equation 2]
      The effective aperture of Ae is related to the physical size of the antenna,
     is related to the carrier frequency by:
       = c/f = 2c / c [Equation 3]
        f is carrier frequency in Hertz
        c is carrier frequency in radians per second.
        c is speed of light in meters/sec

## Slide 28: Free-Space Propagation Model
An isotropic radiator is an ideal antenna that radiates power with unit gain uniformly in all directions. It is as the reference antenna in wireless systems.
The effective isotropic radiated power (EIRP) is defined as:
  EIRP = PtGt [Equation 4]
Antenna gains are given in units of dBi (dB gain with respect to an isotropic antenna) or units of dBd (dB gain with respect to a half-wave dipole antenna).
    Unity gain means:
        G is 1 or 0dBi

## Slide 29: Free-Space Propagation Model
Path loss, which represents signal attenuation as positive quantity measured in dB, is defined as the difference (in dB) between the effective transmitted power and the received power.
    PL(dB) = 10 log (Pt/Pr) = -10log[(GtGr2)/(4)2d2] [Equation 5]
    (You can drive this from equation 1)
  If antennas have unity gains (exclude them)
    PL(dB) = 10 log (Pt/Pr) = -10log[2/(4)2d2] [Equation 6]

## Slide 30: Free-Space Propagation Model
For Friis equation to hold, distance d should be in the far-field of the transmitting antenna.
The far-field, or Fraunhofer region, of a transmitting antenna is defined as the region beyond the far-field distance df given by:
    df = 2D2/[Equation 7]
      D is the largest physical dimension of the antenna.
    Additionally, df >> D and df >> 

## Slide 31: Free-Space Propagation Model – Reference Distance d0
It is clear the Equation 1 does not hold for d = 0.
For this reason, models use a close-in distance d0 as the receiver power reference point.
    d0 should be >= df
    d0 should be smaller than any practical distance a mobile system uses
Received power Pr(d), at a distance d > d0 from a transmitter, is related to Pr at d0, which is expressed as Pr(d0).
The power received in free space at a distance greater than d0 is given by:
    Pr(d) = Pr(d0)(d0/d)2 d >= d0 >= df [Equation 8]

## Slide 32: Free-Space Propagation Model
Expressing the received power in dBm and dBW
    Pr(d) (dBm) = 10 log [Pr(d0)/0.001W] + 20log(d0/d) where d >= d0 >= df and Pr(d0) is in units of watts. [Equation 9]
    Pr(d) (dBW) = 10 log [Pr(d0)/1W] + 20log(d0/d) where d >= d0 >= df and Pr(d0) is in units of watts. [Equation 10]
Reference distance d0 for practical systems:
    For frequncies in the range 1-2 GHz
      1 m in indoor environments
      100m-1km in outdoor environments

## Slide 33: Example Question
A transmitter produces 50W of power.
  A) Express the transmit power in dBm
  B) Express the transmit power in dBW
  C) If d0 is 100m and the received power at that distance is 0.0035mW, then find the received power level at a distance of 10km.
    Assume that the transmit and receive antennas have unity gains.

## Slide 34: Solution
A)
  Pt(W) is 50W.
  Pt(dBm) = 10log[Pt(mW)/1mW)] Pt(dBm) = 10log(50x1000) Pt(dBm) = 47 dBm
B)
  Pt(dBW) = 10log[Pt(W)/1W)] Pt(dBW) = 10log(50) Pt(dBW) = 17 dBW

## Slide 35: Solution
Pr(d) = Pr(d0)(d0/d)2
Substitute the values into the equation:
  Pr(10km) = Pr(100m)(100m/10km)2 Pr(10km) = 0.0035mW(10-4) Pr(10km) = 3.5x10-10W
  Pr(10km) [dBm] = 10log(3.5x10-10W/1mW) = 10log(3.5x10-7) = -64.5dBm

## Slide 36: Two main channel design issues
Communication engineers are generally concerned with two main radio channel issues:
    Link Budged Design
      Link budget design determines fundamental quantities such as transmit power requirements, coverage areas, and battery life
      It is determined by the amount of received power that may be expected at a particular distance or location from a transmitter
    Time dispersion
      It arises because of multi-path propagation where replicas of the transmitted signal reach the receiver with different propagation delays due to the propagation mechanisms that are described earlier.
      Time dispersion nature of the channel determines the maximum data rate that may be transmitted without using equalization.

## Slide 37: Link Budged Design Using Path Loss Models
Radio propagation models can be derived
  By use of empirical methods: collect measurement, fit curves.
  By use of analytical methods
    Model the propagation mechanisms mathematically and derive equations for path loss
Long distance path loss model
  Empirical and analytical models show that received signal power decreases logarithmically with distance for both indoor and outdoor channels

## Slide 38: Announcements
  Please download the homework from the course webpage again. I made some important corrrections and modifications!
  I recommend that you read Chapter 4 of the book and “radio propagation paper” in parallel.
  Start early doing the homework! The last night before deadline may be loo late!!!.
  I put some links about math and statistics resources on the course webpage.
  I put a Z table on the webpage. Q-table and Z-table are related as follows: Q_table(z) = 0.5 - Z_table(z)

## Slide 39: Long distance path loss model
The average large-scale path loss for an arbitrary T-R separation is expressed as a function of distance by using a path loss exponent n:
    The value of n depends on the propagation environment: for free space it is 2; when obstructions are present it has a larger value.
Equation 11

## Slide 40: Path Loss Exponent for Different Environments
Environment | Path Loss Exponent, n
Free space | 2
Urban area cellular radio | 2.7 to 3.5
Shadowed urban cellular radio | 3 to 5
In building line-of-sight | 1.6 to 1.8
Obstructed in building | 4 to 6
Obstructed in factories | 2 to 3

## Slide 41: Selection of free space reference distance
In large coverage cellular systems
  1km reference distances are commonly used
In microcellular systems
  Much smaller distances are used: such as 100m or 1m.
The reference distance should always be in the far-field of the antenna so that near-field effects do not alter the reference path loss.

## Slide 42: Log-normal Shadowing
Equation 11 does not consider the fact the surrounding environment may be vastly different at two locations having the same T-R separation
This leads to measurements that are different than the predicted values obtained using the above equation.
Measurements show that for any value d, the path loss PL(d) in dBm at a particular location is random and distributed normally.

## Slide 43: Log-normal Shadowing- Path Loss
  X is a zero-mean Gaussian (normal) distributed random variable (in dB) with standard deviation (also in dB).
Then adding this random factor:
denotes the average large-scale path loss (in dB) at a distance d.
is usually computed assuming free space propagation model between transmitter and d0 (or by measurement).
  Equation 12 takes into account the shadowing affects due to cluttering on the propagation path. It is used as the propagation model for log-normal shadowing environments.
Equation 12

## Slide 44: Log-normal Shadowing- Received Power
The received power in log-normal shadowing environment is given by the following formula (derivable from Equation 12)
    The antenna gains are included in PL(d).
Equation 12

## Slide 45: Log-normal Shadowing, n and 
The log-normal shadowing model indicates the received power at a distance d is normally distributed with a distance dependent mean and with a standard deviation of 
In practice the values of n and are computed from measured data using linear regression so that the difference between the measured data and estimated path losses are minimized in a mean square error sense.

## Slide 46: Example of determining n and 
Assume Pr(d0) = 0dBm and d0 is 100m
Assume the receiver power Pr is measured at distances 100m, 500m, 1000m, and 3000m,
The table gives the measured values of received power
Distance from Transmitter | Received Power
100m | 0dBm
500m | -5dBm
1000m | -11dBm
3000m | -16dBm

## Slide 47: Example of determining n and 
We know the measured values.
Lets compute the estimates for received power at different distances using long-distance path loss model. (Equation 11)
Pr(d0) is given as 0dBm and measured value is also the same.
  mean_Pr(d) = Pr(d0) – mean_PL(from_d0_to_d)
  Then mean_Pr(d) = 0 – 10logn(d/d0)
  Use this equation to computer power levels at 500m, 1000m, and 3000m.

## Slide 48: Example of determining n and 
  Average_Pr(500m) = 0 – 10logn(500/100) = -6.99n
  Average_Pr(1000m) = 0 – 10logn(1000/100) = -10n
  Average_Pr(3000m) = 0 – 10logn(3000/100) = -14.77n
Now we know the estimates and also measured actual values of the received power at different distances
In order approximate n, we have to choose a value for n such that the mean square error over the collected statistics is minimized.

## Slide 49: Example of determining n and MSE(Mean Square Error)
The mean square error (MSE) is given with the following formula:
Since power estimate at some distance depends on n, MSE(n) is a function of n.
We would like to find a value of n that will minimize this MSE(n) value. We
We will call it MMSE: minimum mean square error.
This can be achieved by writing MSE as a function of n. Then finding the
value of n which minimizes this function. This can be done by derivating
MSE(n) with respect to n and solving for n which makes the derivative equal to
zero.
[Equation 14]

## Slide 50: Example of determining n
Distance | Measured Value of Pr (dBm) | Estimated Value of Pr (dBm)
100m | 0 | 0
500m | -5 | -6.99n
1000m | -11 | -10n
3000m | -16 | -14.77n
MSE = (0-0)2 + (-5-(-6.99n))2 + (-11-(-10n)2 + (-16-(-14.77n)2
MSE = 0 + (6.99n – 5)2 + (10n – 11)2 + (14.77n – 16)2
If we open this, we get MSE as a function of n which as second order polynomial.
We can easily take its derivate and find the value of n which minimizes MSE. ( I will not show these steps, since they are trivial).

## Slide 51: Example of determining 
We are interested in finding the standard deviation about the mean value
For this, we will use the following formula
Equation 14.1
Equation 14.2

## Slide 52: Some Statistics Knowledge: Computation of mean (), variance (2) and standard deviation ()
Assume we have k samples (k values) X1, X2, …, Xk :
The mean is denoted by 
The variance is denotes by 
The standard deviation is denotes by 2.
The formulas to computer , , and  is given below:
[Equation 15]
[Equation 16]
[Equation 17]

## Slide 53: Path loss and Received Power
In log normal shadowing environment:
    PL(d) (path loss) and Pr(d) (received power at a distance d) are random variables with a normal distribution in dB about a distance dependent mean.
Sometime we are interested in answering following kind of questions:
    What is mean received Pr(d) power (mean_Pr(d))at a distance d from a transmitter
    What is the probability that the receiver power Pr(d) (expressed in dB power units) at distance d is above (or below) some fixed value  (again expressed in dB power units such as dBm or dBW).

## Slide 54: Received Power and Normal Distribution
In answering these kind of question, we have to use the properties of normal (gaussian distribution).
Pr(d) is normally distributed that is characterized by:
    a mean ()
    a standard deviation ()
We are interested in Probability that Pr(d) >= or Pr(d) <= 

## Slide 55: Received Power and Normal Distribution PDF
Figure shows the PDF of a normal distribution for the received power Pr at
some fixed distance d (  = 10,  = 5)
(x-axis is received power, y-axis probability)
EXAMPLE:
Probability that Pr is
smaller than 3.3
(Prob(Pr <= 3.3))
is
given with value of
the stripped area under
the curve.

## Slide 56: Normal CDF
0.090123
0.5
The figure shows the CDF plot of the normal distribution described previously.
Prob(Pr <= 3.3) can be found by finding first the point where vertical line from 3.3
intersects the curve and then by finding the corresponding point on the y-axis.
This corresponds to a value of 0.09. Hence Prob(Pr <= 3.3) = 0.09

## Slide 57: Use of Normal Distribution
PDF (probability density function of a normal distribution is characterized by
two parameters,  (mean)and (standard deviation), and given with the
formula above.
[Equation 18]

## Slide 58: Use of Normal Distribution
To find out the probability that a Gaussian (normal) random variable
X is above a value x0, we have to integrate pdf.
This integration does not have any closed form.
Any Gaussian PDF can be rewritten through substitution of y = x– / to yield
Equation 19
Equation 20

## Slide 59: Use of Normal Distribution
In the above formula, the kernel of the integral is normalized Gaussian
PDF function with  = 0 and = 1.
Evaluation of this function is designed as Q-function and defined as
Hence Equation 19 or 20 can be evaluated as:
Equation 21
Equation 22

## Slide 60: Q-Function
Q-Function is bounded by two analytical expressions as follows:
For values greater than 3.0, both of these bounds closely approximate Q(z).
Two important properties of Q(z) are:
  Q(-z) = 1 – Q(z) Equation 24
  Q(0) = 1/2 Equation 25
Equation 23

## Slide 61: Tabulation of Q-function (0<=z<=3.9)
z | Q(z) | z | Q(z) | z | Q(z) | z | Q(z)
0.0 | 0.5 | 1.0 | 0.15866 | 2.0 | 0.02275 | 3.0 | 0.00135
0.1 | 0.46017 | 1.1 | 0.13567 | 2.1 | 0.01786 | 3.1 | 0.00097
0.2 | 0.42074 | 1.2 | 0.11507 | 2.2 | 0.01390 | 3.2 | 0.00069
0.3 | 0.38209 | 1.3 | 0.09680 | 2.3 | 0.01072 | 3.3 | 0.00048
0.4 | 0.34458 | 1.4 | 0.08076 | 2.4 | 0.00820 | 3.4 | 0.00034
0.5 | 0.30854 | 1.5 | 0.06681 | 2.5 | 0.00621 | 3.5 | 0.00023
0.6 | 0.27425 | 1.6 | 0.05480 | 2.6 | 0.00466 | 3.6 | 0.00016
0.7 | 0.24196 | 1.7 | 0.04457 | 2.7 | 0.00347 | 3.7 | 0.00011
0.8 | 0.21118 | 1.8 | 0.03593 | 2.8 | 0.00256 | 3.8 | 0.00007
0.9 | 0.18406 | 1.9 | 0.02872 | 2.9 | 0.00187 | 3.9 | 0.00005
For values of z higher than 3.9, you should use the equations on the
previous slide to compute Q(z).

## Slide 62: Q-Function Graph: z versus Q(z)
z (1 <= z <= 3.9
Q(z)

## Slide 63: Erf and Erfc functions
The error function (erf) is defined as:
And the complementary error function (erfc) is defined as:
The erfc function is related to erf function by:
[Equation 26]
[Equation 27]
[Equation 28]

## Slide 64: Erf and Erfc functions
The Q-function is related to erf and erfc functions by:
[Equation 29]
[Equation 31]
[Equation 30]

## Slide 65: Computation of probability that the received power is below/above a threshold
We said that Pr(d) is a random variable that is Gaussian distributed with mean  and std deviation Then:
  Probability that Pr(d) is above  is given by:
  Probability that Pr(d) is below  is given by:
      Pr(d) bar denotes the average (mean ) received power at d.
Equation 32
Equation 33

## Slide 66: Percentage of Coverage Area
We are interested in the following problem
    Given a circular coverage area with radius R from a base station
    Given a desired threshold power level .
  Find out
    U(), the percentage of useful service area
      i.e the percentage of area with a received signal that is equal or greater than given a known likelihood of coverage at the cell boundary

## Slide 67: Percentage of Coverage Area
O
R
r
O is the origin of the cell
r: radial distance d from transmitter
0 <= r <= R
Definition: P(Pr(r) >) denotes probability that the random received power at a distance
d = r is greater than threshold within an incrementally small area dA
Then U() can be found by the following integration over the area of the
cell:
Equation 34

## Slide 68: Integrating f(r) over Circle Area
A
B
C
D
R
r

r
O
f(r)

## Slide 69: Percentage of Coverage Area
Using equation 32:
The path loss at distance r can be expressed as:
O d0 r R
PL(from O to r) = PL(from O to d0) + PL(from d0 to R) - PL(from r to R)
PL(from O to r) = PL(from O to d0) + PL(from d0 to R) + PL(from R to r)
(O is the point where base station is located)
Which can be formally expressed as:
Equation 33
Equation 34

## Slide 70: Percentage of Coverage Area
Equation 33 can be expressed as follows using error function:
By combining with Equation 34
Equation 35
Equation 36

## Slide 71: Percentage of Coverage Area
Let the following substitutions happen:
Then
Substitute t = a+ blog(r/R)
Equation 37
Equation 38

## Slide 72: Percentage of Coverage Area
By choosing a signal level such that (i.e. a = ), we obtain:
where
Equation 39
The simplified formula above gives the percentage coverage assuming the mean received power at the cell boundary (r=R) is .
In other words, we are assuming: Prob(Pr(R) >= ) = 0.5

## Slide 73: Indoor and Outdoor Propagation

## Slide 74: Outdoor Propagation
We will look to the propagation from a transmitter in an outdoor environment
  The coverage area around a tranmitter is called a cell.
    Coverage area is defined as the area in which the path loss is at or below a given value.
  The shape of the cell is modeled as hexagon, but in real life it has much more irregular shapes.
  By playing with the antenna (tilting and changing the height), the size of the cell can be controlled.
We will look to the propagation characteristics of the three outdoor environments
  Propagation in macrocells
  Propagation in microcells
  Propagation in street microcells

## Slide 75: Macrocells
Base stations at high-points
Coverage of several kilometers
The average path loss in dB has normal distribution
    Avg path loss is result of many forward scattering over a great many of obstacles
      Each contributing a random multiplicative factor
      Converted to dB, this gives a sum of random variable
    Sum is normally distributed because of central limit theorem

## Slide 76: Macrocells
In early days, the models were based on emprical studies
Okumura did comprehesive measurements in 1968 and came up with a model.
    Discovered that a good model for path loss was a simple power law where the exponent n is a function of the frequency, antenna heights, etc.
    Valid for frequencies in: 100MHz – 1920 MHz for distances: 1km – 100km

## Slide 77: Okumura Model
L50(d)(dB) = LF(d)+ Amu(f,d) – G(hte) – G(hre) – GAREA
  L50: 50th percentile (i.e., median) of path loss
  LF(d): free space propagation pathloss.
  Amu(f,d): median attenuation relative to free space
    Can be obtained from Okumura’s emprical plots shown in the book (Rappaport), page 151.
  G(hte): base station antenna heigh gain factor
  G(hre): mobile antenna height gain factor
  GAREA: gain due to type of environment
    G(hte) = 20log(hte/200) 1000m > hte > 30m
    G(hre) = 10log(hre/3) hre <= 3m
    G(hre) = 20log(hre/3) 10m > hre > 3m
        hte: transmitter antenna height
        hre: receiver antenna height
Equation 40

## Slide 78: Hata Model
Valid from 150MHz to 1500MHz
A standard formula
For urban areas the formula is:
  L50(urban,d)(dB) = 69.55 + 26.16logfc - 13.82loghte – a(hre) + (44.9 – 6.55loghte)logd where
        fc is the ferquency in MHz
        hte is effective transmitter antenna height in meters (30-200m)
        hre is effective receiver antenna height in meters (1-10m)
        d is T-R separation in km
        a(hre) is the correction factor for effective mobile antenna height which is a function of coverage area
        a(hre) = (1.1logfc – 0.7)hre – (1.56logfc – 0.8) dB for a small to medium sized city
Equation 41

## Slide 79: Microcells
Propagation differs significantly
  Milder propagation characteristics
  Small multipath delay spread and shallow fading imply the feasibility of higher data-rate transmission
  Mostly used in crowded urban areas
  If transmitter antenna is lower than the surrounding building than the signals propagate along the streets: Street Microcells

## Slide 80: Macrocells versus Microcells
Item | Macrocell | Microcell
Cell Radius | 1 to 20km | 0.1 to 1km
Tx Power | 1 to 10W | 0.1 to 1W
Fading | Rayleigh | Nakgami-Rice
RMS Delay Spread | 0.1 to 10s | 10 to 100ns
Max. Bit Rate | 0.3 Mbps | 1 Mbps

## Slide 81: Street Microcells
Most of the signal power propagates along the street.
The sigals may reach with LOS paths if the receiver is along the same street with the transmitter
The signals may reach via indirect propagation mechanisms if the receiver turns to another street.

## Slide 82: Street Microcells
B
A
D
C
log (distance)
log (distance)
received power (dB)
received power (dB)
A
C
B
A
D
Breakpoint
Breakpoint
n=2
n=4
n=2
n=4~8
15~20dB
Building Blocks

## Slide 83: Indoor Propagation
Indoor channels are different from traditional mobile radio channels in two different ways:
    The distances covered are much smaller
    The variablity of the environment is much greater for a much smaller range of T-R separation distances.
The propagation inside a building is influenced by:
    Layout of the building
    Construction materials
    Building type: sports arena, residential home, factory,...

## Slide 84: Indoor Propagation
Indoor propagation is domited by the same mechanisms as outdoor: reflection, scattering, diffraction.
  However, conditions are much more variable
    Doors/windows open or not
    The mounting place of antenna: desk, ceiling, etc.
    The level of floors
Indoor channels are classified as
  Line-of-sight (LOS)
  Obstructed (OBS) with varying degrees of clutter.

## Slide 85: Indoor Propagation
Buiding types
    Residential homes in suburban areas
    Residential homes in urban areas
    Traditional office buildings with fixed walls (hard partitions)
    Open plan buildings with movable wall panels (soft partitions)
    Factory buildings
    Grocery stores
    Retail stores
    Sport arenas

## Slide 86: Indoor propagation events and parameters
Temporal fading for fixed and moving terminals
    Motion of people inside building causes Ricean Fading for the stationary receivers
    Portable receivers experience in general:
      Rayleigh fading for OBS propagation paths
      Ricean fading for LOS paths.
Multipath Delay Spread
    Buildings with fewer metals and hard-partitions typically have small rms delay spreads: 30-60ns.
      Can support data rates excess of several Mbps without equalization
    Larger buildings with great amount of metal and open aisles may have rms delay spreads as large as 300ns.
      Can not support data rates more than a few hundred Kbps without equalization.
Path Loss
    The following formula that we have seen earlier also describes the indoor path loss:
      PL(d)[dBm] = PL(d0) + 10nlog(d/d0) + X
        n and  depend on the type of the building
        Smaller value for  indicates the accuracy of the path loss model.

## Slide 87: Path Loss Exponent and Standard Deviation Measured for Different Buildings
Building | Frequency (MHz) | n |  (dB)
Retail Stores | 914 | 2.2 | 8.7
Grocery Store | 914 | 1.8 | 5.2
Office, hard partition | 1500 | 3.0 | 7.0
Office, soft partition | 900 | 2.4 | 9.6
Office, soft partition | 1900 | 2.6 | 14.1
Factory LOS |  |  | 
Textile/Chemical | 1300 | 2.0 | 3.0
Textile/Chemical | 4000 | 2.1 | 7.0
Paper/Cereals | 1300 | 1.8 | 6.0
Metalworking | 1300 | 1.6 | 5.8
Suburban Home |  |  | 
Indoor Street | 900 | 3.0 | 7.0
Factory OBS |  |  | 
Textile/Chemical | 4000 | 2.1 | 9.7
Metalworking | 1300 | 3.3 | 6.8

## Slide 88: In building path loss factors
Partition losses (same floor)
Partition losses between floors
Signal Penetration into Buildings

## Slide 89: Partition Losses
There are two kind of partition at the same floor:
  Hard partions: the walls of the rooms
  Soft partitions: moveable partitions that does not span to the ceiling
  The path loss depends on the type of the partitions

## Slide 90: Partition Losses
Material Type | Loss (dB) | Frequency (MHz)
All metal | 26 | 815
Aluminim Siding | 20.4 | 815
Concerete Block Wall | 3.9 | 1300
Loss from one Floor | 20-30 | 1300
Turning an Angle in a Corridor | 10-15 | 1300
Concrete Floor | 10 | 1300
Dry Plywood (3/4in) – 1 sheet | 1 | 9600
Wet Plywood (3/4in) – 1 sheet | 19 | 9600
Aluminum (1/8in) – 1 sheet | 47 | 9600
Average signal loss measurements reported by various researches for radio paths obscructed by some common building material.

## Slide 91: Partition Losses between Floors
The losses between floors of a building are determined by
    External dimensions and materials of the building
    Type of construction used to create floors
    External surroundings
    Number of windows
    Presence of tinting on windows

## Slide 92: Partition Losses between Floors
Building | FAF (dB) | (dB)
Office Building 1 |  | 
Through 1 Floor | 12.9 | 7.0
Through 2 Floors | 18.7 | 2.8
Through 3 Floors | 24.4 | 1.7
Through 4 Floors | 27.0 | 1.5
Office Building 2 |  | 
Through 1 Floor | 16.2 | 2.9
Through 2 Floors | 27.5 | 5.4
Through 3 Floors | 31.6 | 7.2
Average Floor Attenuation Factor in dB for One, Two, Three and
Four Floors in Two Office Buildings

## Slide 93: Signal Penetration Into Buildings
RF signals can penetrate from outside transmitter to the inside of buildings
    However the siganls are attenuated
The path loss during penetration has been found to be a function of:
    Frequency of the signal
    The height of the building

## Slide 94: Signal Penetration Into Buildings
Effect of Frequency
    Penetration loss decreases with increasing frequency
Effect of Height
    Penetration loss decreases with the height of the building up-to some certain height
      At lower heights, the urban clutter induces greater attenuation
    and then it increases
      Shadowing affects of adjascent buildings
Frequency (MHz) | Loss (dB)
441 | 16.4
896.5 | 11.6
1400 | 7.6

## Slide 95: Conclusion
More work needs to be done to understand the characteristics of wireless channels
3D numerical modeling approaches exist
To achieve PCS, new and novel ways of classifying wireless environments will be needed that are both widely encompassing and reasonably compact.