## Slide 1: Propagation: fundamentals and models
Carol Wilson, CSIRO
Vice-Chairman ITU-R Study Group 3 & Chairman WP 3M
3rd Summer School in Spectrum Management for Radio Astronomy
31 May – 4 June 2010, Tokyo

## Slide 2: Outline of presentation
Introduction – why propagation matters
Mechanisms of radiowave propagation and prediction methods
Types of models
Software
Conclusion

## Slide 3: Why does propagation matter?
Predict levels of interference from other radio sources
Understand variability of interference
Assess possible interference mitigation methods

## Slide 4: Basic definitions
Propagation – what happens to an radio signal as it travels.
  Enough signal where you want it to be? (System design)
  Too much signal where you don’t want it to be? (Interference)
Attenuation – loss due to:
  Distance
  Ground
  Obstacles (terrain, buildings…)
  Tropospheric and ionospheric variations (weather, etc)
Loss = 10*log (Ptx/Prx) (expressed as positive number)
Does not (generally) include antenna gain

## Slide 5: Mechanisms of propagation
Free space – loss due simply to distance
  Generally sets the lower bound on the loss (upper bound on interference level)
Mechanisms that increase loss (decrease interference)
  Diffraction (including sub-path diffraction)
  Attenuation by rain (snow, etc) and atmospheric gases
Mechanisms that decrease loss (increase interference)
  Reflection/refraction (ground or atmospheric layers)
  Multipath in cluttered environments
  Atmospheric ducting
  Ionospheric sporadic-E propagation (VHF/HF)
  Rain scatter
Environment is complex and difficult (or impossible) to define in detail  uncertainty in prediction. (c.f. weather forecasting)

## Slide 6: Interference mechanisms
Tropospheric scatter
Diffraction
Line of sight
Ducting
Reflection/refraction by elevated layers
Hydrometeor scatter
Line of sight with multipath enhancement
Long-term effects 
 Short-term effects

## Slide 7: ITU-R Study Group 3 Recommendations
Study Group 3 webpage:
www.itu.int/ITU-R/index.asp?category=study-groups&link=rsg3&lang=en
Recommendations:
http://www.itu.int/rec/R-REC-P/en
Go here to get three free Recommendations per year:
http://www.itu.int/publications/bookshop/how-to-buy.html#free
Updated when better methods or information is available. Use most recent version. (Rec P.526-11 rather than P.526-10)

## Slide 8: Relation between propagation values
Field strength for a given isotropically transmitted power:
E = Pt – 20 log d + 74.8
Isotropically received power for a given field strength:
Pr = E – 20 log f – 167.2
Free-space basic transmission loss for a given isotropically transmitted power and field strength:
Lbf = Pt – E + 20 log f + 167.2
Power flux-density for a given field strength:
S = E – 145.8
where:
Pt : isotropically transmitted power (dB(W))
Pr : isotropically received power (dB(W))
E : electric field strength (dB(V/m))
f : frequency (GHz)
d : radio path length (km)
Lbf : free-space basic transmission loss (dB)
S : power flux-density (dB(W/m2)).
From ITU-R Recommendation P.525

## Slide 9: Free space loss
Attenuation of signal due to distance alone.
Lbf = 20 log (4d / ) dB
or in practical units
Lbf = 32.4 + 20 log(f) + 20 log (d) dB
where f is in MHz and d is in distance
For most practical situations, free space loss is the minimum loss  worst case interference.
Applicable to interference from aircraft, satellites.
Apparent “line-of-sight” paths not necessarily free space loss only!
ITU-R Recommendation P.525

## Slide 10: Refraction through atmospheric layers
Ordinary atmospheric conditions create ray bending so that the radio horizon is greater than the geometric horizon.
Modelled by use of k-factor multiplied by physical earth radius. Median global value of k is 4/3.
Physical earth radius is ~6370 km. ae = 6370*(4/3) = ~8500 km
For antenna heights h1 and h2, line of sight distance is:
Recommendation ITU-R P.834
re
ae =k re
re

## Slide 11: Diffraction – within line-of-sight
Not only when direct line between transmitter and receiver is obstructed.
Subpath diffraction – due to Earth bulge on paths within line-of-sight distance if clearance is less than
Recommendation ITU-R P.526

## Slide 12: Diffraction – simple obstructions
Smooth earth diffraction – curvature of the Earth itself on a transhorizon path. (Rec P.526; below 10 MHz, use Rec P.368.)
Single obstacles. Approximated as ideal knife-edge or rounded cylinders. Methods in Rec. P.526.

## Slide 13: Diffraction – more complicated terrain
Multiple knife-edge diffraction model:
  Used for prediction of signal level over long distances or wide areas
  Uses digital terrain map
  Simple to implement but surprisingly accurate compared to measurements
  Used by ITU for prediction of both wanted and interfering signals

## Slide 14: Knife-edge diffraction model
  Terrain profile includes earth curvature and atmospheric refraction
  Diffraction parameter  is a function of how far the terrain point obstructs the first Fresnel zone radius:
  Point with largest  on entire path: principal edge
  Points with largest  either side of principal edge: auxiliary edges
  Sum diffraction loss from three edges
  L = J(p) + {1.0 – exp( –J(p) / 6 )} [J(t) + J(r) + 10.0 + 0.04D ]
Recommendation ITU-R P.526

## Slide 15: Tropospheric scatter and ducting
Scattering from inhomogeneities (troposcatter) is the main long-term effect on long paths (more than ~100 km) when diffraction loss becomes high.
Ducting may occur for short periods of time due to atmospheric layers near the surface (over water or flat coastal areas) or elevated layers in the atmosphere. May be significant for distances up to ~ 300 km.
Recommendation ITU-R P.452 gives an empirical calculation method for troposcatter, ducting and reflection from atmospheric layers.
Scatter from rain can also calculated using Recommendation ITU-R P.452. (May be significant above ~ 5 GHz)

## Slide 16: Mechanisms affecting HF and VHF
Small but intense ionization layers in the E-region of the ionosphere (Sporadic-E) can cause abnormal VHF propagation for periods lasting several hours. Effect decreases with increasing frequency but can be significant up to ~135 MHz.
Recommendation P.534 gives a method for predicting field strength and probability of occurrence.
At frequencies to ~30 MHz, ground wave propagation is the major propagation mechanism.
Recommendation P.368 gives a method for predicting ground wave field strength, based on curves.

## Slide 17: Ground wave 10 kHz to 30 MHz

## Slide 18: Other propagation mechanisms
Multipath – reflections from objects may cause distortion of wanted signal. In some specific scenarios, may increase interference power.
Attenuation due to rain, clouds, fog, snow, etc. Noticeable above about 5 GHz. Decreases wanted signal (and interference signal). Raises noise temperature.
Atmospheric attenuation noticeable with increasing frequency and at specific molecular resonance frequencies. Provides good isolation between active transmitters and passive services in frequency bands above ~ 200 GHz.

## Slide 19: Specific attenuation due to atmosphere
Chart shows specific attenuation at 1013 hPa, 15°C, water vapour density 7.5 g/m3
At frequencies above 100 GHz, loss becomes significant.
Helpful in protecting passive services as very high bands.

## Slide 20: Types of models
Propagation models typically used to define worst case scenario for the intended purpose.
Interference varies with changing conditions, leading to statistical descriptions.
Models for system design focus on high attenuation scenarios.
Models for interference focus on low attenuation scenarios.
Be cautious about applying system design propagation models for interference analysis.
Model accuracy depends on quality of information available.
Generic models useful when specific sites not known.
Site-specific models useful when terrain information is available.

## Slide 21: Key ITU-R Recommendations
Recommendation ITU-R P.452 (Prediction of interference between stations on the surface of the Earth at frequencies above 0.1 GHz)
  Uses multiple knife-edge diffraction model for specific terrain, and troposcatter, ducting, etc.
Recommendation ITU-R P.1546 (Point-to-area predictions for terrestrial services 30 MHz to 3 000 MHz). Generic terrain assumptions.
  Based on curves of measured data over a number of land paths.
  Used in 2006 by ITU as technical basis to replan broadcasting across Europe, Africa and the Middle East.

## Slide 22: Recommendation P.1546 for 30 MHz to 3 GHz
Curves represent field strength exceeded at 50% of locations for 1kW ERP transmission as function of:
  Frequency: 100, 600, 2000 MHz
  Time: 50%, 10%, 1%
  Tx antenna height: 10 to 1200 m; Rx antenna height: local clutter height (minimum 10 m)
  Path type: land, warm sea, cold sea
  Distance: 1 to 1000 km
  Interpolation method for all of above.
Curves are based on extensive measurement campaigns in Europe, North America, the North Sea and Mediterranean.

## Slide 23: A word about software packages
Many commercial software packages available and useful, but:
Be aware of purpose (system design vs interference analysis)
Sometimes mistakes in coding go unnoticed.
Often out-of-date with respect to ITU-R Recommendations.
Understand the underlying mechanisms being modelled and look for anomalies.
ITU Study Group 3 website has some free software available on “as is” basis. (Including Rec P.452, curves for P.1546, etc)

## Slide 24: Expectations
Propagation prediction method
Measurements
“Reality”
Error:
Mean
Std Dev
???
Prediction method development – aim to minimize mean error
Site specific models – std deviation of several dB
SG 3 goals: 1) accuracy, 2) clarity, 3) simplicity, 4) physical representation.
On all but shortest paths, propagation loss varies with time.
Models useful for comparison of different options, for overall statistics.
An accepted, transparent model often useful in regulatory situations.

## Slide 25: Conclusions
Propagation prediction methods necessary to estimate, understand interference to radioastronomy.
Prediction methods available from ITU (and other sources) to model various propagation mechanisms.
Statistics of interference and system design are different.
General knowledge of propagation phenomena useful in radioastronomy design and operation.
See you at the Study Group 3 website!
www.itu.int/ITU-R/index.asp?category=study-groups&link=rsg3&lang=en

## Slide 26: Thank you! Questions?
Contact Us
Phone: 1300 363 400 or +61 3 9545 2176
Email: enquiries@csiro.au Web: www.csiro.au
Carol Wilson, Research Consultant
carol.wilson@csiro.au