## Slide 1: Radio Waves
Electromagnetic Radiation
Radio Transmission and Reception
Modulation Techniques
Notes: <number>
<footer>
<header>
<date/time>

## Slide 2: Electromagnetism
Electricity and magnetism are different facets of electromagnetism
  recall that a static distribution of charges produces an electric field
  charges in motion (an electrical current) produce a magnetic field
  a changing magnetic field produces an electric field, moving charges
Electric and Magnetic fields produce forces on charges
An accelerating charge produces electromagnetic waves (radiation)
Both electric and magnetic fields can transport energy
  Electric field energy used in electrical circuits & released in lightning
  Magnetic field carries energy through transformer

## Slide 3: Electromagnetic Radiation
Interrelated electric and magnetic fields traveling through space
All electromagnetic radiation travels at c = 3108 m/s in vacuum – the cosmic speed limit!
  real number is 299792458.0 m/s exactly

## Slide 4: Examples of Electromagnetic Radiation
AM and FM radio waves (including TV signals)
Cell phone communication links
Microwaves
Infrared radiation
Light
X-rays
Gamma rays
What distinguishes these from one another?

## Slide 5: Wavelength (Frequency)

## Slide 6: The Electromagnetic Spectrum
Relationship between frequency, speed and wavelength
f · = c
f is frequency,  is wavelength, c is speed of light
Different frequencies of electromagnetic radiation are better suited to different purposes
The frequency of a radio wave determines its propagation characteristics through various media

## Slide 7: Generation of Radio Waves
Accelerating charges radiate EM energy
If charges oscillate back and forth, get time-varying fields
E
+
+
+



+










## Slide 8: Generation of Radio Waves
If charges oscillate back and forth, get time-varying magnetic fields too.
Note that the magnetic fields are perpendicular to the electric field vectors
B
+
+
+



+










## Slide 9: Polarization of Radio Waves
B
E
Transmitting
antenna

## Slide 10: Reception of Radio Waves
Receiving antenna works best when ‘tuned’ to the wavelength of the signal, and has proper polarization
Electrons in antenna are “jiggled”
by passage of electromagnetic wave
B
E
Optimum antenna length is /4: one-quarter wavelength

## Slide 11: Encoding Information on Radio Waves
What quantities characterize a radio wave?
Two common ways to carry analog information with radio waves
  Amplitude Modulation (AM)
  Frequency Modulation (FM): “static free”

## Slide 12: AM Radio
Amplitude Modulation (AM) uses changes in the signal strength to convey information
pressure modulation (sound)
electromagnetic wave
modulation

## Slide 13: AM Radio in Practice
Uses frequency range from 530 kHz to 1700 kHz
  each station uses 9 kHz
  spacing is 10 kHz (a little breathing room)  117 channels
  9 kHz of bandwidth means 4.5 kHz is highest audio frequency that can be encoded
    falls short of 20 kHz capability of human ear
Previous diagram is exaggerated:
  audio signal changes slowly with respect to radio carrier
    typical speech sound of 500 Hz varies 1000 times slower than carrier
    thus will see 1000 cycles of carrier to every one cycle of audio

## Slide 14: FM Radio
Frequency Modulation (FM) uses changes in the wave’s frequency to convey information
pressure modulation (sound)
electromagnetic wave
modulation

## Slide 15: FM Radio in Practice
Spans 87.8 MHz to 108.0 MHz in 200 kHz intervals
  101 possible stations
  example: 91X runs from 91.0–91.2 MHz (centered at 91.1)
Nominally uses 150 kHz around center
  75 kHz on each side
  30 kHz for L + R (mono)  15 kHz audio capability
  30 kHz offset for stereo difference signal (L - R)
Again: figure exaggerated
  75 kHz from band center, modulation is > 1000 times slower than carrier, so many cycles go by before frequency noticeably changes

## Slide 16: AM vs. FM
FM is not inherently higher frequency than AM
  these are just choices
  aviation band is 108–136 MHz uses AM technique
Besides the greater bandwidth (leading to stereo and higher audio frequencies), FM is superior in immunity to environmental influences
  there are lots of ways to mess with an EM-wave’s amplitude
    pass under a bridge
    re-orient the antenna
  no natural processes mess with the frequency
    FM still works in the face of amplitude foolery

## Slide 17: Frequency Allocation

## Slide 18: Converting back to sound: AM
AM is easy: just pass the AC signal from the antenna into a diode
  or better yet, a diode bridge
  then use capacitor to smooth out bumps
    but not so much as to smooth out audio bumps
B
D
radio signal
amplifier/
speaker

## Slide 19: Converting back to sound: FM
More sophisticated
  need to compare instantaneous frequency to that of a reference source
  then produce a voltage proportional to the difference
  Compute L = [(L+R) + (L-R)]/2; R = [(L+R) - (L-R)]/2
  amplify the L and R voltages to send to speakers
Amplification is common to both schemes
  intrinsic signal is far too weak to drive speaker

## Slide 20: Assignments
HW5: 12.E.24, 13.E.13, 13.E.15, 13.E.16, 13.P.7, 13.P.9, 13.P.11, plus additional required problems available on website