## Slide 1: Radio Propagation
Spring 07
CS 527 – Lecture 3

## Slide 2: Overview
Motivation
Block diagram of a radio
Signal Propagation
  Large scale path loss
  Small scale fading
Interesting link measurement observations
Implications of protocol design

## Slide 3: Motivation for Wireless propagation
Wireless channel is vastly different from wired counterpart
  Different access mechanisms
    Common channel but …
      State of channel at each node can vary drastically
      E.g.: Sender thinks that channel is free but receiver senses a busy channel – Packet drop?
  Unreliable channel
    Highly sensitive to environment (surroundings) and weather
  Modest bandwidth
Effects of Propagation has a high impact on higher layer protocols
  E.g.: Are the assumptions made by TCP protocol valid under wireless channel?

## Slide 4: Radio Block Diagram
In today's class:
  How does the signal propagate? What are the prominent effects?
Coding
Modulation
Antenna
Demodulation
Decoding
Antenna

## Slide 5: Signal Propagation Effects
Large scale Path loss
  Large distances (w.r.t. to wavelength of the wave) between transmitter and receiver
Small scale Fading
  Fluctuation in received signal strengths due to variations over short distances (w.r.t. to wavelength of the wave)
Consider the wavelength of radio signals for 802.11
  802.11 a: Frequency = 5.2 GHz Wavelength = 5.8 cm
  802.11 b/g: Frequency = 2.4 GHz Wavelength = 12.5 cm

## Slide 6: Large scale Path loss
General Observation:
  As distance increases, the signal strength at receiver decreases
Free-space Propagation model:
  Line-of-Sight (LoS) based
  E.g.: Satellite Communication, Microwave LoS Radio Links
  Signal strength observed at receiver is inversely proportional to square of distance

## Slide 7: Is it so simple?
But in realistic settings, lot of factors act on the wave
Three major reasons:
  Reflection:
  From objects very
  large (wrt to wavelength
  of the wave).
  Diffraction:
  From objects that have
  sharp irregularities.
  Scattering
    From objects that are small (when compared to the wavelength)
    E.g.: Rough surfaces
Figures borrowed from [1]

## Slide 8: Accounting for Ground Reflection
Two-ray (Ground reflection) model
  Considers LoS path + Ground reflected wave path
θi
θo
ELOS
Ei
Eg
ETOT = ELOS +
Eg
Transmitter
Receiver
Figures partially borrowed from [Rappaport]

## Slide 9: Empirical models
Above models are very simplistic in realistic settings
    E.g: Points 4 and 5 in the above figure
Alternative Approach:
  Use empirical data to construct propagation models
  But, can measurements at few places generalize to all scenarios?
    Different environments?
    Different frequencies?
  Recognize "patterns" in the empirical data and use statistical techniques for approximating.
Figures borrowed from [1]

## Slide 10: Empirical Models
Log-distance Path loss model
  Uses the idea that both theoretical and empirical evidence suggests that average received signal strength decreases logarithmically with distance
  Measure received signal strength near to transmitter and approximate to different distances based on above “reference” observation
Log-normal shadowing
  Observes that the environment can be vastly different at two points with the same distance of separation.
    Empirical data suggests that the power observed at a location is random and distributed log-normally about the “mean” power

## Slide 11: Small scale fading
Rapid fluctuations of the signal over short period of time
Invalidates Large-scale path loss
Occurs due to multi-path waves
  Two or more waves (e.g: reflected/diffracted/scattered waves)
  Such waves differ in amplitude and phase
  Can combine constructively or destructively resulting in rapid signal strength fluctuation over small distances
Example of Multipath
Phase difference between
original and reflected wave
Figures borrowed from [http://www.iec.org/online/tutorials/smart_ant/topic05.html]

## Slide 12: Factors affecting fading
Multipath propagation
Speed of mobile/surrounding objects
  The frequency of the signal varies if relative motion between transmitter and receiver
  E.g: The difference of sound heard when train is moving towards you or away from you
Transmission bandwidth
Discussion related to Lecture-2:
  Does mobility increase/decrease the throughput while thinking about mobile computing?
    Large scale/ Small scale?
Figures borrowed from [http://www.glenbrook.k12.il.us/GBSSCI/PHYS/CLASS/waves/u10l3d3.gif]

## Slide 13: Link measurement observations
Is propagation disk shaped?
  Directionality due to environment?
Does it observe Free-space Propagation model?
Figure 1 borrowed from [Aguayo – Link level measurements in 802.11b mesh network]
Figure 2 borrowed from [Deepak Ganesan -- Complex]
Figure 2: Contour of probability
of packet reception wrt distance
Figure 1: SNR values v/s distance
Distance v/s observed signal strength

## Slide 14: Link measurement observations
Shows packet reception rates of 4 different links
Temporal variations over a long time period (96 hours) is significant
  Note: This is not the signal strength, but packet reception rate (broadcast packet)
Figure borrowed from [Cerpa – Temporal]
Temporal variations

## Slide 15: Impact of protocol design
MAC protocol
  Constant retransmissions needed
  Neighborhood discovery
  More problems when we consider asymmetry of links
    Source can talk to receiver but not vice-versa
      ACKs?
Routing protocol
  Multi-hop reliability is low after 4 to 5 hops
    Consider 5 links each with packet-throughput 95%. Overall throughput (assuming no ACK) is 95%. Overall throughput (assuming no ACK) is ~77%.
Transport protocol
  Effect of unpredictable packet losses on TCP?
And other effects like packet delivery success based on relative motion between transmitter and receiver
  Multipath effects?