## Slide 1: MINISTORY OF SCIENCE AND TECHNOLOGY DEPARTMENT OF TECHNICAL AND VOCATIONAL EDUCATION
ME – 2014
STRENGTH OF MATERIALS(1)
A.G.T.I (Second Year)
Prof. U Kyaw San
Department of Mechanical Engineering.
Y.T.U

## Slide 2: Scope of Presentation
Direct Stress
Load, Stress and Strain, Hook’s law ,
Principal of Superposition & Example Problems
Tensile Test , Factor of Safety
Strain Energy, Resilience & Example Problems
Impact Loads & Example Problems
Varying Cross-section and Loads & Example Problems
Strain Energy , Resilience & Example Problems
Compound Bars & Example Problems
Temperature Stresses & Example Problems
Chapter 1
- 2 -

## Slide 3: Chapter 2
Shear Stress
Shear stress
Shear Strain
Modulus of Rigidity
Shear Strain Energy
Example Problems
- 3 -

## Slide 4: Chapter 1
1.1 Load
Typical loading types are
Static load or dead load ,ie non-fluctuating load, generally caused by gravity effects.
Live load as produced by, for example lorries crossing a bridge
Impact or shock load caused by sudden blows
Fatigue, Fluctuating or alternating loads, the magnitude and sign of the load changing with time
The simplest type of load is
Direct push or pull , known as tension or compression
Units newton (N) , kilonewton (kN) , meganewton (MN)
- 4 -

## Slide 5
1.2 Stress
P
P
tensile force
compression force
P
P
force ( pull)
Tensile stress = ----------------------------
Cross-sectional area
force ( push)
Compression stress = ----------------------------
Cross-sectional area
- 5 -

## Slide 6: 2.3 Strain
Bar in tension
P
P
P
P
l
x
P
P
l
x
- 6 -

## Slide 7: Example 2 ( Page-11 in ME 2014)
P
P
l
x
Given data
Tensile load P = 15,000 kg
Steel rod diameter, d = 2 cm
To find
stress
Calculation
- 7 -

## Slide 8: Example 4 ( Page 12 in ME 2014 )
P
P
l
x
Given data
A wire , Tensile strain  = 0.0002
Elongation x = 0.75 mm
To find
Length of wire l
Calculation
- 8 -

## Slide 9: 1.4 Hook’s law, Principal of superposition
Hook’s law
stress ( load)  strain (extension)
Substituting  = P / L and  = x / L
Principal of superposition
The effect of a system of forces acting on a body is equal to the sum of the effects
these same forces applied.
L
x
P
Strain ( elongation)
Stress
(load)
Stress – strain graph
- 9 -

## Slide 10: Example 5 ( Page-12 ~13 in ME 2014 )
A
B
C
5 m
x
10 tonnes
100
P = 10 x1000 kg
50
50
PCA
PCB
x
y
Given data two steel rods
Length l = 5 m
Working stress  = 560 kg/cm2
E = 2.1 x 106 kg/cm2
To find
Diameter of rod d = ?
Elongation x =?
Calculation
Fx = 0 gives PCA = PCB
Fy = 0 gives 10,000 kg = 2 x PCA cos 50 PCA = 77778.62 kgs
- 10 -

## Slide 11: Example 6 ( Page-14 ~15 in ME 2014 )
A
B
C
D
10000 lb
9000 lb
2000 lb
3000 lb
2 ft
3 ft
4 ft
1
2
3
1
2
3
10000 lb
(applied)
9000 lb
(applied)
10000 lb
9000 lb
B
B
C
C
3000 lb
(applied)
2000 lb
(applied)
Action from 1 , 10000 lb
9000 lb ( action from 3 )
7000 lb ,Resultant
Resultant 7000 lb
Given data
A steel bar
cross-sectional area = 1 in2
forces are shown in figure
E = 30 x 106 lb/in2
To find
The stresses
in each portion = ?
total elongation = ?
Similarly CD = 9000 lb / in2 ,xCD = + 0.0144 in
Total elongation = xAB + XBC + xCD = + 0.0308 in
- 11 -

## Slide 12: 1.3 Tensile Test
Universal tensile testing machine
Specimen and extensometer
- 12 -

## Slide 13
A – Proportional limit
B – Elastic limit
C – Upper yield point
D – Lower yield point
E – Ultimate limit
F - Fracture point
- 13 -

## Slide 14: Example 7 ( Page-24 in ME 2014 )
Given data A tensile test result
a mild steel specimen d = 2 cm
gauge length l = 4 cm
At the limit of proportionality, PA = 80000 N
the extension , xA = 0.048 mm
Yield load, PC = 85000 N
The maximum load PE = 150000 N
After bring broken , gauge length l’ =5,56 cm
at the neck, dia. d’ = 1.58 cm
To find Young ‘s modulus = E =?
The stress at the proportionality = ?
The yield stress = ?
Ultimate stress = ?
Percentage elongation and contraction =?
Solution
Cross-sectional area A = /4 X 22 = cm2
- 14 -

## Slide 15: Example 8 ( Page-26 in ME 2014 )
I cm
Wall thickness
60 tonnes compression load
A short hollow
Cast iron cylinder
d
D
Given data
P= 60 tonnes
ultimate crushing stress = 5400 kg/cm2
factor of safety = 3
To find
Outside diameter , D = ?
Calculation
d = D - 2
1 cm , thickness
P
P
- 15 -

## Slide 16: 1.10 Impact loads ( Page-30 in ME 2014 )
L
h
x
W
Area, A
Weight = W
Falling height = h
Maximum instantaneous tensile stress = I
Equivalent load = P
Maximum instantaneous extension = x
Assuming the stress induced does not exceed
the elastic limit
Loss of potential energy of weight = Gain of strain energy of rod
= Strain energy stored in rod
W ( h +x ) = ½ x Pi X where x = i L / E
Pi = I A
Induced tensile stress in the rod
Where W in N , h & L in mm , A in mm2 and E in N/mm2
- 16 -

## Slide 17: Example 11 ( Page-34 in ME 2014 )
L
h
x
W
Area, A
Given data
W = 100 kg = 9.81 x 100 N
d = 2 cm = 20 mm
L = 3 m = 3000 mm
h = 4 cm = 40 mm
E = 205,000 N/mm2
To find
Maximum stress set up I = ?
Solution
A =  (d/2)2
=  x 102 mm2
1 = 132.92 N/mm2
- 17 -

## Slide 18: 1.11 Varying cross-section and loads
P
P
L1
L2
L3
d1
d2
d3
1
2
3
Loads P = P1 = P2 = P3
P = 1 A1 = 2 A2 = 3 A3
The changes in length
The total changes of length = x1 + x2 + x3
- 18 -

## Slide 19: Example 12 ( Page-36 in ME 2014 )
P
P= 10000 lb
L1= 6ft
L2= 12ft
L3= 6 ft
d1 =1 1/8 in
d2=1in
d3=1 ¼ in
1
2
3
Given data
A wrought iron bar
d1 = 1 1/8 in
L1 = 6 ft = 6 x 12 in
d2 = 1 in
L2 = 12 ft = 12 x 12 in
d3 = 1 ¼ in
L3 = ( 24 – 6 – 12 ) = 6 ft = 6 x 12 in
E = 28 x 106 lb/in2
P = 10,000 lb
Solution
To find
The total change in length =?
The energy stored in the bar =?
- 19 -

## Slide 20: 1.11 Compound bars ( Page 37 in ME-2014)
P
P
Rod A
Tube B
LA = LB
Rigid two plates
Equilibrium equation
P = PA + PB …… (1)
P = A AA + B AB
Compatibility equation
(strain equation) xA = xB ….. (2)
A LA =  B LB
A = B
- 20 -

## Slide 21: Example 13 ( Page 39 in ME 2014)
P = 100 tons
Concrete column
4 steel rods
d = 1 in
A
A
Section A -A
18 in
18 in
Given data
Concrete column 18 x 18 in. square
4 steel rods d = 1 in.
EC = 2 x 106 lb/in2 ,ES = 30 x 106 lb/in2
Load P = 100 tons
= 100 x 2240 lbs
To find
S = ? , C = ?
Solution
Area of steel rod , AS = 4 x (/4) x d2
= 3.14 in2
Net area of concrete AC = 18 x 18 – 3.14
= 320.86 in2
For compound bar P = S AS + C AC
224000 = S x 3.14 + C x 320.86 eq.(1)
From equations (1) and (2), C = 608 lb/in2 , S = 9120 lb/in2 (Ans)
- 21 -

## Slide 22: 1.12 Temperature stresses ( P-41 in ME- 2014 )
Brass
Steel
Steel
L
B L t
S L t
Extension of steel. XS
Compression
of brass, xB
Final position of
Compound bar
Original position of
Compound bar
Free expansion
due to temp. rise. t
For compound bar
Subjected to a change of temperature t
Let B = compressive stress induced
in the bar due to rise in trmp. T
xB = compression of bar dur to trmp. change
Similarly
XT
Strain equation
XT = S L T + xS for steel rod
xT = S L T - xS for copper cube
xS + X B = L T (B - C )
Equilibrium equation
PS = PB
S AS = B AB
-22 -

## Slide 23: Example 15 ( Page-45 in ME 2014 )
Given data
A steel rod dS = 25 mm
A brass tube external dia. DB = 35 mm
internal dia. dB = 25 mm
Induced stress in steel due to tighten initially
S = 100 kg/cm2
Temperature rise t = 60C
To find
The final stresses in the rod and the tube
Solution
Induced stress in steel due to tighten initially
S1 = 100 kg/cm2 , tension ( given)
Equilibrium equation S1 AS = B1 AB where AS = /4 x 2.52 = 4.91 cm
and AB = /4 (3.52 -2.52) = 4.71 cm2
100 x 4.91 = B x 4.71
B1 = 104.25 kg/ cm2 , compression
Due to rise in temperature t = 60 C
Equilibrium equation P = S2 x AS = B2 x AB
S2 x 4.91 = B2 x 4.71 eq(1)
Strain equation
From equation (1) & (2)
S2 =5391.99 kg/cm2 (Tensile)
B2 = 6185.6 kg/cm2 ( comp)
Final stresses
S= S1+S2= 6031.99 kg/cm2
( tensile)
B= B1+B2=6289.85 kg/cm2
(compressive)
- 23 -

## Slide 24: CHAPTER 2 Shear Stress
2.2 Shear strain
Ø
Shear strain  Ø
2.3 Modulus of rigidity
2.4 Shear strain energy
Strain energy ( U) = Work done in straining
= ½ ( final couple ) x ( Angle turned through
U =(2/2 G ) x volume
L
M
- 24 -

## Slide 25: Example 2 ( Page-36 in ME 2014 )
1.4 cm
d=10 cm
P
Weight support
shaft
collar
Given data
A solid circular shaft and collar
The ultimate shear stress = 3 tonnes / cm2
Factor of safety N = 3
To find
The greatest compressive load P =?
Tthe maximum stress on the shaft = ?
Solution
Shearing area in collar Acollar =  d t =  x 10 x 1.4 cm2
- 25 -

## Slide 26: Example 3 ( Page-57 in ME 2014 )
Circle dia.
d = 14 cm
Coupling
bolt
shaft
Power 250 kW, 1000 rpm
Given data
Transmit power P =250 kW
rpm = 1000
No of bolts n = 6
Pitch circular dia = 14 cm
Allowable shear stress bolt =75 N/cm2
To find
diameter of bolt = ?
P
P
P
P
P
P
T
- 26 -

## Slide 27: Example 6 ( Page-62 in ME 2014 )
1 m
4 cm diameter shaft
P
W
Key width = 1.25 cm
Given data
A shaft diameter = 4 cm
A key width = 1.25 cm
length = 5 cm
Allowable shear stress key = 650 kg/cm2
Lever arm distance = 1 m
To find
Applied force W = ?
Solution
Key shearing area A = width x key length
A key = 1.25 x 5 cm2
d
- 27 -

## Slide 28: Example 7 ( Page-65 in ME 2014 )
Given data
diameter of rod d = 5 cm
Thickness of cotter = 1.25 cm
Permissible stress
tension stress T = 300 N/mm2
shear stress in member mem = 150 N/mm2
shear stress in cotter cot = 225 N/mm2
crushing stress  = 450 N/mm2
To find
Required diameters in the joint shown
Solution
Shear of cotter
225 = 588,000 / ( 2 e x 12.5 )
e = 105 mm eq(2)
Shear of right –hand member
150 = 588,000 / 4 ab
Ab = 980 mm eq(3)
Shear of left–hand member
150 = 588,000 / 2 ch
Ch = 1960 mm eq(4)
Crushing between right-hand member and cotter
450 = 588,000 / ( 2 a x 12.5 )
a = 52.4 mm eq(5)
P = 300 N/mm2 x (  / 4 ) x 502 = 588000 N eq (1)
From equation(3)
b = 18.7 mm
Crushing between left-hand member and cotter
450 = 558,000 / ( 12.5 x h )
h = 104.8 mm
From equation(4)
C = 18.7 mm
- 28-

## Slide 29
THANK YOU VERY MUCH