## Slide 1
MINISTRY OF SCIENCE AND TECHNOLOGY DEPARTMENT OF TECHNICAL AND VOCATIONAL EDUCATION ME- 01034 A.G.T.I (First Year) MECHANICAL ENGINEERING FUNDAMENTAL Daw Myint Myint Lwin Department of Mechanical Engineering (Y.T.U)

## Slide 2
Chapter 1
Thermodynamics deals with relations between the properties of a substance and the quantities ‘work’ and ‘heat’ witch cause of state.
Properties and state
Any characteristic of a substance which can be observed or measured is called a Property of the substance.
Pressure, volume and temperature, witch are dependent upon the physical and chemical structure of the substance, are called INTERNAL or THERMODYNAMIC properties. Temperature and pressure, which are independent of mass are called INTENSIVE properties.
volume and energy in its various forms, which are dependently upon mass, are called EXTENSIVE properties.

## Slide 3
Phase
Matter can exist in three phases, solid, liquid and vapour (or) gas. If the matter in only one of these forms then it is in a Single Phase. If two phases exist together then the substance is in the form of a TWO PHASE MIXTURE.
Process
A substance is said to have undergone a Process:
When the state of the substance is changed by means of an operation such as the conversion of water into steam; or
Operations are carried out on the substance; e.g. the expansion or compression of a gas.
Cycle
If processes are carried out on a substance such that, at the end, the substance is returned to its original state, then the substance is said to have been taken through a Cycle.
A sequence of events takes place which must be repeated and repeated. In this way the engine continues to operate.
Each repeated sequence of events is called a Cycle.

## Slide 4
The System
When the same matter remains within the region throughout the process and only work and heat across the boundary, it is called a Closed System.
In an Open System, matter may flow across the boundary, in addition to work and heat.
System
Energy leaving
Energy entering
Surroundings
Boundary can
Change shape
Fixed mass
System
Energy leaving
Surroundings
Mass leaving
Energy entering
Mass leaving
Boundary can
Change shape

## Slide 5
Internal energy (U)
Internal energy is the store of energy which results from the motion of the atoms and molecules of a body. Specific internal energy is desingnated u.
Enthalpy (H)
Internal energy pressure and volume are properties. So is their combination in the form,
h = u + PV
Work (W)
If a system exists in which a force at the boundary of the system is moved through a distance, the work is done by or on the system
Heat (Q)
During an energy transfer process which results from the temperature difference, the energy transferred is called HEAT.

## Slide 6
Specific Head Capacity (c)
The specific heat capacity of a substance is defined as the amount of heat which transfers into or out unit mass of the substance while the temperature of the substance changes by one degree. Thus,
Q = mc (t2 – t1)
Where, c = specific heat capacity of substance
t1 = original temperature of substance
t2 = final temperature of substance
Q = heat transferred to produce change
Ex. 5kg of steel, specific heat capacity 480 J/kgK, is heated from 15C to 100  C. How much heat is required?
Heat required = m c (t2-t1)
= 5 x 480 x (100 -15)
= 5 x 480 x 85
= 204000 J = 204 kJ

## Slide 7
Heat Engine
Work, W = QA – QR
Efficiency  = Output
Input
Source
Engine
Sink
QA
W
QR
Heat addition to engine
CV = calorific value (J/kg)
QA = m x CV

## Slide 8
Ex(1.2) = 20.4 Kg/hr
CV = 43 MJ/kg = 43 x 106 J/kg
 = 20 % = 0.2
Power output = ?
Energy rejected = ? (by min)
QA = m x CV
= 20.4 x 43 x 106
= 877.2 x 106 J/h
QA =
= 0.2436 MW
=
W = 0.2 x 0.2436 x 10
= 0.05 x 10
= 0.05 MW (Ans)
W = QA - QR

## Slide 9
QR= 0.2436 – 0.04872
= 0.19488 MJ/s
= 0.19488 x 60
= 11.688 MJ/min
The Steady Flow Energy Equation (S.F.E.E)
P1, V1, C1
z1
z2
P2, V2, C2
leaving
entering
W
Q
Entering Leaving
P1 = Pressure P2 = Pressure
V1 = Specific volume V2 = Specific volume
C1 = velocity C2 = velocity

## Slide 10
Potential energy (PE) Internal Energy (u)
PE = mg z (kg – m/s2 – m) = J
PE = gz J/kg (for unit mass)
Kinetic energy (KEJ) Flow Work energy
KE = ½ mv2 W = Pv (N/m2 x m3/kg =J/kg)
= ½ mc2 (kg x m2/s2 = J)
= ½ C2 J/kg
The Steady flow energy equation
Entering = leaving
PE1 + KE1 + FW1 + IE1 + (Q) = PE2 + KE2 + FW2 + IE2 + W
gz1 + + P1v1+ U1 = gz2 + + P2v2+ U2 + W

## Slide 11
gz1 + + h1 + Q = + + h2 + W
Eg.(1.2) C1 = 16 m/s C2 = 37 m/s
h1 = 2990 k J/kg h2 = 2530 kJ/kg
Q = -25 kJ/kg m = 324000 kg/h
W = ? (kW)
gz1 + + h1 + Q = gz2 + + h2 + W
W = Q + + (h1 – h2)
= -25 + + (2990 – 2530)
= 434.443 kJ/kg

## Slide 12
W (kW) = 434.4435 x m
= 434.4435 x
= 3909.915 kW (Ans)
Non-flow energy equation (close system)
gz1 + + P1v1 + U1 + Q = gz2 + + P2v2 + U2 + W
U1 + Q = U2 + W
Q = (U2 – U1) + W
Q = W + U

## Slide 13
Chapter 2
Boyle’s Law
PV = C if T = constant
P1V1 = P2V2 m = constant
Charle’s Law
= c If p = constant
= m = constant
The characteristic equation of a perfect gas
During a change of state of any gas in which neither pressure, volume nor temperature remain constant, the change of state from 1 to 2 is equivalent to a Boyle’s Law change from 1 down to some intermediate state A and then a charle’s law change to the final condition 2.

## Slide 14
(1)

V
PV = C
Boyle’s Law change
1
A
2
Charles’ law change
(A)

## Slide 15
(A)
where 3 and 4 represent other new conditions of state of the same mass of gas
(2)

## Slide 16
If follow that for any fixed mass of gas, changes of state are connected by the equation
Let v = the specific volume = vol. of 1kg of gas
when 1kg of gas is considered this constant is written R and is called the characteristic gas constant.
for 1 kg of gas
For mkg of gas

## Slide 17
This is known as the characteristic equation of a perfect gas.
R = 0.287 KJ/Kg-k for air
Thermodynamic process
constant volume process (V = C)


(1)
(2)
(1)
(2)
V =C (cooling)
V =C (heating)
V
V

## Slide 18
(2) Work done (W)
W = 0
heat (Q)
CV = specific heat capacity at constant volume.
Change of internal energy (U)
® for any process
non flow energy equation
Constant pressure process (P = C)

  V
  2
  1
  P=C (heating)

  V
  1
  2
  P=C (cooling)
Q=W+U
 U=mcv(T2-T1)

## Slide 19
(1) P, V, T relation
(2) Work done W
W = (V2 – V1) P (or) W = mR (T2-T1)
(3) heat (Q)
Q = mcp (T2 - T1)
(4) Change of internal energy (DU)
DU = mcv (T2 - T1)
Q = W + DU

## Slide 20
Polytropic process
(1) P,V,T reaction
(2) Work done (W)
(3) Change of internal energy (DU)
DU = mcv (T2 – T1)
(4) heat (Q)
Q = W + DU


(2)
(1)
(2)
(1)
expansion
compression
V
V

## Slide 21
Ex 2.2
V1 = 0.015 m3 V2 = 0.09m3
T1 = 285 + 273 = 558K T2 = ?
V2 = 0.09m3
T2 = 298.0446 K
Adiabatic process


(2)
(1)
(2)
(1)
expansion
compression
Q = 0
r = k
V
V

## Slide 22
(1) P,V,T reaction
(2) Work done (W)
(3) heat (Q)
Q = 0
(4) Change of internal energy (DU)
DU = mcv (T2 – T1)
W = - DU, R = Cp – Cv, r =

## Slide 23
EX 2.3 Pg -13
P1 = 700 KN/m2 P2 = 140KN/m2
V1 = 0.015 m3
V2 =?
W =?
DU = ?, CP = 1.046 KJ/Kgk
CV = 0.752 KJ/Kgk

## Slide 24
V2 = 0.048 m3
W = 9.692 KJ
Q = 0
Q = W + DU
DU = -9.692 KJ
Isothermal Process


(2)
(1)
(2)
(1)
T = C
PV = C
PV= C,T=C
DU = 0
expansion
V
V

## Slide 25
(1) P,V,T relation
PV = C
P1V1 = P2V2
(2) Work done (W)
(3) Change of internal energy (D U)
D U = mcv (T2 – T1)
D U = 0
(4) heat (Q)
Q = W Q = W + DU

## Slide 26
EX 2.4, Pg 14
V1 = 0.3m3
P1 = 100 KN/m2
T1 = 20 + 273
= 293K
V3 = V1
= 0.3m3
(b) DU2-3 = ?
(c) m = ?
(a) Q1-2 = ?
PV = C
Q = W + DU
P2V2 = P1V1
V2 = 0.06m3
W = -48.28 KJ
Q = -48.28 KJ
1
3
2

PVr= C
PV= C
V
PVr= C

## Slide 27
r = 1.4
CP = 1KJ/Kg-K
CV = 0.714
m = 0.358Kg
= 35.6 Kg
Q = W + D U
D U = -35.6 Kg

## Slide 28
Thank You