## Slide 1
Baseline wandering - a receiver will evaluate the average power of the received signal (called the baseline) and use that to determine the value of the incoming data elements. If the incoming signal does not vary over a long period of time, the baseline will drift and thus cause errors in detection of incoming data elements.
A good line encoding scheme will prevent long runs of fixed amplitude.
Considerations for choosing a good signal element referred to as line encoding

## Slide 2: DC components - when the voltage level remains constant for long periods of time, there is an increase in the low frequencies of the signal. Most channels are bandpass and may not support the low frequencies. This will require the removal of the dc component of a transmitted signal.
Line encoding C/Cs