## Slide 1
Low Buildings. Figure 3.4a illustrates the application of diagonal bracing to a
low, industrial-type building. Bracing in the plane of the roof acts with the rafters,
ridge beam, and an edge roof beam as an inclined truss, which resists wind pressures
on the roof. Each truss transmits the wind load to the ends of the building.
Diagonals in the end walls transmit the load to the foundations. Wind pressure on the end walls is resisted by diagonal bracing in the end panels of the longitudinal
walls. Wind pressure on the longitudinal walls, like wind on the roof, is transmitted
to the end walls.
FIGURE 3.4 Bracing of low buildings: (a) diagonal bracing in roofs and walls; (b) isolated pairs
of shear walls in a T pattern; (c) service-core enclosure used as shear walls; (d ) shear walls at ends
of building and rigid frames in the perpendicular direction