## Slide 1
A stairway consists of a series of steps and landings. Each step consists of a
horizontal platform, or tread, and a vertical separation or enclosure, called a riser
(Fig. 1.9a). Railings are placed along the sides of the stairway and floor openings
for safety reasons. Also, structural members may be provided to support the stairs
and the floor edges. Often, in addition, the stairway must be enclosed for fire
protection.
Escalators, or powered stairs, are installed in such buildings as department
stores and transportation terminals, or in the lower stories of office buildings and
hotels, where there is heavy pedestrian traffic between floors. Such powered stairs
consist basically of a conveyor belt with steps attached; an electric motor for moving
the belt, and steps, controls, and structural supports.
Elevators are installed to provide speedier vertical transportation, especially in
tall buildings. Transportation is provided in an enclosed car that moves along
guides, usually within a fire-resistant vertical shaft but sometimes unenclosed along
the exterior of a building. The shaft, or the exterior wall, has openings, protected
by doors, at each floor to provide access to the elevator car. The car may be suspended on and moved by cables (Fig. 1.9b) or set atop a piston moved by hydraulic
pressure (Fig. 1.9c).
More information on vertical-circulation elements is given in Sec. 16.

## Slide 2
FIGURE 1.9 Vertical-circulation elements: (a) stairs; (b) electric traction elevator; (c) hydraulic elevator.