## Slide 1
Openings are provided in exterior walls for a variety of purposes, but mainly
for windows and doors. Where openings occur, structural support must be provided
over them to carry the weight of the wall above and any other loads on that portion
of the wall. Usually, a beam called a lintel is placed over openings in masonry
walls (Fig. 1.5a) and a beam called a top header is set over openings in woodframed
walls.
A window usually consists of transparent glass or plastics (glazing) held in place
by light framing, called sash. The window is fitted into a frame secured to the
walls (Fig. 1.5a). For sliding windows, the frame carries guides in which the sash
slides. For swinging windows, stops against which the window closes are built into
the frame.
Hardware is provided to enable the window to function as required. For movable
windows, the hardware includes grips for moving them, locks, hinges for
swinging windows, and sash balances and pulleys for vertically sliding windows.
The main purposes of windows are to illuminate the building interior with daylight,
to ventilate the interior, and to give occupants a view of the outside. For retail
stores, windows may have the major purpose of giving passersby a view of items
displayed inside. (See also Sec. 11.)
Doors are installed in exterior walls to give access to or from the interior or to
prevent such access. For similar reasons, doors are also provided in interior walls
and partitions. Thus, a door may be part of a system for enclosing a building or a
component of a system for enclosing interior spaces.