## Slide 1
3.4.3 Roof Drainage
Many roof failures have been caused by excessive water accumulation. In most cases, the overload that caused failure was not anticipated in design of those roofs, because the designers expected rainwater to run off the roof. But because of inadequate drainage, the water ponded instead.
On flat roofs, ponding of rainwater causes structural members to deflect. The
resulting bowing of the roof surface permits more rainwater to accumulate, and the additional weight of this water causes additional bowing and collection of even more water. This process can lead to roof collapse. Similar conditions also can occur in the valleys of sloping roofs.
To avoid water accumulation, roofs should be sloped toward drains and pipes
that have adequate capacity to conduct water away from the roofs, in accordance
with local plumbing codes.