## Slide 1
(a)
FIGURE 1.6 Examples of floor-ceiling and roof-ceiling systems. (a) Concrete structural slab
carries hollow-steel deck, concrete fill, and flexible tile flooring. (b) Acoustical-tile ceiling
incorporating a lighting fixture with provisions for air distribution is suspended below a floor.
(c) Insulated roof and steel beams are sprayed with mineral fiber for fire protection. (d) Insulated
roof and open-web joists are protected by a fire-rated suspended ceiling.

## Slide 2
Systems for Enclosing Interior Spaces. The interior of a building usually is compartmented
into spaces or rooms by horizontal dividers (floor-ceiling or roof-ceiling
systems) and vertical dividers (interior walls and partitions). (The term partitions is
generally applied to non-load-bearing walls.)
Floor-Ceiling Systems. The basic element of a floor is a load-carrying deck.
For protection against wear, esthetic reasons, foot comfort, or noise control, a floor
covering often is placed over the deck, which then may be referred to as a subfloor.
Figure 1.6a shows a concrete subfloor with a flexible-tile floor covering. A hollowcold-
formed steel deck is incorporated in the subfloor to house electric wiring.