## Slide 1
.10 BUILDING CODES
Many of the restrictions encountered in building design are imposed by legal regulations.
While all must be met, those in building codes are the most significant
because they affect almost every part of a building.
Building codes are established under the police powers of a state to protect the health, welfare, and safety of communities. A code is administered by a building official of the municipality or state that adopts it by legislation. Development of a local code may be guided by a model code, such as those promulgated by the International Conference of Building Officials, Inc.,
Building Officials and Code
Administrators International, Inc., and Southern Building Code Congress International,
Inc.

## Slide 2
Forms of Codes. Codes often are classified as specifications type or performance
type.
A specification-type code names specific materials for specific uses and specifies minimum or maximum dimensions, for example, ‘‘a brick wall may not be less than 6 in thick.’’ A performance-type code, in contrast, specifies required performance of a construction but leaves materials, methods, and dimensions for the designers to choose. Performance-type codes are generally preferred, because they give designers greater design freedom in meeting clients’ needs, while satisfying the intent of the code. Most codes, however, are neither strictly specifications nor performance type but rather a mixture of the two. The reason for this is that insufficient information is currently available for preparation of an entire enforceable performance code.

## Slide 3
The organization of building codes varies with locality. Generally, however, they
consist of two parts, one dealing with administration and enforcement and the other specifying requirements for design and construction in detail. specifying requirements for design and construction in detail.
Part 1 usually covers licenses, permits, fees, certificates of occupancy, safety,
projections beyond street lines, alterations, maintenance, applications, approval of drawings, stop-work orders, and posting of buildings to indicate permissible live loads and occupant loads.
Part 2 gives requirements for structural components, lighting, HVAC, plumbing,
gas piping and fixtures, elevators and escalators, electrical distribution, stairs, corridors, walls, doors, and windows. This part also defines and sets limits on occupancy and construction-type classifications. In addition, the second part contains provisions for safety of public and property during construction operations and for fire protection and means of egress after the building is occupied.

## Slide 4
Type of construction of a building is determined, in general, by the fire ratings
assigned to its components. A code usually establishes two major categories: combustible and noncombustible construction. The combustible type may be subdivided in accordance with the fire protection afforded major structural components and the rate at which they will burn; for example, heavy timber construction is considered slow-burning. The noncombustible type may be subdivided in accordance with the fire-resistive characteristics of components.
Building codes may set allowable floor areas for fire-protection purposes. The
limitations depend on occupancy group and type of construction. The purpose is
to delay or prevent spread of fire over large portions of the building. For the same
reason, building codes also may restrict building height and number of stories.
In addition, to permit rapid and orderly egress in emergencies, such as fire, codes limit the occupant load, or number of persons allowed in a building or room. In accordance with permitted occupant loads, codes indicate the number of exits of adequate capacity and fire protection that must be provided.