## Slide 1
4.40.3 Types of Carbon Steels
Most of the steel used for construction is low- to medium-carbon, relatively mild,
tough, and strong, fairly easy to work by cutting, punching, riveting, and welding.
Table 4.16 summarizes the most important carbon steels and low-alloy steels used
in construction as specified by ASTM.
The plain iron-carbon metals with less than 0.8% carbon content consist of
ferrite and pearlite and provide the low-carbon (0.06 to 0.30%), medium-carbon
(0.30 to 0.50%), and high-carbon (0.50 to 0.80%) steels called hypoeutectoid steels.
The higher-carbon or hypereutectoid tool steels contain 0.8 to 2.0% carbon and
consist of pearlite and cementite. The eutectoid steels occurring in the vicinity of
0.8% carbon are essentially all pearlite.
The American Iron and Steel Institute and the Society of Automotive Engineers
have designated standard compositions for various steels including plain carbon
steels and alloy steels.