## Slide 2
ceiling is suspended below a floor or roof for esthetic or other reasons. Figure 1.6b shows such a ceiling. It is formed with acoustical panels and incorporates a lighting fixture and air-conditioning inlets and outlets.
Metal and wood subfloors and beams require fire protection. Figure 1.6c shows
a roof and its steel beams protected on the underside by a sprayed-on mineral fiber.
Figure 1.6d shows a roof and open-web steel joists protected on the underside by a continuous, suspended, fire-resistant ceiling. As an alternative to encasement in or shielding by a fire-resistant material, wood may be made fire-resistant by treatment with a fire-retardant chemical.