## Slide 1
Joists are closely spaced to carry light loads.
Stringers support stairs.
Headers support structural members around openings in floors, roofs, and walls.
Purlins are placed horizontally to carry level roof decks.
Rafters are placed on an incline to carry sloping roof decks.
Girts are light horizontal members that span between columns to support walls.
Lintels are light horizontal beams that support walls at floor levels in multistory
buildings or that carry the part of walls above openings for doors and windows.
Girders may be heavily loaded beams or horizontal members that support other
beams (Fig. 1.3).
Spandrels carry exterior walls and support edges of floors and roofs in multistory
buildings.
Trusses serve the same purposes as girders but consists of slender horizontal,
vertical, and inclined components with large open spaces between them. The
spaces are triangular in shape. Light beams similarly formed are called openweb
joists (Fig. 1.6d).

## Slide 2
FIGURE 1.3 Structural-steel skeleton framing for a multistory building.
(Courtesy of the American Institute of Steel Construction.)