## Slide 1
FIGURE 1.5 Types of exterior wall construction: (a) concrete-block wall; (b) wood-framed wall; (c) precast-concrete curtain wall.

## Slide 2
Exterior walls enclose a building below the roof. The basis element in the walls
is a strong, durable, water-resistant facing. For added strength or lateral stability,
this facing may be supplemented on the inner side by a backing or sheathing (Fig.
1.5b). For esthetic purposes, an interior facing usually is placed on the inner side
of the backing. A layer of insulation should be incorporated in walls to resist
passage of heat.
Generally, walls may be built of unit masonry, panels, framing, or a combination
of these materials.
Unit masonry consists of small units, such as clay brick, concrete block, glass
block, or clay tile, held together by a cement such as mortar. Figure 1.5a shows a
wall built of concrete blocks.
Panel walls consist of units much larger than unit masonry. Made of metal,
concrete, glass, plastics, or preassembled bricks,