## Slide 1
11.14 STUD-WALL CONSTRUCTION
Load-bearing and non-load-bearing stud walls may be built of wood, aluminum, or cold-formed steel. Basic framing consists of vertical structural members, or studs, seated on a bottom, horizontal, bearing member, called a sole plate, and capped with a horizontal tie, called a top plate (Fig. 11.16). In addition, diagonal and horizontal bracing may be applied to the framing to prevent racking due to hori- zontal forces acting in the plane of the wall.
The studs usually are spaced 16 or 24 in on centers. Traditional surfacing ma- terials are manufactured to accommodate these spacings; for example, panels to be attached to the framing usually come 48 in wide. (Inasmuch as the panels are fastened to each stud, panel thickness required, and hence cost, is determined by the stud spacing and generally is larger for 24-in spacing than for 16-in. Overall wall cost, however, may not be larger for the wider spacing, because it requires fewer studs.)
FIGURE 11.16
Stud-wall construction incorporating
a window opening.