## Slide 1
11.44 WINDOW SELECTION
Distribution and control of daylight, desired vision of outdoors, privacy, ventilation
control, heat loss, and weather resistance are all-important aspects of good design
principles. Most building codes require that glass areas be equal to at least 10% of
the floor area of each room. Nevertheless, it is good practice to provide glass areas
in excess of 20% and to locate the windows as high in the wall as possible to
lengthen the depth of light penetration. Continuous sash or one large opening in a
room provides a more desirable distribution of light than separated narrow windows.
Either arrangement eliminates the dark areas between openings.
Location, type, and size of window are most important for natural ventilation.
The pattern of air movement within a building depends to a great extent on the
angle at which the air enters and leaves. It is desirable, particularly in summer, to
direct the flow of air downward and across a room at a low level. However, the
type and location of windows best suited to ventilation may not provide adequately
for admission of light and clear vision, or perhaps proper weather protection. To
arrive at a satisfactory relationship, it may be necessary to compromise with these
functional requirements.
While building codes may establish a minimum percentage of glass area, they
likewise may limit the use of glass and also require a fire rating in particular
locations. In hazardous industrial applications subject to explosions, scored glass is
an added precaution for quick release of pressure.
Heat transmittance is of economic importance and can also affect comfort.
Weather stripping or the use of windows with integral frame and trim can minimize
air infiltration. Double glazing or heat-absorbing glazing makes large glass areas
feasible by materially reducing heat transmittance. Solar heating may be achieved
by placement of glass areas so that the rays of the sun can be admitted during the
winter.