## Slide 1
9.39 JOINTS IN CONCRETE
Several types of joints may occur or be formed in concrete structures:
Construction joints are formed when fresh concrete is placed against hardened
concrete.
Expansion joints are provided in long components to relieve compressive
stresses that would otherwise result from a temperature rise.
Contraction joints (control joints) are provided to permit concrete to contract
during a drop in temperature and to permit drying shrinkage without resulting
uncontrolled random cracking
FIGURE 9.8 Control joints for restraining temperature and shrinkage cracks: (a) vertical section through a slab on grade; (b) horizontal section through a wall.