## Slide 1
MASONRY WALLS
Masonry comprises assemblages of nonmetallic, incombustible materials, such as stone, brick, structural clay tile, concrete block, glass block, gypsum block, or adobe brick. Unit masonry consists of pieces of such materials, usually between 4 and 24 in in length and height and between 4 and 12 in in thickness. The units are bonded together with mortar or other cementitious materials.
Walls and partitions are classified as load-bearing and non-load-bearing. Differ- ent design criteria are applied to the two types.
Minimum requirements for both types of masonry walls are given in ANSI Standard Building Code Requirements for Masonry, A41.1 and ANSI Standard Building Code Requirements for Reinforced Masonry, A41.2, American National Standards Institute; Building Code Requirements for Engineered Brick Masonry, Brick Institute of America, and ACI Standard Building Code Requirements for Concrete Masonry Structures, ACI 531, American Concrete Institute.
Like other structural materials, masonry may be designed by application of en- gineering principles. In the absence of such design, the empirical rules given in this section and adopted by building codes may be used.
FIGURE 11.1 Brick exterior walls:
brick veneer with metal-stud framing;
(b) masonry- bonded hollow walls;
(c) hollow wall with metal ties between wythes;
(d ) insulated cavity wall.