## Slide 1
10.12.8 Wall Systems
Rated siding (panel or lap) may be applied directly to studs or over nonstructural fiberboard, or gypsum or rigid-foam-insulation sheathing. Nonstructural sheathing is defined as sheathing not recognized by building codes as meeting both bending and racking-strength requirements.
A single layer of panel siding, since it is strong and rack resistant, eliminates the cost of installing separate structural sheathing or diagonal wall bracing. Panel sidings are normally installed vertically (Fig. 10.8a), but most may also be placed horizontally (long dimension across supports) if horizontal joints are blocked (Fig.
10.8b). Maximum stud spacings for both applications are given in Table 10.20.
FIGURE 10.8 Wall built of wood
studs and APA Rated Siding panels.
(a) Vertical panel siding.
If permitted by the local building and
energy codes, no building paper is required
when paneledges are shiplapped, battened,
and caulked. If caulking is not used with
unbattened square buttjoints, apply a water
repellent to panel edges.
Caulk around windows and doors.
(b) Horizontal lap siding. Diagonal bracing or
other code-approved bracing methods for
the wall should be provided.
For engineered shear-wall segments,
use APA Rated Sheathing under
the lap siding.
(c) Siding joint details at a window.