## Slide 1
11.22 TYPES OF PARTITIONS
Bearing partitions may be built of masonry or concrete or of wood or light-gage
metal studs. These materials may be faced with plaster, wallboard, plywood, wood
boards, plastic, or other materials that meet functional and architectural requirements.
Masonry partitions should satisfy the requirements of Arts. 11.2 to 11.12.
See also Art. 11.14.
Nonbearing partitions may be permanently fixed in place, temporary (or movable)
so that the walls may be easily shifted when desired, or folding. Since the
principal function of these walls is to separate space, the type of construction and
materials used may vary widely. They may be opaque or transparent; they may be
louvered or hollow or solid; they may extend from floor to ceiling or only partway;
and they may serve additionally as cabinets or closets or as a concealment for
piping and electrical conduit.

## Slide 2
11.23 STRUCTURAL REQUIREMENTS
OF PARTITIONS
Bearing partitions should be capable of supporting their own weight and superimposed
loads in accordance with recommended engineering practice and should rest
in turn on adequate supports that will not deflect excessively. Masonry partitions
should meet the requirements of Arts. 11.2 to 11.12.
Nonbearing partitions should be stable laterally between lateral supports or additional
lateral supports should be added. Since they are not designed for vertical
loads other than their own weight, such partitions should not be allowed to take
loads from overhead beams that may deflect and press down on them. Also, the
beams under the partition should not deflect to the extent that there is a visible
separation between bottom of partition and the floor or that the partition cracks.