## Slide 1
1.2 Railways
While the railways found themselves in a monopoly position up to the twentieth-century, with the advent of the combustion engine and the jet engine they had to face strong competition in the form of buses, cars and aeroplanes.
Mass motorization after World War II expressed by the growing prosperity brought about many prob- lems, especially in densely populated areas: lack of space, congestion, lack of safety, emission of harmful substances and noise pollution. Exactly in these cases railways can be advantageous as they are characterized by the following:
– Limited use of space compared to large transport capacity;
– Reliability and safety;
– High degree of automation and management;
– Moderate environmental impact.

## Slide 2
Basic considerations and guidelines to be used in the establishment
of railway horizontal and vertical alignments.
The route upon which a train travels and the track is constructed is defined as an alignment. An alignment is defined in two fashions. First, the horizontal alignment defines physically where the route or track goes (mathematically the XY plane). The second component is a vertical alignment, which defines the elevation,
rise and fall (the Z component).
Alignment considerations weigh more heavily on railway design versus highway design for several reasons. First, unlike most other transportation modes, the operator of a train has no control over horizontal movements (i.e. steering). The guidance mechanism for railway vehicles is defined almost exclusively by track location and thus the track alignment. The operator only has direct control over longitudinal aspects of train movement over an alignment defined by the track, such as speed and forward/reverse direction. Secondly, the relative power available for locomotion relative to the mass to be moved is significantly less than for other forms of transportation, such as air or highway vehicles. (See Table 6-1) Finally, the physical dimension of the vehicular unit (the train) is extremely long and thin, sometimes approaching two miles in length. This compares, for example, with a barge tow, which may encompass 2-3 full trains, but may only be 1200 feet in length.
These factors result in much more limited constraints to the designer when considering alignments of small terminal and yard facilities as well as new routes between distant locations.

## Slide 3
As a vehicle traverses a curve, the vehicle transmits a centrifugal force to the rail at the point of wheel contact. This force is a function of the severity of the curve, speed of the vehicle and the mass (weight) of the vehicle. This force acts at the center of gravity of the rail vehicle. This force is resisted by the track. If the vehicle is traveling fast enough, it may derail due to rail rollover, the car rolling over or simply derailing from the combined transverse force exceeding the limit allowed by rail-flange contact.
This centrifugal force can be counteracted by the application of superelevation (or banking), which effectively raises the outside rail in the curve by rotating the track structure about the inside rail. (See Figure 6-6) The point, at which this elevation of the outer rail relative to the inner rail is such that the weight is again equally distributed on both rails, is considered the equilibrium elevation. Track is rarely superelevated to the equilibrium elevation. The difference between the equilibrium elevation and the actual superelevation is termed underbalance.

## Slide 5
Underbalance limits above three to four inches (to as much as five or six inches upon FRA approval of a waiver request) for specific passenger equipment may be granted after testing is conducted.
Track is rarely elevated to equilibrium elevation because not all trains will be moving at equilibrium speed through the curve.
Furthermore, to reduce both the maximum allowable superelevation along with a reduction of underbalance provides a margin for maintenance. Superelevation should be applied in 1/4-inch increments in most situations. In some situations, increments may be reduced to 1/8 inch if it can be determined that construction and maintenance equipment can establish and maintain
such a tolerance.
Even if it is determined that no superelevation is required for a curve, it is generally accepted practice to superelevate all curves a minimum amount (1/2 to 3/4 of an inch). Each railway will have its own standards for superelevation and underbalance, which should be used unless directed otherwise.

## Slide 6
Track is rarely elevated to equilibrium elevation because not all trains will be moving at equilibrium speed through the curve.
Furthermore, to reduce both the maximum allowable superelevation along with a reduction of underbalance provides a margin for maintenance. Superelevation should be applied in 1/4-inch increments in most situations. In some situations, increments may be reduced to 1/8 inch if it can be determined that construction and maintenance equipment can establish and maintain
such a tolerance.
Even if it is determined that no superelevation is required for a curve, it is generally accepted practice to superelevate all curves a minimum amount (1/2 to 3/4 of an inch). Each railway will have its own standards for superelevation and underbalance, which should be used unless directed otherwise.
A freight train is most commonly comprised of power and cars. The power may be one or
several locomotives located at the front of a train. The cars are then located in a line behind
the power. Occasionally, additional power is placed at the rear, or even in the center of the train and may be operated remotely from the head-end. The train can be effectively visualized for this
discussion as a chain lying on a table. We will assume for the sake of simplicity that the power is all at one end of the chain.

## Slide 7
As the train moves or accelerates, the chain is pulled from one end. The force at any point in the chain (Figure 6-11) is simply the force being applied to the front end of the chain minus the frictional resistance of the chain sliding on the table from the head end to the point under consideration.
Figure 6-11 Force Applied Throughout the Train - ATSF Railroad Technical Manual - Courtesy of BNSF