## Slide 1
H, the height of the embankment is fixed by the height of normal flood levels plus a clearance of 0.5m.
The area of the cross-section can then be calculated as: (5.5 + 2H) x H [m2], which is equivalent to cubic metres per metre road length when we calculate volumes.
Example:
An embankment of 0.80m average height would have a cross-section area of:
(5.5 + 2 x 0.8) x 0.8 = 5.68 m2
or 5.68 m3 per metre length.

## Slide 2
However, for the supervisor this does not give sufficient detail to organise the work on a day to day basis.
The embankment will be built up in compacted layers. The width (W), of each layer depends on the gradient of the side slope and the height of the embankment.
The thickness of the layers will depend on the method and equipment used for compaction. Let us assume compaction by a 1 tonne vibrating roller, which can compact a layer about 15cm thick. So, the embankment will need to built in 15cm layers.
The supervisor needs to estimate the volume of each layer to be able to allocate the right number of labourers for the work each day. For an embankment with a 5.5m carriage width, this is calculated as follows:
The first layer (at the top) 6.1 x 0.15 = 0.91m3 per metre or 18.3m3/20m, the second layer 6.7 x 0.15 = 1.01m3 per metre or 20.1m3/20m,
the third layer 7.3 x 0.15 = 1.10m3 per metre or 21.9m3/20m.

## Slide 3
To calculate the regulating layers, we will need to make some practical assumptions:
• that ground levels are to be rounded to the nearest 10cm, and
• that the ground slope between points can be represented as a straight line.
It is then possible to calculate the volumes of layers of different thickness and shape.

## Slide 4
Drainage
Water is the main contributor to the wear and damage of low-volume rural
roads. The water can be in the form of ground water, surface water (streams
and rivers) or rain. Water can damage the road in two ways:
• by washing away the soil (erosion or scouring), or
• by making the road body less strong to traffic (lowering the road bearing
capacity).
It is therefore important to install an efficient drainage system which allows for the
water to flow of the road and away from it as quickly as possible. This is achieved by
a system consisting of the following components:
• road surface drainage which enables the water to flow off the road surface,
• side drains and mitre drains which collect and lead the water away from the
road,
• catchwater drains which catches surface water before it reaches the road,
• scour checks which prevent erosion in the ditches by slowing down the flow of
the water,
• culverts which lead the water from the side drains under the road to the other
(lower) side,
small bridges and drifts which allows the road to cross small rivers and streams
in a controlled manner throughout the seasons.

## Slide 6
Road Surface Drainage
Road surface drainage is achieved by installing a camber on the road carriage way, thereby enabling the surface water to run off to the side drains. The combination of stagnant water on the road surface and traffic will quickly cause erosion of the road surface. Secondly, if surface water penetrates into the road, it will deteriorate the bearing strength of the road body. To avoid these problems all roads are provided with a camber.
The camber is the slope from either side of the centre line towards the road shoulders. The gradient of this slope varies depending on the type of surface materials. For earth and gravel roads, it is recommended that this slope is in the range of 5 to 10 per cent in order to obtain a sufficient run-off.
Since traffic will eventually erode the road surface, create wheel ruts and causing more erosion in the centre of the road, it is recommended that the road camber of a gravel road is constructed at 7 to 10 percent. This will prolong the life time of the road and allow a longer period of time and use before reshaping of the camber is required.

## Slide 7
Side Drains
The side drains need to have sufficient capacity to collect all rain water from the road carriage way and dispose of it quickly and in a controlled manner to minimise damage.
Sides drains can basically be constructed in three forms: V-shaped, rectangular or as a trapezoid.
Sides drains can basically be constructed in three forms: V-shaped, rectangular or as a trapezoid.
The V-shape is the standard shape for ditches constructed by a motor- grader. It can be easily maintained by heavy equipment, however it carries a low capacity. The rectangular shape requires little space but needs to be lined with rock or concrete to maintain its shape. When using labour-based methods, it is possible to construct a trapezoid shaped side drain. This shape carries a high flow capacity and by carefully selecting the gradients of its side slopes, will resist erosion.

## Slide 8
Erosion Control
The main problems for the side drains are erosion and silting. Erosion is caused by a large quantity of water travelling at high speeds. It is possible to reduce the speed by widening the side drain, but the best way to control erosion is by reducing the amount of water flowing through the drain. This is done by using mitre drains to empty the side drain at regular intervals before the volume of water builds up and causes
erosion.
Another method to control erosion is to place scour checks. These are only used in hilly terrain with steep road gradients where it may not be possible to remove water using mitre drains. Their function is to slow down the water flow by reducing the natural gradient of the drain by allowing the drain to silt up behind the scour check.
Silting is caused by sand and silt settling out of the water. This only occurs with slow flowing, or stationary water. It takes time for the particles to settle, so the further the water has to travel in the drain, the more time there is for the silting to take place.
The solution is to empty the side drains frequently by means of installing mitre drains
at regular intervals.
In some cases, it is wise to construct cut-off or interception drains which prevents surface water from reaching the road. These are particularly useful in the surrounding areas to drift approaches, culverts and bridges. They are also effective in channelling away water from the high side of the road in side sloping terrain.

## Slide 9
Mitre Drains
The location of mitre drains should be determined during the initial stages when setting out the road alignment, thereby ensuring that the road receives a good off road drainage. Make sure that sufficient numbers of mitre drains have been located before side drain excavation starts.
Calculating the correct space between the mitre drains can be quite complicated, in principle the more mitre drains provided, the better. A general rule is to:
• wherever possible, provide a mitre drain for every 100m or less, and
• when the road gradient is very small, provide mitre drains at every 50m along the side drain.

## Slide 10
> Make a strong block off in the side drain, and make it easy for the water to flow along
and out of the mitre drain.
Water will always flow the easiest way. The water will try to continue to flow down the side of the road because it is usually steeper and in a straight line. If you want to divert the water into the mitre drain you must make it easier for it to flow where you want it to go.
The best way to provide a strong block-off is to leave 3 - 8m of natural ground on the drain line not excavated. Forming the block-off with excavated material is not as strong. Block-offs act as useful turning points for trucks and other equipment during the gravelling operation. They are also a natural point to off-load and store gravel for future routine maintenance works.
> The amount of water entering the mitre drain cannot be greater than the amount flowing out. Otherwise, the drain will fill up and over flow, often damaging the block off and causing even greater problems at the next mitre drain. In most cases, the standard mitre drain should be big enough to carry water coming from the standard side drain, except when:
• the side drains carry more water than usual,
• the side drain slope is much greater than the mitre drain slope
In such cases, the mitre drain should be made wider than the side drain so that it can carry more water.

## Slide 11
> The length of the drain depends on the terrain ground levels and the slope of the drain.
Mitre drains should be as short as possible. Long mitre drains are expensive, more
likely to silt up or get blocked off, and in general more difficult to maintain.
A good slope for a mitre drain is 2%. The gradient should not exceed 5%, otherwise there may be erosion in the drain or to the land where the water is discharged. In mountainous terrain, it may be necessary to accept steeper gradients. In such cases, appropriate soil erosion measures should be considered. In flat terrain, a small gradient of 1% or even 0.5% may be necessary to discharge water, or to avoid very long drains. These low gradients should only be used when absolutely necessary. The slope should be continuous with no high or low spots.
> Try to select a line for the mitre drains which will connect with natural run-off channels that take the water well clear of the road. If this is not possible, make sure that the next mitre is set out to catch this water before it enters back into the side drains.
> Finally, it is important that the discharged water does not disturb farming activities in the surrounding areas. By discussing the location where to discharge water from the road with the local farmers, it may be possible to achieve solutions which may assist the farmers rather than destroying the water management of their farm lands.

## Slide 12
Block off 3 to 8 m

## Slide 13
When road gradients are steeper than 4%, the drainage water will gain high speed which may cause erosion of the side drains. Apart from leading the water off in mitre drains, scour checks may reduce the speed of water and prevent the water from eroding the road structure.
Scour checks are usually constructed in natural stone or with wooden or bamboo stakes. By using natural building materials available along the road side, they can easily be maintained after the road has been completed. The distance between scour
checks depend on the road gradient. This relation is shown in the following table
Road Gradient | [%] | Scour Check Interval [m]
4 |  | not required
5 |  | 20
6 |  | 15
7 |  | 10
8 |  | 8
9 |  | 7
10 |  | 6

## Slide 14
After the basic scour check has been constructed, an apron should be built immediately downstream using stones. The apron will help resist the forces of the waterfall created by the scour check. Sods of grass should be placed against the upstream face of the scour check wall to prevent water seeping through it and to encourage silting to commence on the upstream side. The long term goal is to establish complete grass covering over the silted scour checks to stabilize them.

## Slide 15
Cut-off Drains
The purpose of cut-off or interception drains is to prevent water from reaching the road, or to direct water to where it can cross the road safely at constructed water crossings such as culverts, bridges, drifts, etc.
These drains, when properly thought out, properly set out and properly built, can be very useful in reducing damage to the road and reducing maintenance costs.
In most cases, it is cheaper and safer to direct water away from the road, using these drains, rather than providing erosion control measures in the side drains. However, there are certain dangers with cut-off drains that must be considered:
• the water usually carries a lot of silt and if not properly built can silt up quickly,
• as they are off the road they will probably receive less maintenance -
especially when they are difficult to maintain,
• when they fail, water will break through in a concentrated flow causing damage, and
• they may be ploughed up or blocked off by people using the land.

## Slide 16
These dangers can only be avoided if careful planning goes into the drains before
construction and if they are built properly. The following precautions should be taken:
• reduce the danger of silting by making sure there is a continuous down hill gradient and that there is a clear outlet at the end,
• make sure they are easy to maintain and that erosion damage is reduced so
that maintenance needs are small (wide with sloped sides),
• make the drain strong - anticipate the possible weak points of the drain where water could break through and strengthen the drain there,
• locate drains carefully after discussion with local people - where people have to cross the drain, provide easy side slopes so that people will not fill the
drain.

## Slide 17
Siting of Culverts
The siting of culverts should be carried out during the initial setting out of the road alignment. It is important that the culverts are regarded as an integral part of the overall drainage system of the road.
If an existing road is being improved, most culvert sites will be obvious, because the road will have been damaged in some way. In such a situation, look for places where:
• small gullies have formed because water has been flowing across the road,
• sand has deposited on the road because of standing water, or
• drains have been badly damaged because they have been carrying too much water.

## Slide 18
Drifts provide an efficient and economic method of allowing water to cross from one side of a road to the other. In the case of drifts, the water is actually allowed to pass over the surface of the road. As a result, the road surface will need special protection to stand up to the flow of water. This is usually done by making a stone packed or concrete surface where the water will pass. The level of the drift will be lower than the road on each side, to make sure that water does not spill over onto the unprotected road surface.
Notes: <number>

## Slide 19
Site Location
The most important step is to locate a suitable site for the river crossing. If the drift is
wrongly placed, it may result in both extra work during construction and maintenance
afterwards. The main points to consider are:
• The angle between the centre line of the road and the flow of the water should
be close to 90o.
• The site should be on a straight length of the stream bed.
• Avoid places where there are signs of scouring or silting. Both will cause
future maintenance problems.
• Avoid places where there are steep banks which will involve a lot of
excavation and steep approach slopes.
The site should be on a straight length of the road.

## Slide 20
Drift Approaches
The ideal slope for a drift approach is 5%. When considering building a drift, set out the approaches first to see how much excavation is required.
Two profiles are set out to a 5% slope at each side of the crossing. The length of the
approach can be found by means of a traveller 1m high moved along the line of the
slope profiles until it levels up with the slope profiles when standing on the natural
ground.
The traveller can also be used to measure the depth of the dig along the proposed
approach, and this can be used to estimate the volume of excavation required. It may
indicate the need to look for another site for the drift.

## Slide 21
The above is an example of a drift which in principle consists of a porous dam which retains the gravel/rock from being carried away by the water flow. The top of the gabion dam is between 15 and 20cm higher than the river bed at the downstream end.

## Slide 22
Once the concrete has been placed, keep it damp and let it cure for 7 to 10 days. If the length of the slab is less than 12m there is no need for an expansion joint. On long river crossings, make expansion joints for approximately every 10 to 15 metres
Gravelling is carried out to provide a strong surface layer which is passable in
both dry and wet weather, and which does not deform under the expected traffic loads. Together with the road camber, a good gravel surface will prevent water from entering into the road body and thereby avoiding surface water from deteriorating the bearing strength of the road.
In principle, the following methods can be used to gravel a road:
• use of a mix of labour and equipment, or
• use labour for all activities except hauling over distances longer than 150 metres.

## Slide 23
Transport of gravel can be organised in many ways, depending on the distance from the gravel quarry to the site and the type of equipment available to the project. The following table provides a general picture of the types of transport appropriate for different haulage distances:
Distance Transport
10 – 150 m Wheelbarrows
150 – 2000 m Animal Carts
500 – 8000 m Tractors & Trailers
1000 - Trucks
Gravelling away from the quarry implies that the trucks will pass over the newly completed road sections. This method has the advantage that the vehicles frequently pass over the
newly levelled gravel and thereby provide some compaction to the gravel layer. However, this method also have some disadvantages. It requires that the delivered gravel needs to be levelled before a new truck can dump
its gravel and may therefore delay the un-loading. Finally, a large number of heavy traffic on the road may result is some damages to the newly constructed road.

## Slide 24
Work Procedure
Before carrying out any gravelling works, first check that the earth works have been properly carried out and levelled to the exact and required standards. Set up the profile boards once again, and ensure that all levels are correct and that the camber has not been damaged.
Placing the gravel, involves four activities, namely un-loading, spreading, watering and compaction.