## Slide 1
1.1.1 Solar energy
The most important supplier of energy for the earth is the sun. The whole of life
depends on the sun’s energy. It is the starting point for the chemical and biological
processes on our planet. At the same time it is the most environmentally friendly form of all energies, it can be used in many ways, and it is suitable for all social systems.
In the core of the sun a fusion process takes place in which pairs of hydrogen
nuclei are fused into helium nuclei. The energy thus released is radiated into space in the form of electromagnetic radiation. As the sun is 148 million km from the earth, it radiates only a tiny fraction of its energy to the earth. In spite of this, the sun offers more energy in four hours than the human race uses in a whole year.

## Slide 3
IRRADIATED POWER, IRRADIANCE, HEAT QUANTITY
When we say that the sun has an irradiance, G, of for example 1000 W/m2, what is meant here is the capability of radiating a given irradiated power, φ (1000 W), onto a receiving surface of 1 m2 (10.76 ft2).
The watt is the unit in which power can be measured. If this power is referred, as in this case, to a unit area, then it is called the irradiance.
1 kW (kilowatt) = 103 W (1000 watts)
1 MW (megawatt) = 106 W (1 million watts) = 103 kW
1 GW (gigawatt) = 109 W (1 thousand million watts) = 106 kW
1 TW (terawatt) = 1012 W (1 million million watts) = 109 kW
When the sun shines with this power of 1000 W for 1 hour it has performed 1 kilowatt-hour of work (1 kWh) (Work = Power × Time).
If this energy were converted completely into heat, a heat quantity of 1 kWh would be produced.
Irradiated power, φ (W)
Irradiance, G (W/m2)
Heat quantity, Q (Wh, kWh)

## Slide 4
other directions and not just directly from the sun. This proportion of the radiation,
which reaches the eye of the observer through the scattering of air molecules and dust
particles, is known as diffuse radiation, Gdif. Part of this is also due to radiation
reflected at the earth’s surface. The radiation from the sun that meets the earth
without any change in direction is called direct radiation, Gdir. The sum of direct and
diffuse radiation is known as global solar irradiance, GG (Figure 1.5).
GG = Gdir + Gdif

## Slide 5
Figure 1.3.
Daily courses and daily totals for
irradiation in London

## Slide 6
Figure 1.5.
Global solar irradiance and its
components

## Slide 7
The sun’s radiation in space, without the influence of the earth’s atmosphere, is
described as spectrum AM 0. As it passes through the earth’s atmosphere, the
radiation intensity is reduced by:
■ reflection caused by the atmosphere
■ absorption by molecules in the atmosphere (O3, H2O, O2, CO2)
■ Rayleigh scattering (scattering by the air molecules)
■ Mie scattering (scattering by dust particles and contamination in the air).
γS AM Absorption (%) Rayleigh scattering (%) Mie scattering (%) Total attenuation (%)
90° 1.00 8.7 9.4 0–25.6 17.3–38.5
60° 1.15 9.2 10.5 0.7–25.6 19.4–42.8
30° 2.00 11.2 16.3 4.1–4.9 28.8–59.1
10° 5.76 16.2 31.9 15.4–74.3 51.8–85.4
5° 11.5 19.5 42.5 24.6–86.5 65.1–93.8

## Slide 12
MEASURING SOLAR RADIATION
Devices that measure the global solar irradiance on a horizontal surface are called pyranometers (Figure 1.11). If these devices are screened from the sun’s direct rays by a fixed ring that covers the whole path of the sun in the sky, then the device measures only the diffused radiation.
The radiation receiver is seated beneath a spherical glass cover and consists of a star-shaped arrangement of black and white thermo-elements. These elements generate thermo-electromotive forces, depending on their temperature, which can be measured.
Pyranometers are relative measuring instruments that have to be
calibrated. Other global solar irradiance measuring devices that are available on the market and are cheaper than pyranometers possess a solar cell as a receiver, as in the MacSolar (Figure 1.12), for example.
The simplest and most commonly used device for measuring the sunshine duration is the Campbell–Stokes sunshine recorder (Figure 1.13).
This consists of a solid glass sphere, which generates a focal point on the side that is turned away from the sun and which is always at the same distance. A correspondingly curved flameproof paper strip is placed around the sphere. A track is burned on the paper strip. When clouds cover the sun, the burnt track is interrupted.

## Slide 13
Figure 1.11.
Pyranometer made by Kipp & Zonen

## Slide 14
Figure 1.12 (left).
MacSolar
Figure 1.13 (right).
Campbell–Stokes sunshine recorder

## Slide 16
SHADING
Shading reduces the yield of a solar thermal system. To take account of shading of the receiving surface by the surroundings (houses, trees etc.), three methods can be used:
■ graphical method (indicative)
■ photographic method (indicative)
■ computer-aided method.
GRAPHICAL METHOD
This method requires a scale drawing of the layout of the surroundings, details of the height of each object that could shade the potential collector position, and a solar altitude diagram for the latitude at which the collector is to be located.
First, the elevation and azimuth angles of the relevant objects must
be established, and then the shade silhouette must be plotted in the solar altitude diagram. If large areas of shade arise in time periods with high radiation, then the expected radiation received must be reduced correspondingly.

## Slide 17
PHOTOGRAPHIC METHOD
In this method a camera with a ‘fish-eye’ lens is used in connection with special solar-geometrical accessories to photograph the surrounding silhouette while blending in the solar altitude diagram of the respective location.
The results can then be read directly off the photograph.
COMPUTER-AIDED METHOD
Several simulation programs are provided with shade simulators (see for instance TRNSYS and Sundi in Chapter 10). After determining the elevation and azimuth angles of important objects, the influence of shade can be directly calculated within the scope of the system simulation.
This method yields more accurate results than the previous two methods.
Figure 1.16 shows an example of a solar altitude diagram with surrounding silhouette.

## Slide 19
The solar collector mounted on the roof converts the light that penetrates its glass
panes (short-wave radiation) into heat.
The collector is therefore the link between the sun and the hot water user. The heat is created by the absorption of the sun’s rays through a dark-coated, usually metal, plate – the absorber.
This is the most important part of the collector. In the absorber is a system of pipes filled with a heat transfer medium (usually water or an antifreeze mixture). This takes up the generated heat.
Collected together into a pipe it flows to the hot water store. In most solar water
heating systems – by far the most commonly used type of solar thermal systems – the
heat is then transferred to the domestic water by means of a heat exchanger. The
cooled medium then flows via a second pipeline back to the collector while the heated
domestic water rises upwards in the store.
According to its density and temperature, a stratified system is set up in the store: the warmest water is at the top (from where it leaves the tank when the taps are turned on) and the coldest is at the bottom (where cold water is fed in).

## Slide 20
Figure 2.1.
Standard solar water heating system with heating boiler for additional heating
(S = temperature sensor)

## Slide 21
Figure 2.2.
Standard thermosyphon solar water heater with outdoor tank
Source: Solahart

## Slide 22
For temperate climates, in a solar system for one- and two-family homes with
dimensions of about 0.6–1.0 m2 (6.46–10.76 ft2) of collector surface per person and
approximately 40–60 l (10.6–15.9 gallons) of storage volume per person, the water is
mostly heated by the solar system in the summer.
This provides an annual degree of coverage (proportion of solar energy to the total energy required for domestic water heating) of about 50–60%. The remaining 40–50% has to be covered by auxiliary heating.
For pumped systems, this is often done by means of an extra heat exchanger
in the top of the store. Other common solutions are to use the solar water heater as a
preheater and connect the solar-heated water to a conventional boiler, or (mainly for
sunny climates) to use an electrical element immersed in the store.
Another decisive factor in establishing the level of supplementary energy required
is the target domestic water temperature on the boiler controller. The lower this is set,
for example 45°C (113°F), the higher the coverage proportion of solar energy and
correspondingly the lower the proportion of auxiliary energy, and vice versa.
However, in some countries, domestic hot water regulations pose a lower limit on this
temperature setting, of 60°C (140°F).

## Slide 23
Collectors have the task of converting light as completely as possible into heat, and
then of transferring this heat with low losses to the downstream system.
There are many different types and designs for different applications, all with different costs and performances. See Figures 2.3 and 2.4.
Different definitions of area are used in the manufacturers’ literature to describe
the geometry of the collectors, and it is important not to confuse them:
■ The gross surface area (collector area) is the product of the outside dimensions, and defines for example the minimum amount of roof area that is required for mounting.
■ The aperture area corresponds to the light entry area of the collector – that is, the area through which the solar radiation passes to the collector itself.

## Slide 25
The absorber area (also called the effective collector area) corresponds to the area
of the actual absorber panel. See Figures 2.5–2.7.

## Slide 26
Figure 2.5.
Cross-section of a flat-plate collector with description of the different areas

## Slide 27
Figure 2.6.
Cross-section of a heat-pipe evacuated tube collector with description of the different surface areas

## Slide 28
Figure 2.7.
Cross-section of a double evacuated tube collector (‘Sydney tubes’) with
description of the different surface areas

## Slide 29
2.2.2 Glazed flat-plate collectors
2.2.2.1 DESIGN
Almost all glazed flat-plate collectors currently available on the market consist of a
metal absorber in a flat rectangular housing. The collector is thermally insulated on its back and edges, and is provided with a transparent cover on the upper surface. Two pipe connections for the supply and return of the heat transfer medium are fitted, usually to the side of the collector. See Figure 2.8.
Figure 2.8.
Section through a glazed flat-plate collector

## Slide 30
ABSORBER
The core piece of a glazed flat-plate collector is the absorber. This consists of a heatconducting metal sheet (made of copper or aluminium for example, as a single surface or in strips) with a dark coating. The tubes for the heat transfer medium, which are usually made of copper, are connected conductively to the absorber.
When the solar radiation hits the absorber it is mainly absorbed and partially reflected. Heat is created through the absorption and conducted in the metal sheet to the heat transfer medium tubes or channels. Through these tubes flows the liquid heat transfer medium, which absorbs the heat and transports it to the store.
A variant is the so-called cushion absorber, which has full-surface flow-through.
The task of a solar collector is to achieve the highest possible thermal yield. The
absorber is therefore provided with a high light-absorption capacity and the lowest possible thermal emissivity. This is achieved by using a spectral-selective coating.
Unlike black paint, this has a layered structure, which optimizes the conversion of
short-wave solar radiation into heat while keeping the thermal radiation as low as
possible. See Figure 2.9.

## Slide 31
Figure 2.9.
Absorption and emission behaviour of different surfaces

## Slide 32
RADIATION AND INTERACTION WITH MATTER
When short-wave sunlight (wavelength 0.3–3.0 m) hits an object, such as a solar cover, it is reflected more or less strongly according to the surface structure (material, roughness and colour).
White surfaces reflect much more than dark surfaces. The proportion of reflected radiation (especially for glass panes) also depends on the angle of incidence of the radiation (Fresnel’s law).
The remaining portion is absorbed by the object or, for translucent material, is allowed to partially pass through.
Finally, the absorbed portion is converted into long-wave thermal radiation (wavelengths 3.0–30 m) and radiated according to the surface structure.
These processes are described physically as the degrees of reflection, absorption, transmission and emissivity of a body

## Slide 33
Figure 2.10.
Energy flows in the collector

## Slide 34
Figure 2.11.
Optical and thermal losses

## Slide 36
HYBRID COLLECTOR
Hybrid collectors can be realized as a combination of solar panels (PV) with liquidbased collectors as well as with air-based collectors. The combination with solar panels is reasonable, because during the solar electricity conversion only about 12% (with crystalline silicon) of the solar radiation converts into electricity, whereas the remainder converts into heat. This heat is used in the hybrid collector to either heat up a liquid or air (see Section 8.2.1.8).

## Slide 38
2.2.3 Vacuum collectors
2.2.3.1 EVACUATED TUBE COLLECTORS
To reduce the thermal losses in a collector, glass cylinders (with internal absorbers)
are evacuated in a similar way to Thermos flasks (Figure 2.17). In order to completely suppress thermal losses through convection, the volume enclosed in the glass tubes must be evacuated to less than 10–2 bar (1 kPa).
Additional evacuation prevents losses through thermal conduction.
The radiation losses cannot be reduced by creating a vacuum, as no medium is necessary for the transport of radiation.
They are kept low, as in the case of glazed flat-plate collectors, by selective coatings (small value).
The heat losses to the surrounding air are therefore significantly reduced. Even with an absorber temperature of 120°C (248°F) or more the glass tube remains cold on the outside.
Most vacuum tubes are evacuated down to 10–5 bar.

## Slide 39
Figure 2.17.
The principle of vacuum thermal insulation

## Slide 40
DIRECT FLOW-THROUGH EVACUATED TUBE COLLECTORS
In this design (Figure 2.18) the heat transfer medium is either led via a tube-in-tube system (coaxial tube) to the base of the glass bulb, where it flows back in the return flow and thereby takes up the heat from the highly spectral-selective absorber, or it flows through a U-shaped tube.
Direct flow-through evacuated tube collectors can be oriented towards the south, but they can also be mounted horizontally on a flat roof.

## Slide 43
2.2.4 Collector accessories
Collectors cannot be installed without additional materials. They are:
■ for on-roof installation: roof hooks, special bricks, rails, vent tiles
■ for in-roof installation: covering frames
■ for flat roof or free installation: bracing, counterweights, bearers.
2.2.5 Collector characteristic curves and applications
Figure 2.22 shows typical efficiency curves and areas of application with the same global solar irradiance for the following collector types: swimming pool absorber, glazed flat-plate collector, and evacuated tube collector. At = 0 each collector type is at its highest efficiency (0).
At its maximum temperature – that is, when it has reached its stagnation temperature – the efficiency equals zero.

## Slide 44
Figure 2.22.
Efficiency characteristic curves for different types of collector and their
areas of application (at irradiation of 1000W/m2K)

## Slide 45
2.3.2 Domestic hot water stores
Figure 2.24 shows an example of an unvented solar store, as often used in temperate
climates. It has the following features:
■ two heat exchangers for two heat sources (bivalent): a solar heat exchanger and an
additional heat exchanger for a heating boiler
■ direct connection to the cold water supply
■ pressure tank 4–6 bar (58–87 psi) operating pressure.
■ UK: 150–200 l (39.6–52.8 gallons)
■ Germany: 300–500 l (79.3–132.1 gallons) in the one- and two-family home segment
of the market
■ USA: 50–100 gallons (approx 200–400 l)
■ Australia: 300–400 l (79.3–105.7 gallons) for 3–4 persons.

## Slide 47
Figure 2.28.
Section through the Energy Manager
‘SolvisMax’ (Manufacturer: Solvis GmbH
& Co. KG, Braunschweig)

## Slide 48
Figure 2.29.
Section through ‘SolvisMax’ energy
manager with heat pump (Manufacturer:
Solvis GmbH & Co. KG, Braunschweig)

## Slide 49
Figure 2.30.
SolvisMax Heat Pump
(Solvis GmbH & Co. KG, Braunschweig)

## Slide 50
Figure 2.32.
GasSolarUnit from Rotex (Manufacturer:
Rotex, Gussglingen)

## Slide 51
In principle, there are three possibilities to store heat:
1 Heat storage by means of direct heat supply in insulated, water filled tanks;
2 Latent heat storage, which applies the solid–fluid phase transition of salt hydrates or paraffins;
3 Thermo chemical storage units (sorption tanks) with which supply of heat splits a compound into its properties, and later with the recombination of the components frees that heat again.
Thermo chemical heat storage differs from the first two storage principles. Heat storage is based on the reversible chemical reaction according to the formula
A + B AB + Heat
During the load phase, the substance AB is supplied with heat, which dissociates the components A and B. In order to recover the heat, both components A and B are allowed to react with one other. As long as a reaction between A and B is prevented, the heat stored in form of chemical energy cannot be set free. This way, heat can be stored at various temperature levels over a period of time.
In Figure 2.34, A corresponds to dry silica gel, B corresponds to free water vapour and AB to the water saturated silica gel.

## Slide 54
2.4 Solar circuit
The heat generated in the collector is transported to the solar store by means of the solar circuit. This consists of the following elements:
■ the pipelines, which connect the collectors on the roof and the stores
■ the solar liquid or transport medium, which transports the heat from the collector to the store
■ the solar pump, which circulates the solar liquid in the solar circuit (thermosyphon and ICS systems do not have a pump)
■ the solar circuit heat exchanger, which transfers the heat gained to the domestic hot water in the store
■ the fittings and equipment for filling, emptying and bleeding
■ the safety equipment. The expansion vessel and safety valve protect the system from damage (leakage) by volume expansion or high pressures.

## Slide 55
2.4.4 Solar heat exchanger (heat transfer unit)
For the transfer of the heat gained from the sun to the domestic hot water, a heat
exchanger (heat transfer unit) is required in twin-circuit systems. We can differentiate
between internal and external heat exchangers.
2.4.4.1 INTERNAL HEAT EXCHANGERS
As internal heat exchangers, finned tube and plain tube types are available (Figure
2.40). The plain tube heat exchanger possesses a greater heat exchange capacity per
square metre of exchanger face. Compared with the finned tube heat exchanger a
multiple of the pipe length is required.
Plain tube heat exchangers are installed in the factory, whereas finned tube heat exchangers, because of their more compact design, can be installed into the store on site by means of special flanges and seals.
However, the effectiveness of heat exchangers can be reduced by the build-up of limescale.
Even a layer 2 mm (0.08 inches) thick reduces the heat transfer capacity of a heat exchanger by 20%; a 5 mm (0.2 inch) thickness reduces it by more than 40%.

## Slide 56
Figure 2.40.
Top: Finned tube heat exchanger
Bottom: Plain tube heat exchanger

## Slide 57
Figure 2.41.
Plate heat exchanger

## Slide 58
Figure 2.42.
Tubular heat exchanger

## Slide 59
2.5.1 Control principles for temperature difference control
Two temperature sensors are required for standard temperature difference control.
One measures the temperature at the hottest part of the solar circuit before the
collector output (flow); the other measures the temperature in the store at the height of the solar circuit heat exchanger. The temperature signals from the sensors (resistance values) are compared in a control unit. The pump is switched on via a relay when the switch-on temperature is reached (see Figure 2.50).
The switch-on temperature difference depends on various factors. Standard settings are from 5 K to 8 K. In principle, the longer the pipeline from the collector to the store, the greater the temperature difference that should be set.
The switch-off temperature difference is normally around 3 K. A third sensor can be connected for temperature measurement in the upper area of the store, which permits the draw-off temperature to be read.

## Slide 60
Figure 2.50.
Function of a temperature difference controller shown as the daily progression of the collector and store temperature
(schematic)12

## Slide 61
Figure 2.54.
Diagram of the components monitored by IOC
(Manufacturer: RESOL, Hattingen)