## Slide 1
Purpose:
In this section you will learn the definitions of heating terminology, methods of heat transfer, calculating heat energy, and the operation of stoves and air-conditioners.
Objectives: at the completion of this section the learner should be able to: Define the terms heat energy, temperature, specific heat capacity, thermal conductivity, and thermal stability Calculate the input heat energy in Joules and kWHr in a simple heating process Describe the methods of heat transfer Calculate the heat energy output of a heating process Explain the connection method of a two phase stove Describe the operation of reverse cycle air-conditioning.
Topic 5 Electrical Heating Control Devices

## Slide 2
Energy
Energy is the ability to do work. There are two types of energy, kinetic and potential. For example water at the top of a fall has potential or stored energy (the energy of rest). As the water goes over the falls it becomes kinetic energy (or the energy of motion). Energy is available in the different forms of mechanical, electrical, chemical and HEAT ENERGY.

## Slide 3
Temperature
The term temperature is used to indicate the condition of a body which determine if it will receive heat from another body or transfer heat to another body. Temperature is the degree of how hot or cold a body may be.
In the S.I. system the main scales are Centigrade and the Kelvin. Both scales use the same two fixed points which is the freezing point of water as the lower value and the boiling point of water (at normal atmospheric pressure) as the higher value
The scales may extend above and below the fixed points as required.
Table 1: Comparisons between Kelvin and Centigrade |  | 
Kelvin Scale in OK | Condition | Centigrade Scale in OC
0 | Absolute Zero | -273.15
273.15
Freezing Point
0
373.15
Boiling Point
100

## Slide 4
Note: for a point of discussion which is correct Celsius or centigrade? Apparently sometime in 1744, a man named Anders CELSIUS invented the Centigrade scale. He named the hottest temperature as zero degrees and the coldest 100 O C. after his death the scientific community renamed the coldest temperature as zero degrees and the hottest as 100OC. So which is correct, Centigrade or Celsius? Your Call!
In theory if an object reaches absolute zero degrees its mass will increase and its size will decrease as in dead stars.
To convert OC to OK the following expression is used:

## Slide 5
Heat & Temperature
Consider two billets of steel of equal mass. Both are heated at the same rate until they are glowing red. The temperature of the two billets are the same as indicated by the colour red The heat energy of both billets is the same because of equal mass, equal change in temperature and both are the same material.
One of the billets is now further heated to white hot while the other billet remains red hot. The temperature of both billets is now different indicated by the colours The heat energy of both billets is now different because of equal mass, un-equal change in temperature and both are the same material.
Temperature indicates the condition of a body whereas heat shows the energy capacity of a body

## Slide 6
Heat Energy
Whenever a body is caused to change its temperature this change is always accompanied by a transfer in energy: The body is absorbing the energy when increasing its temperature The body is dissipating the energy when decreasing its temperature
The energy transferred is the quantity of heat that may be defined as the energy expressed in Joules which is absorbed or dissipated by a body for a state change in temperature. The quantity of energy involved in any change in temperature depends on three factors: m = mass of the body c = the type of material T = the change in temperature

## Slide 7
Capacity for Heat
Capacity for heat may be defined as the number of heat units (Joules) which a body is able to absorb or give out for a stated change in temperature
Copper for example has about 1/11th the heat capacity of water, that is, it takes about 11 times as much heat to raise the same mass of copper through the same temperature change.
To enable a comparison of the heat capacity of different substances, water is selected as the reference and all other substances compared to it

## Slide 8
Specific Heat Capacity [c]
The specific heat capacity of a material is the quantity of heat required to raise the temperature of one kilogram (1 kg) of a material by one OK
For example it would take 4180 Joules of heat to raise 1kg of water by 1 Kelvin
Since a temperature change of 1OK is equivalent to 1OC
The quantity of heat required for any material is determined from the equation:
Where: m= mass of the material in kilograms
c = specific heat capacity of the material in J/kgOC
T = change in temperature (T2-T1) in OC
Some common specific heat capacities are: Water ………………………… 4189 J/kg OC Aluminium ………………… 900 J/kg OC Copper ………………………. 390 J/kg OC Gold …………………………. 130 J/kg OC Silver ……………………….. 230 J/kg OC

## Slide 9
Thermal Conductivity
The capability of conducting heat depends upon:
Temperature difference across the material Cross sectional area of the conduction path Length of the conduction path Type of material

## Slide 10
Best conductors of heat are metals as they offer a low opposition to heat energy flow. Poor conductors of heat are non-metals as they offer a high opposition to heat energy flow.
Heat Transfer
A transfer of heat energy will occur when there is a temperature differential. The direction of heat energy transfer is from a high temperature to a low temperature.
Thermal Stability Occurs when the temperature of a body is the same as its surroundings.
Kilowatt Hours This is the practical unit of electrical energy. It refers to 1 kW being used for 1 hour. It is referred to as 1 “unit” of electrical energy.

## Slide 11
Practical: Determination of Heat energy
Purpose: To determine the heat energy used in heating a mass of water.
Objectives: compare the input heat energy of a heating process to the output heat energy comment on the results including the efficiency of the process. Method: Measure 250 mm of tap water poured into a glass beaker. Allow the temperature to stabilise for several minutes. Connect a resistor hanging from a cover over the beaker. Use a voltage suitable to allow the resistor to heat the water. Maintain a constant current throughout the test so that input energy can be calculated from I2Rt. Measure the temperature at the start of the heating time and each five minutes thereafter. Once the water has reached about 60 degrees Celcius, cease the experiment. Conclusions Calculate the output heat energy of the process from H = mCΔT where C = 4180 Joules/Kg/oC Compare the heat output to the heat input. Calculate the efficiency of the process.

## Slide 12
Review Questions | 
Question 1: | The transfer of heat energy occurs in:
a) | both directions, between a hot body and a cold body
b) | one direction only, between a cold body and a hot body
c) | one direction only, between a hot body and a cold body
d) | neither direction, no transfer of heat energy
Question 2: | Specific heat capacity is measured in:
a) | Joules
b) | Joules/kg
c) | Joules/kg. oK
d) | Joules/oC
Question 3: | Larger amounts of heat energy are usually measured in:
a) | kilowatt-seconds
b) | kilowatts
c) | kilojoules
d) | kilowatt-hours

## Slide 13
Question 4: | The point of thermal stability is reached when the transfer of heat energy is :
a) | low, and the temperature differential is low
b) | high, and the temperature differential is high
c) | low, and the temperature differential is high
d) | zero, and the temperature differential is zero
Question 5: | The absolute temperature scale is measure in:
a) | centigrade
b) | mho
c) | Kelvin
d) | Farenheit

## Slide 14
Question 6: | What is the temperature at “absolute zero”
a) | 0oC
b) | 0oK
c) | -273.15oK
d) | 273.15oK
Question 7: | The most efficient conductor of heat energy would be:
a) | hardwood dowel
b) | plastic rod
c) | glass rod
d) | brass bar
Question 8: | The specific heat capacity of a material is the amount of heat energy required to raise:
a) | mass of 1 kg of material to a higher level
b) | temperature of 1 kg of material by 1oK
c) | temperature of 1 kg of material by 10oC
d) | mass of 10 kg of material by 1oK

## Slide 15
Question 9: | The transfer of heat energy from the sun is:
a) | radiant energy
b) | convection energy
c) | conduction/convection energy
d) | ultra-violet conduction energy
Question 10: | The transfer of energy by the circulatory motion established in the material at a non-uniform temperature owing to the variation of its density and the action of gravity is :
a) | conduction
b) | radiation
c) | complementary conduction
d) | convection

## Slide 16
Question 16: | How many kilolitres of water are heated by 4.18 Mega-Joules of heat energy to raise the temperature by 1OC?
a) | 1
b) | 10
c) | 100
d) | 1000
Question 17: | How many joules of heat energy are expended every second by a thousand watt heating element?
a) | 1 Joule
b) | 10 Joules
c) | 100 Joules
d) | 1000 Joules
Question 18: | The transfer of heat energy from a soldering iron to the work is by:
a) | radiation
b) | convection
c) | thermal-radiation
d) | conduction

## Slide 17
Question 19.
How many mega-Joules of energy is required to raise the temperature of 250 litres of water by 50 degrees Celcius? (The specific heat capacity of water is 4160 Joules/kg/oC).
Question 20.
How long will a 4.6 kW element take to heat the water in a HWS by 50 degrees Celcius if the energy input required is 50 MJ?