## Slide 1
L
UEENEEG101A Solve problems in electromagnetic devices and related circuits
The DC Generator Part I
Notes: Title

## Slide 2
Objectives
At the end of this section students should be able to:
1. State the basic operating principle for a DC Generator.
2. Apply Fleming’s Right Hand Rule for Generators.
3. Calculate the EMF produced by a simple generator.
4. Identify the main components of a DC Rotating Machine.
5. Draw the connections and equivalent circuit of a separately excited dc generator.
L

## Slide 3
The DC Generator Converts
Mechanical Energy to Electrical Energy
The action of the DC Generator depends on
Mutual or Electromagnetic Induction
L

## Slide 4
A
B
N
S
Generator Operation
VAB
A
B
L

## Slide 5
A
B
N
S
Generator Operation
VAB
A
B
L

## Slide 6
B
A
N
S
Generator Operation
VAB
B
A
L

## Slide 7
N
S
Generator Operation
VAB
B
A
L
B
A

## Slide 8
Generator Operation
VAB
Output of the generator is ALTERNATING
Must rectify it to convert to Direct Current (dc)
0°
90°
180°
270°
360°
After rectification the output is Pulsed DC
L

## Slide 9
B
A
Mechanical rectification is done using a
Commutator
L

## Slide 10
e = Blv
The generated voltage depends on:
The strength of the magnetic field,
Flux Density (B) {Tesla}
The length of the conductor in the magnetic field,
Length (l) {meters}
The velocity of the conductor in the magnetic field,
Velocity (v) {ms-1}
and
L

## Slide 11
Ex. 1
l = 200 mm
B = 0.5 T
v = 12 ms-1
Calculate the EMF induced in a 200 mm length of wire if it is moved through a magnetic field with a flux density of O.5 T at a velocity of 12 m/s.
What do we know?
What do we want to know?
e = Blv
e = 0.5 x 200 x 10-3 x 12
e = 1.2 V
L

## Slide 12
A single loop of wire is moved through a magnetic field with a flux density of O.5 T at a velocity of 12m/s. If each side of the loop has a length of 200mm within the field, calculate the EMF induced in:
One side of the loop, and
The loop.
Ex. 2
B = 0.5 T
v = 12 ms-1
e = Blv
What do we know?
What do we want to know?
l1 = 200 mm
l12 = 400 mm
e1 = 0.5 x 200 x 10-3 x 12
e1 = 1.2 V
e12 = 0.5 x 400 x 10-3 x 12
e12 = 2.4 V
(a)
(b)
(a)
(b)
What is l for the loop?
L

## Slide 13
A DC generator armature is wound using 6 series connected coils of copper wire. Each coil has 40 turns and each side of a coil is 250 mm long. If the armature is rotated in a magnetic field of 0.8 T at a velocity of 10 m/s, determine the EMF induced in :
One half turn
One full turn
One coil
The entire armature
Ex. 3
e = Blv
What do we want to know?
(a) One ½ turn  l1 = 0.250 m
What is l in each case?
(b) One full turn  l2 = 0.250 x 2 = 0.500 m
(c) One coil  l3 = 0.250 x 2 x 40 = 20 m
(d) The armature  l4 = 0.250 x 2 x 40 x 6 = 120 m
B = 0.8 T
v = 10 ms-1
What do we know?
l = 250 mm
L

## Slide 14
Ex. 3
l = 250 mm
N = 40 turns
coils = 6
B = 0.8 T
v = 10 ms-1
l1 = 0.25 m
e = Blv
e1 = 0.8 x 10 x 0.25
e1 = 2 V
(a)
l2 = 2 x 250 = 0.5 m
e2 = 0.8 x 10 x 0.50
e2 = 4 V
(b)
l3 = 40 x 0.5 = 20 m
e3 = 0.8 x 10 x 20
e3 = 160 V
(c)
l4 =6 x 20 = 120 m
e4 = 0.8 x 10 x 120
e4 = 960 V
(d)
L

## Slide 15
A Generator’s Magnetic Fields can be provided by:
Permanent Magnets
OR
Electro-Magnets
Small machines
Invariably used in Large machines
L

## Slide 16
Generator’s are classified according to their Magnetic Field Excitation:
Separately Excited
OR
Self Excited
L

## Slide 17
The DC Generator
5
1
3
2
4
L

## Slide 18
Separately Excited
E1
E2
DC Supply
Field Windings
A1
A2
Armature
L

## Slide 19
E1
E2
Separately Excited
A1
A2
DC Supply
Field Windings
Armature
Field Rheostat
L

## Slide 20
Advantages
Separately Excited
A1
A2
E1
E2
DC Supply
Allows separate control of the output voltage
The excitation is not affected by changes in load
RA
RF
Field Rheostat
Field Windings
Eg
L

## Slide 21
Advantages
Separately Excited Equivalent Circuit
A1
A2
E1
E2
DC Supply
RA
RF
Field Rheostat
Allows separate control of the output voltage
The excitation is not affected by changes in load
Field Windings
Eg
L

## Slide 22
The generated voltage depends on:
The strength of the magnetic field,
Flux Density (B) {Tesla}
The length of the conductor in the magnetic field,
Length (l) {meters}
The velocity of the conductor in the magnetic field,
Velocity (v) {ms-1}
and
The amount of Flux (Φ) and the Number of Poles (P)
The Number of Armature Conductors (Z) and Paths (a)
eg = Blv
L

## Slide 23
a = P
a = 2
Lap Type Windings
Wave Type Windings
L

## Slide 24
eg = Blv
The generated voltage depends on:
The strength of the magnetic field,
Flux Density (B) {Tesla}
The length of the conductor in the magnetic field,
Length (l) {meters}
The velocity of the conductor in the magnetic field,
Velocity (v) {ms-1}
and
The amount of Flux (Φ) and the Number of Poles (P)
The Number of Armature Conductors (Z) and Paths (a)
The revolutions per second (n/60)
L

## Slide 25
Generated voltage depends on:
Things we can change:
Flux (Φ)
Things we can not change:
Number of Revolutions (n)
These make up the Machine Constant (k)
Number of Poles (P)
Number of Armature Conductors (Z)
Number of Armature Paths (a)
Number of seconds in a minute (60)
eg = kΦn
So that:
eg = PZ x Φn 60a
becomes:
L

## Slide 26
Ex. 4
Φ = 0.08 Wb
n = 360 rpm
k = 15
e = kΦn
e = 15 x 0.08 x 360
e = 432 V
Determine the generated voltage of a separately-excited generator with a machine constant of 15, an effective field flux of 0.08 Wb and an operating speed of 360 rpm.
What do we know?
What do we want to know?
L

## Slide 27
Ex. 5
Φ = 0.10 Wb
n = 360 rpm
k = 15
e = kΦn
e = 15 x 0.10 x 360
e = 540 V
Determine the generated voltage of a separately-excited generator with a machine constant of 15, an effective field flux of 0.10 Wb and an operating speed of 360 rpm.
What do we know?
What do we want to know?
L

## Slide 28
Ex. 6
Φ = 0.08 Wb
n = 500 rpm
k = 15
e = kΦn
e = 15 x 0.08 x 500
e = 600 V
Determine the generated voltage of a separately-excited generator with a machine constant of 15, an effective field flux of 0.08 Wb and an operating speed of 500 rpm.
What do we know?
What do we want to know?
L