## Slide 1
L
UEENEEG101A Solve problems in electromagnetic devices and related circuits
The Magnetic Circuit
Notes: Title

## Slide 2
Objectives
At the end of this section students should be able to:
1. Describe and draw the magnetic circuit.
2. Describe Reluctance (Rm) and its effects in magnetic circuits.
3. Describe the relationship between MMF (Fm), Flux (Φ) and Reluctance (Rm).
4. Describe Permeability (μ) and its effects in magnetic circuits.
5. Describe the factors that affect Flux Density (B).
6. Describe the term Magnetising Force (H).
7. Calculate values of Fm, H, B, μ, Rm, and Φ.
L

## Slide 3
+
I
N
+
The Magnetic Circuit
EMF
MMF
Φ
Rm
Rm = Reluctance
MMF = Magneto Motive Force
Φ = Flux
Rm = Resistance
EMF = Electro Motive Force
I = Current
The Electric Circuit
I
L

## Slide 4
A material’s opposition to a magnetic field is called its
Reluctance (Rm)
It is similar to Resistance and is affected by the same physical properties.
Rm α Length of Magnetic Path (l)
Rm α 1/CSA of Magnetic Path (A)
Rm α 1/ Absolute Permeability (μ)
L

## Slide 5
Where:
μ = Absolute Permeability
l = Length of Magnetic Path (m)
A= Cross Sectional Area of the Magnetic Path (m2)
Rm = Magnetic Reluctance (At/Wb)
L

## Slide 6
A material’s ability to accept a magnetic field is called its
Permeability (μ)
The permeability of free air (μo) is:
μo = 4π x 10-7 = 12.57 x 10-7
All other permeabilities are expressed as a value Relative to the permeability of free air.
(Relative Permeability = μr)
(Permeability is similar to Conductance)
L

## Slide 7
Absolute Permeability (μ)
μ = μo x μr
Material’s that
have Good Magnetic Properties
have High Relative Permeability
L

## Slide 8
μo = 4π x 10-7 = 12.57 x 10-7
Material
Copper
Relative Permeability (μr)
1
Absolute Permeability (μ)
12.57 x 10-7
Aluminium
1
12.57 x 10-7
Iron
9,000
11.31 x 10-3
Soft Iron
55,000
69.13 x 10-3
Mu Metals
100,000
125.7 x 10-3
μ = μo x μr
L

## Slide 9
+
I
N
Φ
µ = 10.68 x 10-4
A = 175 mm2
l = 250 mm
L

## Slide 10
+
I
Fm = IN
Magneto Motive Force (MMF or Fm)
Rm = Reluctance
Flux (Φ) => Current (I)
Core A path of low Reluctance
N
Φ
Units of Reluctance are Ampere Turns per Weber (AT/Wb)
Like Ohm’s Law
Fm
L

## Slide 11
+
I
Fm = IN
Magneto Motive Force (Fm)
Rm = 40, 000 At/Wb
Flux (Φ)
N = 1 500 turns
Fm = 2.0 x 1 500
Fm = 3 000 At
I = 2.0A
Φ
+
Fm
Rm
Find MMF (Fm) & Flux (Φ)
L

## Slide 12
+
I
Fm = IN
Magneto Motive Force (Fm)
Rm = 50, 000 At/Wb
Flux (Φ)
N = 800 turns
Fm = 1.5 x 800
Fm = 1 200 At
I = 1.5A
Φ
+
Fm
Rm
Find MMF (Fm) & Flux (Φ)
L

## Slide 13
I = 1 A
Rm = 20, 000 At/Wb
N = 1 000 turns
I
Φ = 50 mWb
Find Current (I)
L

## Slide 14
N = 750 turns
Rm = 60, 000 At/Wb
I = 200 mA
I
Φ = 2.5 mWb
Find the number of turns in the coil (N)
L

## Slide 15
Φ = Flux in Webers
h
w
Area = width x height
A = Area in m2
B = Flux Density
What is Flux Density?
L

## Slide 16
d
d
Area = πr2 = π(d/2)2
A = Area in m2
Φ = Flux in Webers
B = Flux Density
What is Flux Density?
L

## Slide 17
The SI Unit of Magnetic Flux is the Weber (Φ)
Magnetic Flux per unit Area is called Flux Density (B)
The SI Unit of Flux Density is the Tesla (T)
A = Area in m2
1 Wb/m2 = 1 Tesla
1 Wb = 1 x 108 Magnetic Lines of Force
Φ = Flux in Webers
B = Flux Density
L

## Slide 18
+
I
CSA = 500 mm2.
Φ = 0.55 mWb.
Find Flux Density (B).
L

## Slide 19
+
I
Magnetising Force (H) aka Magnetic Field Strength
l = Length of Magnetic Path
N
Φ
L

## Slide 20
H = 6000 At/m
l = 200 mm
I = 4 A
I
N = 300 turns
Find Magnitising Force:
L

## Slide 21
H = 500 At/m
l = 200 mm
I = 100 mA
N = 1 000 turns
Find Magnitising Force:
I
L

## Slide 22
I
I = 10 mA
l = 20 mm
H = 500 At/m
N = 1 000 turns
Find Current:
L

## Slide 23
H = 500 At/m
l = 200 mm
I = 100 mA
N = 1 000 turns
Find Magnitising Force:
I
L
I
I = 10 mA
l = 20 mm

## Slide 24
Practical Exercise
The Relay
L